## Slide 1: Lab Report
Return to MC by April 3rd, 10 pm. Discussion session April 4th, 9:15 am
Shared data, individual task

## Slide 2
Q1: (a) What determines the photoresist thickness during spinning? What happens to AZ5214 photoresist during UV exposure? Is AZ5214 positive or negative resist? How do positive or negative resists react to UV light? (0.25p)
(b) What happens to photoresist during soft bake? What is different between soft back and hard bake? (0.25p)

## Slide 3
Q2: (a) Calculate the metals (Al and W) thin film resistivity of deposited samples. Compare it to literature values; remember to include reference! (0.75p)
(b) If you measure Al or W sheet resistance, and film thickness is non-uniform, how do you know resistivity? (0.25p)
(c) Compare resistivity values calculated with resistance measured before annealing and measured sheet resistance for both metals. (0.5p)
NOTE: remember compatible units, e.g., Ωm vs. µΩcm
(d) What is different between two-point probe and four-point probe electrical measurements? (0.5p)
(e) Calculate the length of serpent wires (choose one of the metals; Al or W). Use your measured data. (0.5p)
NOTE: Serpent wires 1 and 3 have the same width as wires number 1 and 3, respectively.

## Slide 4
Q3: (a) Why is electrical resistance higher during annealing? (0.25p)
(b) How does annealing affect the electrical resistance? (0.25p)
(c) What happens to metals during annealing? (0.25p)
(d) What about resistance after annealing at RT: lower? higher? why? (check literatures for both Al and W and remember to include reference) (0.25p)
(e) Recalculate resistivity for both metals! Compare “before annealing” and “after annealing” resistivities! (1p)

## Slide 5
Q4: (a) Calculate metals (Al and W) TCR (Temperature coefficient of resistance) (0.5p)
(b) Compare it for both metals and check it with literature values and give your comments of the match. (1p)
(remember to include references!)

## Slide 6
Q5: (a) We used sputtered Al and W films; find out (from the scientific literature) typical deposition rates and film thicknesses for the sputtering of aluminum and tungsten. (0.5p)
(b) what would be different if we had evaporated metals film? Would this also change the electrical properties? (0.5p)
(c) What is different between wet etched, and plasma etched samples? (0.5p)
Note: Think of wet etched Al vs. plasma etched W and vice versa.