## Slide 1: Combustion II: Flame Development
EEN-E2002 Combustion Technology
2019
D.Sc (Tech) Ossi Kaario

## Slide 2: Contents
Touch on Turbulence and its significance
Diesel and Otto cycle combustion

## Slide 4: Turbulence in flow
Turbulence chaotically swirling flow
Turbulent flow consists of vortices (eddies) of different size
The biggest vortices are of the size of the flow geometry
The eddies are breaking up into smaller eddies (kinetic energy is transported from the bigger eddies to smaller ones)
At the smallest turbulent scale (Kolmogorov scale) kinetic energy is dissipated into heat
Smallest scales dissipate quickly. Thereby, in order to have small scale turbulence and efficient mixing, first large scale turbulence must be created
Fluctuations
Turbulence = increased mixing !

## Slide 5: Experimental flame
Increased area compared to laminar flow

## Slide 6: Flame speed in a premixed H2 -case
M. Ghaderimasouleh 2016
Flame front marked with hydroperoxyl (HO2) radical
Even low turbulence levels may increase the flame area dramatically

## Slide 7: Effect of turbulence
Turbulence has significant effect on combustion because it increases the reaction rate by multiplying the reaction area
Turbulence can increase the reaction rate by a factor of 100
Kaario, 2013

## Slide 8: Diesel combustion
Combustion is mainly controlled by the fuel spray
Non-premixed / diffusion flame
Turbulent mixing is controlling and limiting the fuel consumption rate
Strong influence from combustion conditions: gas density, temperature, EGR (exhaust gas recirculation)
In high-speed engines swirl enhances mixing
Ignition is characterized by chemistry
Fuel injection and combustion are proceeding at the same time

## Slide 9: Diesel combustion
High-pressure fuel spray (1000-2000 bar)
  Atomization, Breakup, Evaporation
Vapor mixing
Auto-ignition
Combustion
Lean overall mixture
Reactions take place close to Lambda=1
High efficiency
No pumping losses at low load
Requires good ignition characteristics from fuel
NOx and soot emissions

## Slide 10
Diesel combustion

## Slide 11: Schematic diesel flame
J. Dec 1997

## Slide 12: New / Advanced Diesel combustion processes
HCCI = Homogeneous Charge Compression Ignition
  Very early fuel injection. Problems with ignition control. Typically strong EGR used.
PCCI or PCI = Premixed Charge Compression Ignition / Premixed Compression Ignition
  Early fuel injection (later than in HCCI). Problems with ignition control. Typically strong EGR used.
RCCI = Reactivity Controlled Compression Ignition
  Two different fuels of different reactivity used. Ignition delay is controlled by the low-high reactivity fuels.

## Slide 13: Std vs HCCI Diesel combustion

## Slide 14: Gasoline engine combustion
Otto combustion
Turbulent premixed combustion
Fuel injection takes place much before combustion
Stoichiometric or lean combustion
Problems in efficiency due to low compression ratio and at low load due to pumping losses (choking)
High combustion temperature  NOx emissions
High octane fuel that resists auto-ignition and evaporates easily
Catalyst removes nitrogen oxides
Picture from optical gasoline engine

## Slide 15: Flame speed in Otto engines
Flame speed in laminar combustion is close to 0.3-0.5 m/s
3000 rpm, 90% of mixture has burned in about 3.5ms
Laminar flame would have propagated about ~1.2mm
Real flame speed is in this case close to 40-times higher
Higher rotational speed 
Higher turbulence 
Increased flame area 
Faster combustion

## Slide 16: Diesel – Otto Comparison
Diesel Otto
Fuel injection Direct injection (DI) Intake runner / DI
Time between injection Very short Long
and combustion
Ignition Auto ignition Spark
Combustion Non-premixed Premixed

## Slide 17: Group work
Watch videos about various engine combustion variants (see next slide)
In groups, discuss what you saw (e.g. otto and diesel groups)
Present your main observations based also on the lecture material. Focus on topics like
  Initial situation
  Mixture preparation
  Flame type
  How is the combustion proceeding in each case ?
    Draw the combustion schematically at two time instances in 2D
  What controls the combustion and reaction rate
  Combustion phases

## Slide 18: Videos
6 different engine combustion concepts are presented:
Otto (gasoline) combustion
Diesel
HCCI (homogenous charge compression ignition)
PCI (premixed compression ignition)
MK (modulated kinetics)
RCCI (reactivity controlled compression ignition)
Videos are from Sandia National Laboratories, USA
http://www.sandia.gov/ecn/tutorials/visualization.php

## Slide 19: The Optical engine in the videos
Fully optical (optical imaging possible through the piston and cylinder liner)
All test points made with 1200 rpm rotational speed
Load load conditions (IMEP 3.7 – 4.6 bar)
Engine compression ratio is rc =10.75

## Slide 20
Otto combustion
-No EGR
-Fuel: Iso-Octane
-High engine-out HC, CO, and NOx emissions, but low tailpipe emissions (catalyst)
-Peak thermal efficiency typically 30%, full load range possible

## Slide 21
Diesel combustion
-No EGR
-Fuel: n-heptane
-’Normal’ fuel injection close to TDC
-High engine-out and tailpipe PM and NOx emissions (3-way catalyst not possible)
-Peak thermal efficiency typically 40-45%, full load range possible

## Slide 22
HCCI combustion
-No EGR
-Fuel: Primary Reference Fuel (PRF) mixture PRF57.
PRF is a mixture of iso-octane and n-heptane.
-Very early fuel injection
-Low engine-out PM and NOx emissions, high CO and HC emissions
-High efficiency (~50%), limited to lower loads unless EGR and/or high boost

## Slide 23
Premixed Compression Ignition (PCI) combustion
-Strong EGR used
-Fuel: n-heptane
-Early fuel injection (-25 cad)
-Low engine-out PM and NOx emissions, high CO and HC emissions
-Wall-wetting can be problematic (with diesel fuel), limited to lower loads

## Slide 24
Modulated Kinetics (MK) – late injection
-Strong EGR used
-Fuel: n-heptane
-Late injection (+3 cad)
-Low engine-out PM and NOx emissions, high CO and HC emissions
-Less wall wetting than PCI, lower efficiency (combustion phasing), limited to lower loads

## Slide 25
Reactivity Controlled Compression Ignition (RCCI)
-No EGR used
-Fuels: iso-octane (early injection) and direct injection of n-heptane.
-Injection in multiple steps (GDI type injection first)
-Low engine-out PM and NOx emissions, high CO and HC emissions
-High efficiency (~50%), limited to low to medium loads (with EGR and/or boost)