## Slide 1
Hydraulic control system
Hydraulic control system consists of
Power source (electric motor or combustion engine + pump)
Control component (typically valve, sometimes pump)
Actuator (cylinder or motor)
Transducers (in valve, in actuator)
Control electronics and control (feedback) loops (one or more)
System output is, e.g., position, speed, force, of the actuator.

## Slide 2
Control systems – open and closed loop
Control system
Control system with feedback

## Slide 3: Fluid power control systems – feedback control
Figures: Rydberg (1, 2, 3) and Linjama (4)
4. Digital Hydraulic (Valve) Control
3. Valve Control
2. Pump Control
1. Electric Motor Control
DFCU
Digital Flow Control Unit

## Slide 4
Majority of continuously controlled systems are realized either with proportional or servo valve technology, where the actuator is controlled with a single valve. This valve is in turn controlled with an electric actuator that is either
Linear magnet – Proportional solenoid
Torque motor
or
Output of electric actuator is proportional to its command value and thus also the output of the valve is proportional to it.
Bosch Rexroth AG
Electric control components in hydraulics

## Slide 5: Proportional solenoid
Force-stroke curves for force-controlled solenoid
Electric actuator for controlling spool force or displacement
Stroke-controlled proportional solenoid
Force-controlled proportional solenoid
Due to position feedback position …
Hysteresis small
Repetition error small

## Slide 6: Valves for control systems (1)
Proportional Directional Control Valve
Rexroth 4WRPH6
Step response at 100 % step < 10 ms
Spool valve
Separate control electronics
Proportional Solenoid operated proportional control valves
Proportional solenoid
LVDT position sensor

## Slide 7: Valves for control systems (2)
http://www.parker.com/literature/Hydraulic%20Controls%20Europe/Manuals%20UK/D_FP_20%205715-658%20UK.pdf
Voice Coil operated Proportional Directional Control Valve
Parker DFplus
Nominal flow up to 40 l/min @ 35 bars
Step response at 100 % step < 3.5 ms
Measured with load (100 bar pressure drop/two control edges)
Spool valve
Voice coil
Control electronics
Voice Coil operated proportional control valves
http://www.parker.com/literature/Hydraulic%20Controls%20Europe/HY11-3500UK/PDF_2013/D1FP%20UK.pdf
Size:
NG06 / CETOP 03 / NFPA D03

## Slide 8: Torque motor – core of servo valve
Flapper-jet system
First stage
Valves for control systems (3a)
ARMATURE
UPPER POLEPIECE
LOWER POLEPIECE
COILS

## Slide 9: Servo valve – two stages and mechanical feedback
Feedback spring
Torque motor (1) electric current changes
Displacement of torque motor and flapper plate (6)
Unbalance of pressure losses in flapper/nozzle
Pressure difference acts on spool (5) ends
Spool (5) moves
Feedback spring (3) bends and pulls flapper plate (6) back
New equilibrium is achieved due to feedback (spring)
  Certain torque motor current
  Certain spool position
Valves for control systems (3b)

## Slide 10
Traditionally the use of torque motors has resulted into significantly higher boundary frequencies of valve output, but the recent development of linear magnets has diminished the frequency gap between these technologies.
Dynamic characteristics of valves depend greatly on the characteristics of the electric actuator, on the feedback system and on valve size. Examples of boundary frequencies:
- proportional magnet  70 Hz
- servoproportional magnet  120 Hz
- voice-coil-magnet  220 Hz
- torque motor  300 Hz
Example diagram, does not represent any certain valve.
Electric control components in hydraulics

## Slide 11: Digital valves
Use only on/off valves to control flow rate
    Valve either completely open (ON) or closed (OFF)
    Simple valve structure
      Cheap
    Usually leak-free
    No small gaps
      More tolerant for contaminated fluid and temperature changes
Two methods of proportional flow control
    Switching control
    Parallel digital valve systems

## Slide 12: Switching control
One on/off valve per metering edge controlled with PWM
Analoguous to switching PSUs in electronics
Simple
Very fast valves ~1 ms
Constant valve switching
    Valve wear
    Pulsating pressure
      Noise
      Oscillating movement
Notes: PWM = pulse width modulation

## Slide 13: Digital valve systems 1/2
A number of parallel on/off valves for each metering edge
Stepwise flow control
Throttling based control
    Similarly to proportional valves
Energy efficiency
    Usually leak-free valves
      No actuator movement -> no flow required
    Independent metering
      Regenerative modes
Notes: http://www.tut.fi/cs/groups/public_news/@l102/@news/@p/documents/liit/mdbw/mdq0/~edisp/p044763.pdf

## Slide 14: Digital valve systems 2/2
Works fine with slower valves, response time 5-15 ms
Fault tolerant
    Parallel connection – no problem if one valve breaks
    Faulty valves can be detected and compensated for
Independent metering reduces need for external valves
    Counter-balance
    Anti-cavitation

## Slide 15: Digital valve systems currently
Machined manifold & commercial cartridge valves
    Response time ~10 ms
    Large and heavy
    Simple valves – relatively complex valve system
    5-7 valves per metering edge
      Limited flow control resolution

## Slide 16: Valve miniaturizing basics
Replacing large valves with several small ones leads to
    Smaller combined size / more flow capacity
    Faster response
    Lower electrical power consumption
    More complex valve system
      Manifold
      Control electronics
    Smaller manufacturing tolerances
    Valves more sensitive to contamination?

## Slide 17: Miniature valve research
Research mainly at Tampere University of Technology and Aalto University
Integrating valves as parts of the manifold

## Slide 18: Tapio Lantela’s (Aalto) research:
Digital valve system based on pilot operated miniature valves
4 x 8 on/off valves
Response time < 2 ms
Flow capacity 78 l/min @ 35 bar

## Slide 19: Valves for control systems (4)
Nominal flow up to 8*9 l/min @ 35 bars
Step response at 100 % step < circa 1 ms
Solenoids
Electronics
Solenoid and pilot valve operated digital hydraulic valve
Aalto University – Tapio Lantela
NG06 / CETOP 03 / NFPA D03 sub plate  can replace NG6 proportional control valve
32 Poppet valves (ON/OFF)
8 valves per control edge
Enhanced 3D printed version also ready and tested
http://www.tandfonline.com/doi/full/10.1080/14399776.2017.1358025