## Slide 1: Testing and Measurement
Department of Energy Technology
General
-testing and methods
-measurements
-measurement chain

## Slide 2: Engine test in laboratory
Main focus areas are:
-emissions
-performance
-fuel consumption
-sound
-driveability

## Slide 3: Testing according Din 50322
Class 1. Full scale test on the road
Class 2. Car on the test stand, environment
Class 3. Fully equipped engine from vehicle on a test stand with stock equipment, control unit, exhaust system
Class 4. Tests with special test machine, reciprocating movement, actual engine components
Class 5. Test with modified components, loading system resembles actual system, reciprocating.
Class 6. Test with general test machine, simple test specimens Pin-On-Disk

## Slide 4: Loading equipment
At engine test rig dynamometer, brake is used to load engine
-mechanical brake
-electrical brakes: eddy current, electric motor
-pump brakes
-inertia brakes, transient only

## Slide 5: Eddy current dynamometer
All power engine procuces is converted
to heat. It will not generate electricity.

## Slide 6: Eddy current dynamometer

## Slide 7: AC-dynamometer
Is basically a generator-> All power engine produces can be transferred back to electric network.
Can be used on load situations which are impossible for Eddy Current (EC) dynos, long down hill driving.
Needs heavy electrical connections,
5 times more money for purchasing than EC

## Slide 8: Typical test set-up
Torque measurement
F
r
M= F r
P= M n / 9550

## Slide 9: Typical test set-up

## Slide 10: Testing procedures
-testing can be steady speed, speed and load of the engine is kept constant
-testing can be transient, load and speed varies, usually according standardized, (EU-norm) test cycle.

## Slide 11: Testing procedures
Test cycle for cars, car is on
chassis dyno (rolling road). Load
is calculated and adjusted to
realistic values after evaluation of a drag and
rolling resistance. Validation i.e. fuel con-
Sumption.

## Slide 12: Testing procedures
Truck and off-road enginesare tested on
a engine dyno with OEM engine control
system. Approval for emission standards,
EURO 1-6.

## Slide 13: Testing
Case study: Piston rings; wear
To test engine it must be loaded. Engine testing can be
made in authentic circumstances, for example on the
road while driving a car. Results are valid and represents
real world very well. Down side is repeatability, amount of
labor and time.
Department of Energy Technology

## Slide 14: Measured values
-torque and force
-rotational speed
-temperature
-pressure
-mass flow
-gas concentration

## Slide 15: Measurement chain
-sensor
-input
-display
-storage

## Slide 16: Measurement chain, sensors
-temperature
-pressure
-torque and force
-rotational speed
-mass flow, air and fuel
-gas concentration, exhaust gas components

## Slide 17: Pressure, equipments
Manometers, u-tube
Meters, gauges
Sensors, transducers

## Slide 18: U-tube, manometer
Δp=Δh⋅ρ⋅g
where Δh is the vertical distance between water levels
ρ is the density of the liquid
g is the gravitational acceleration

## Slide 19: Sensors, temperature
-themocouples, laboratory level approach. K-type most popular.
-NTC resistor (negative temperature coeffient) usually engine control systems.

## Slide 20: Thermocouples
-two different metals joined together
-several types for diffrent temperature ranges
-temperature difference creates small amount of voltage
Usually K-type on engine tests, max. 1370 C

## Slide 21: NTC resistor
Chart: 
| -30 | -20 | -10 | 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130
Vout | 11.1429 | 10.6256 | 9.8942 | 8.9605 | 7.8564 | 6.6667 | 5.5258 | 4.4409 | 3.5314 | 2.755 | 2.1478 | 1.6685 | 1.2569 | 1.0261 | 0.80597 | 0.64174 | 0.51125
Resistance | 26 | 15.462 | 9.397 | 5.896 | 3.792 | 2.5 | 1.707 | 1.175 | 0.834 | 0.596 | 0.436 | 0.323 | 0.234 | 0.187 | 0.144 | 0.113 | 0.089
+12VConstant
3000 ohm
Vout
temperature
NTC sensor

## Slide 22: Pressure sensors and tranducers
-simple, robust, up to 3000 bar
-suitable for slow measuremens, control, diesel fuel pressure
-linear output:
for example
2V = 0 bar
10V = 20 bar

## Slide 23: Pressure sensors, engine research
Intake and exhaust manifold pressure level and pulses
Cylinder reference pressure
-fast 1000 Hz
-Pietzo resistive sensor
-combined with amplifier

## Slide 24: Pressure sensors, engine research
Maximum cylinder pressure measurements
-350 bar
-fast
-can only measure dynamic, change of pressure
- high resulation

## Slide 25: Cylinder pressure measurement

## Slide 26: Cylinder pressure measurement

## Slide 27: Cylinder pressure measurement

## Slide 28: Measurement of force
-Load cell, constructed on strain gage
-measured over Wheatstone bridge bet-
ween points A-B

## Slide 29: Measurement of force
-strain gage is glued on metal bar
-force make bar and gage longer->
increases resistance.

## Slide 30: Measurement of force, load cell
F

## Slide 31: Rotational speed and position of crank shaft
-inductive sensor
-Hall sensor
-rotary encoders, (angle measurement) for cylinder pressure curve

## Slide 32: Rotational speed
-inductive sensor (fast enough for turbo charger speed)

## Slide 33: Rotational speed
-Hall sensor

## Slide 34: Crank angle sensor
-used to crank angle based
measurements, cylinder pressure
and intake and exhaust manifold
pressures
-resolution 1440 pulses/rev

## Slide 35: Massflow
-intake air mass
-fuel mass flow
-blow-by gases from crankcase

## Slide 36: Mass flow of fluids
-scale type measurement
-gear type flow meter
-coriolis flow meter
-rotameters

## Slide 37: Air mass flow measurement
Electrical
-hot wire or film measurement, non-linear
-coriolis flow meter, out-put linear
Manual
-measurement flanges
-flow calculated from
pressure drop

## Slide 38: Emission measurements
-Nox
-CO
-CO2
-O2
-HC (unbuned fuel)
-smoke
-particles (mass, size distribution), soot
Measured with exhaust gas analyzers.
200-1500 kEur

## Slide 39: Data aquisation
Science: Engine and test systems are running on same platform (PC and National instruments), data is stored and processed during measurement and after testing,
R&D: Engine is running on own OEM ECU control unit, data is gathered from additional sensors and from ECU via CAN-bus.

## Slide 40: Data aquisation
-booklet
-plotters/recorders
-computer (PC) with suitable hardware and software

## Slide 41: Recording data today
Example:
USB to PC
Thermocouples
Analog inputs
Digital inputs
Different modules for different
signals