## Slide 1: EEN-E2002 Combustion Technology LE2 advice session
18.01.2019, Jonny

## Slide 2: Problem 1a: the differences of laminar and turbulent flame
Laminar premixed flame
Turbulent premixed flame
Turbulent flow results when instabilities in a flow are not sufficiently damped by viscous action and the fluid velocity at each point in the flow exhibits random fluctuations.
Velocity as a function of time at a fixed point in a turbulent flow.

## Slide 3: Problem 1a: the differences of laminar and turbulent flame
Premixed gas flames can arise from fuel gas and air being mixed prior to entering the burner
Gas mixed after leaving the burner they are called diffusion flames.
The gas flow rate may be relatively low, in which case, the incoming gaseous flow of fuel and air is laminar, as is the flame.
With high gas flows, they may be turbulent. Thus, flames can be laminar premixed, laminar diffusion, turbulent premixed or turbulent diffusion flames as indicated in right.
The transition from laminar to turbulent flame takes place as the flow velocity increases as shown in right
They can also be categorized into stationary flames or propagating (travelling) flames, the former being the most widely used in domestic or industrial burners, the latter being involved in explosions.

## Slide 4: Problem 1b: the turbulent flames at different length scales
L Characteristic width of flow or macroscale
l0 Integral scale or turbulence macroscale
lλ Taylor microscale
lK Kolmogorov microscale.
This is the largest length scale in the system and is the upper bound for the largest possible eddies.
this length scale is defined by the actual hardware or device being considered.
This length scale is frequently used to define a Reynolds number based on the mean flow velocity, but is not used to define a turbulence Reynolds number, as are the other three length scales.
the Kolmogorov scale is the scale at which molecular effects (kinematic viscosity) are significant.
Four Length Scales
Characteristic Width of Flow or Macroscale, L
Integral Scale or Turbulence Macroscale, l0
The integral scale physically represents the mean size of the large eddies in a turbulent flow: those eddies with low frequency and large wavelength.
Taylor Microscale, λ The Taylor microscale
Kolmogorov Microscale, K
where is the molecular kinematic viscosity, and the dissipation rate is approximately expressed as

## Slide 5: Problem 1b: the differences of laminar and turbulent flame
Chemical reactions occur in thin sheets.
The reaction-sheet regime is characterized by fast chemistry.
The flamelets propagate with a velocity consistent with a plane (one-dimensional) laminar flame.
The only effect of turbulence is the wrinkling of the flame, which results in an increase in flame area
The first model is by Damköhler
Three Flame Regimes
Distributed-reaction Regime
One way to enter this regime is to require small integral length scales, l0 / dL < 1, and small Damkoler numbers (Da < 1).
Flamelets-in-eddies regime
The intrinsic idea behind the eddy-breakup model is that the rate of combustion is determined by the rate at which parcels of unburned gas are broken down into smaller ones, such that there is sufficient interfacial area between the unburned mixture and hot gases to permit reaction
Conceptual view of turbulent flame propagation in the distributed-reaction regime showing various length scales of turbulence within the reaction zone proper.
Conceptual view of turbulent flame propagation in the flamelets-in-eddies regime.
Wrinkled Laminar-flame Regime

## Slide 6: Problem 2a: how the turbulence effect on the premixed flames
Turbulent premixed flames lie at the basis of gas turbines and various other technical combustion devices.
Turbulence affects the rates of fuel burn by increasing the flame surface and increasing the rates of heat and mass transfer.
Although fundamental questions of the scaling of turbulent flames with Reynolds number lie at the basis of effective design of combustion devices, the scaling of the flame surface and overall burn rates with the Reynolds number of the flow are not clear.

## Slide 7: Problem 2b: how the turbulence effect on the non-premixed flames
Turbulent non-premixed flames have wrinkled, contorted and brushy looking edges, just like turbulent premixed flames.
You probably can answer the question from following aspects:
Fuel/air mixing
Reaction zone
Velocity
Flame structure
Temperature distribution
Emission
Others

## Slide 8: Problem 3a: combustion processes in modern gasoline direct injection engines

## Slide 9: Problem 3b: combustion processes in modern gasoline direct injection engines

## Slide 10: CI and SI combustion processes
Parameter | SI | CI
Fuel | highly volatile fuels with high self ignition temperatures | non volatile fuels whose self ignition temperature is comparatively lower.
Fuel Injection | Port Fuel Injection(PFI), Gasoline Direct injection(GDI) | Common Rial Direct Injection
Injection Pressure | PFI: lower than 10bar GDI:50-600bar | CRI: 800-3000bar
Timing Delay | Depends to the spark timing, Relatively long | Denpends on the fuel properties (e.g. CN, etc.), charge air temeprature, and compression ratio. Relatively short
Method of ignition | Spark ignition | Compressed ignition
Subsequent combustion | Premixed combustion | Diffusion combustion

## Slide 11: Problem 5
Step 1: the mean piston speed
Where L is the stroke, N is the rotational speed of the crankshaft.
Step 2: the furthest distance between the spark plug and cylinder wall.
15+43=58mm
Step 3: convert the degree to ms
Step 4: convert the degree to ms
Step 6: Laminar flame speed at spark
Step 5: turbulence intensity at TC
Where =298K, =1 atm. is the equivalence ratio at which is a maximum with value . ,,are constants for a given fuel, equivalence ratio and burned gas diluent fraction
=
Fuel |  | , cm/s | , cm/s
Gasoline | 1.21 | 30.5 | -54.9
Fuel |  |  | 
Gasoline | 1.21 | 30.5 | -54.9
Step 7: firing pressure/motored pressure at TC
Where is he velocity fluctuation, we can assume it is . is the firing pressure/motoring pressure
.

## Slide 12: Problem 5
Step 8: calculate the mean expansion speed of the burned gas
=
Step 10: calculate the volume at TDC
Step 9: calculate burned mass fraction at TDC
Where a=5 and m=2,=0, =-30, =35
Where is the volume fraction of burned gas. We can assume under the residual gas fraction 8% condition, the relations between and follow the trends as right figure. So we can derive the from .
Step 11: calculate stoichiometric fuel/air ratio
=15.12
Assume the gasoline is C8H18,
Step 12: calculate pure air fuel mass in cylinder
Step 14: calculate fuel in cylinder
=
=
Where =

## Slide 13: Problem 6
Step 1: the ignition delay (in crank angle degree in terms of charge temperature T and pressure p) during the delay (Taken as TC conditions)
Where is the mean piston speed, is the universal gas constant 8.3143J/mol.K , is the apparent activation energy, and is given by,
=
Where is the fuel Cetane Number, normally, CN=45
Step 2: the apparent activation energy
Step 3: Values for T and p can be estimated using a polytropic model for the compression process:
Step 4: calculate
=
Probably you have to calculate the results with Matlab.

## Slide 14: GOOD LUCK !!!
18.01.2019, Jonny