## Slide 1: MEC-E5005 Fluid Power Dynamics L (5 cr)
Time: Fridays 11:15-15:00 o’clock
Schedule:
Staff
Jyrki Kajaste
DSc (Tech), University Teacher
jyrki.kajaste@aalto.fi
MEC-E5005 Fluid Power Dynamics L |  |  |  |  | 
Week | # | Day | Time | Room | Milestone check
37 | 1 | 11.9.2020 | Fri 11:15 - 15:00 | R001/U344 | 
38 | 2 | 18.9.2020 | Fri 11:15 - 15:00 | R001/U257 | 
39 | 3 | 25.9.2020 | Fri 11:15 - 15:00 | R001/U344 | Cylinder model
40 | 4 | 2.10.2020 | Fri 11:15 - 15:00 | R001/A046a | 
41 | 5 | 9.10.2020 | Fri 11:15 - 15:00 | R001/A046a | Valve model
42 | 6 | 16.10.2020 | Fri 11:15 - 15:00 | R001/A046a | 
43 |  | 23.10.2020 |  |  | 
44 | 7 | 30.10.2020 | Fri 11:15 - 15:00 | R001/Y344 | Seal model
45 | 8 | 6.11.2020 | Fri 11:15 - 15:00 | R001/Y344 | Personal simulation work
46 | 9 | 13.11.2020 | Fri 11:15 - 15:00 | R001/U351 | 
47 | 10 | 20.11.2020 | Fri 11:15 - 15:00 | R001/U351 | Group assignment check
48 | 11 | 27.11.2020 | Fri 11:15 - 15:00 | R001/U351 | 
49 | 12 | 4.12.2020 | Fri 11:15 - 15:00 | ? | 
50 | 13 | 11.12.2020 | Fri 11:15 - 15:00 | R001/U351 | Group assignment ready
 |  |  |  |  | Asko Ellman, Tampere University ??

## Slide 2: Workload estimate
Workload
  5 cr
  Lectures 2 h (1 x 2 h) and mini-lessons (12 x 0.5 h)
  Modelling and simulation exercises 36 h (12 x 3 h)
  Autonomous studying, working on exercises and assignment 91 h

## Slide 3: Information
Needed in excercises - Aalto –password - Ellman & Linjama textbook ”Modeling of Fluid Power Systems" (MyCourses webpage)
Course material https://mycourses.aalto.fi/course/view.php?id=29537 (MyCourses)
Benchmarking of submodels
Students demonstrate and document
  Realization of Simulink modeling, block diagrams
  Simulation results with given parameter values and inputs.
  The submodels include
    Cylinder model
    Proportional control valve
    Seal friction/force model
  The main idea is to validate the functionality of the submodels. The documents are included in the personal final report. (return 6.11.2020 at the latest).
Project work
  15.12. deadline of report

## Slide 4: Learning Outcomes
After the course the student is able to:
- Describe the principles of modeling and simulation and the potentials of these in system design and analysis
- Use some modeling and simulation environment/software (Matlab ja Simulink)
- Identify (analyze) dynamic structures of hydraulic systems
- Create models for static and dynamic elements (hydraulic and pneumatic components and systems) and run simulations with them
- Identify (analyze) parameter values for models from component catalogs and measurement results
- Analyze dynamic characteristics of hydraulic systems with the help of measurement data (step and frequency responses)
- Analyze the operation of hydraulic systems by modeling and simulation
- Evaluate critically the quality and deficiencies of a component or system model (i.e. validate the model using measurement data)
- Design and tune an electrohydraulic position, speed and force servo by using modeling and simulation
- Estimate the quality of an electrohydraulic position, speed and force servo by modeling and simulation
- Create well-defined and comprehensive modeling and simulation documents
- Describe the principle of real-time simulation and the special demands of it

## Slide 5: Simulation of Fluid Power
Modeling of fluid properties
Modeling of valves
Modeling of actuators
Modeling of fluid power systems

## Slide 6: Simulation work
Cylinder system
  Hydraulic cylinder (actuator)
  Proportional control valve (Regel Ventil)
  Load (mass)
  Control system (open loop control)
Control system
  PID control of systems
    Position control

## Slide 7: Hydraulic circuit to be modeled 1
M
CONTROL
x
p/U
p/U
pA
pB
U

## Slide 8: Hydraulic circuit to be modeled 2
M
CONTROL
x
p/U
p/U
pA
pB
U
POSITION
CONTROL

## Slide 9: Hydraulic circuit to be modeled 3 option 1
M
M
Direct Driven Hydraulics (DDH) system

## Slide 10: Hydraulic circuit to be modeled 3 option 2
HIL CONTROL
,x
p/U
p/U
pA
pB
Ucommand
Fhydr
https://www.bgmotorsport.co.uk/suspension/ohlins-suspension/ohlins-damper-anatomy/
mS
mU
(measured)
Fdamper
virtual mechanics
HYDRAULIC SERVO ACTUATOR
Motion control
Virtual inputs by ”road”
p/U
pP
m
Fdamper
1
2
3
4
5
6
7
8
9
10
A
11
12
Hardware In the Loop testing arrangement
Sensors for HIL
Damper force
Mass position
Mass velocity
Other sensors
Cylinder force
Cylinder pressure A
Cylinder pressure B
Pump pressure P
Damper pressure A
Damper pressure B
Damper pressure Accu
Fluid temperature
Valve position signal
Output signals
Valve command U
ON/OFF valve A
ON/OFF valve B

## Slide 11: Simulation of dynamics
Phenomena are time dependent
Differential equations are solved
The core of fluid power simulation is solving of the pressure of a fluid volume (pipe, cylinder tms.) by integration
  ”Hydraulic capacitance”

## Slide 12: Simulation of fluid power - variables
Essential variables in fluid power technology are
  Flow Rate qv [m3/s]
  Pressure p [Pa], [N/m2]
The variables in question define the hydraulic power
P= p qv (power of a hydraulic component, pump, valve etc.)
  p pressure difference over a component
  q flow rate through a component

## Slide 13: Modeling of a system
Common way to realize a model of a system is to divide it into
  Fluid volumes (pressure is essential to these volumes)
  Components between fluid volumes (”valves” ja ”pumps”, flow rate is essential to these volumes)
V
qv1IN
qv2IN
pOUT
”Fluid volume”: pressure is solved,
flow rates as inputs
qvOUT
p1IN
p2IN
”Valve”: flow rate is solved,
pressures as inputs

## Slide 14: Building up a system of ”fluid volumes” and ”valves” (flow sources)
V1
V2
”pump” – ”pipe” – ”valve” – ”pipe” – ”valve” – ”actutor”
V3

## Slide 15: Pressure in a constant fluid volume
The way to build up a system model presented earlier is advantageous for numerical solution. The pressure is solved by integration.
”The generation of pressure” in a constant volume can be expressed as follows:
Kf bulk modulus of fluid [Pa], n. 1.6109 Pa (mineral oil)
V fluid volume [m3]
qv net flow rate [m3/s]
volume of fluid transferred into the volume [m3]

## Slide 16: Time to think 1
Pressure must be changed very rapidly in certain applications (for instance servo control)
Based on ”equation of pressure generation” how can you speed you the pressure response of your system?
Kf bulk modulus of fluid [Pa], n. 1.6109 Pa (mineral oil)
V fluid volume [m3]
qv net flow rate [m3/s]
volume of fluid transferred into the volume [m3]

## Slide 17: Hydraulic cylinder – linear motor
If
  the fluid volume is small and
  the fluid has high bulk modulus
  even a small alteration of fluid amount in a hydraulic cylinder causes a significant change in pressure (gain Kf/V) as well as in force.
For enhanced dynamic performance (rapid changes in pressure/force) the fluid volumes should be kept as small as possible (fluid power jargon: ”dead volumes”)
qv
F

## Slide 18: More of generation of pressure
The pressure in a fluid volume can be changed also by altering the size of the fluid volume
Kf bulk modulus of fluid [Pa]
V (changing) volume full of fluid [m3]
V change in volume [m3]
Attention: the sign ()
F
V

## Slide 19: Time to think 2
Pressure acting perpendicular to the piston surface produces a force
A surface area [m2]
As which component does the cylinder operate if the piston rod is loaded with force?
Kf bulk modulus of fluid [Pa]
V (changing) volume full of fluid [m3]
V change in volume [m3]
F

## Slide 20: Liquid spring and mass
Liquids are incompressible
Cylinder filled with (slightly compressible) liquid acts as a spring (spring constant?)
The cylinder and mass attached to the piston rod form a spring –mass system which has a tendency to vibrate with nominal frequency f.
k
M

## Slide 21: Time to calculate
How much does pressure increase if the volume of a (stiff) chamber filled with hydraulic oil is reduced by 1 %?
Kf bulk modulus of fluid [Pa], circa 1.6109 Pa (hydraulic fluid)
V (changing) volume full of fluid [m3]
V change in volume [m3]

## Slide 22: Equation for pressure generation - combination
The mechanisms in fluid power which may alter the pressure in a chamber include a) change in fluid amount b) change in volume.
”Equation for pressure generation” may be expressed as follows:
                Ellman & Linjama: Modeling of Fluid Power Systems
Textbook p. 18
Equation 25
a)
b)
Negligible changes in total volume (V0= constant)
Significant changes in total volume (V)
This equation can be applied in hydraulic cylinder calculations.

## Slide 23: Time to think 3
What fluid power component is this?
When does pressure change in the cylinder and when does it remain constant?
F
qv

## Slide 24: Piston pump
In fluid power technology pumps usually work based on displacement principle. This means that the volumes of displacement chambers in pumps change periodically.
The pressure in the cylinder (pump) increases if the movement of piston reduces the size of the cavity faster than the liquid flows out of the cylinder.
The pump pressure depends on how much the outflow is restricted.

## Slide 25: To think about
Is the bulk modulus really a constant?
How do pressure, liquid temperature and free air (bubbles) in the liquid affect the bulk modulus?
How does temperature affect the pressure in a closed vessel? (mineral oil 6.410-4 1/°C – carbon steel 0.324 10-4 1/°C )