## Slide 1: MEC-E5005 Fluid Power Dynamics L (5 cr)
Time: Fridays 11:15-15:00 o’clock
Schedule:
Staff
Jyrki Kajaste
DSc (Tech), University Teacher
jyrki.kajaste@aalto.fi
MEC-E5005 Fluid Power Dynamics L |  |  |  |  | 
Week | # | Day | Time | Room | Milestone check
37 | 1 | 11.9.2020 | Fri 11:15 - 15:00 | R001/U344 | 
38 | 2 | 18.9.2020 | Fri 11:15 - 15:00 | R001/U257 | 
39 | 3 | 25.9.2020 | Fri 11:15 - 15:00 | R001/U344 | Cylinder model
40 | 4 | 2.10.2020 | Fri 11:15 - 15:00 | R001/A046a | 
41 | 5 | 9.10.2020 | Fri 11:15 - 15:00 | R001/A046a | Valve model
42 | 6 | 16.10.2020 | Fri 11:15 - 15:00 | R001/A046a | 
43 |  | 23.10.2020 |  |  | 
44 | 7 | 30.10.2020 | Fri 11:15 - 15:00 | R001/Y344 | Seal model
45 | 8 | 6.11.2020 | Fri 11:15 - 15:00 | R001/Y344 | Personal simulation work
46 | 9 | 13.11.2020 | Fri 11:15 - 15:00 | R001/U351 | 
47 | 10 | 20.11.2020 | Fri 11:15 - 15:00 | R001/U351 | Group assignment check
48 | 11 | 27.11.2020 | Fri 11:15 - 15:00 | R001/U351 | 
49 | 12 | 4.12.2020 | Fri 11:15 - 15:00 | ? | 
50 | 13 | 11.12.2020 | Fri 11:15 - 15:00 | R001/U351 | Group assignment ready
 |  |  |  |  | Asko Ellman, Tampere University ??

## Slide 2: Workload estimate
Workload
  5 cr
  Lectures 2 h (1 x 2 h) and mini-lessons (12 x 0.5 h)
  Modelling and simulation exercises 36 h (12 x 3 h)
  Autonomous studying, working on exercises and assignment 91 h

## Slide 3: Learning Outcomes
After the course the student is able to:
- Describe the principles of modeling and simulation and the potentials of these in system design and analysis
- Use some modeling and simulation environment/software (Matlab ja Simulink)
- Identify (analyze) dynamic structures of hydraulic systems
- Create models for static and dynamic elements (hydraulic and pneumatic components and systems) and run simulations with them
- Identify (analyze) parameter values for models from component catalogs and measurement results
- Analyze dynamic characteristics of hydraulic systems with the help of measurement data (step and frequency responses)
- Analyze the operation of hydraulic systems by modeling and simulation
- Evaluate critically the quality and deficiencies of a component or system model (i.e. validate the model using measurement data)
- Design and tune an electrohydraulic position, speed and force servo by using modeling and simulation
- Estimate the quality of an electrohydraulic position, speed and force servo by modeling and simulation
- Create well-defined and comprehensive modeling and simulation documents
- Describe the principle of real-time simulation and the special demands of it

## Slide 4: Simulation of Fluid Power
Modeling of fluid properties
Modeling of valves
Modeling of actuators
Modeling of fluid power systems

## Slide 5: Simulation work
Cylinder system
  Hydraulic cylinder (actuator)
  Proportional control valve (Regel Ventil)
  Load (mass)
  Control system (open loop control)
Control system
  PID control of systems
    Position control

## Slide 6: Hydraulic circuit to be modeled 1
M
CONTROL
x
p/U
p/U
pA
pB
U

## Slide 7: Hydraulic circuit to be modeled 2
M
CONTROL
x
p/U
p/U
pA
pB
U
POSITION
CONTROL

## Slide 8: Hydraulic circuit to be modeled 3 option 1
M
M
Direct Driven Hydraulics (DDH) system

## Slide 9: Hydraulic circuit to be modeled 3 option 2
HIL CONTROL
,x
p/U
p/U
pA
pB
Ucommand
Fhydr
https://www.bgmotorsport.co.uk/suspension/ohlins-suspension/ohlins-damper-anatomy/
mS
mU
(measured)
Fdamper
virtual mechanics
HYDRAULIC SERVO ACTUATOR
Motion control
Virtual inputs by ”road”
p/U
pP
m
Fdamper
1
2
3
4
5
6
7
8
9
10
A
11
12
Hardware In the Loop testing arrangement
Sensors for HIL
Damper force
Mass position
Mass velocity
Other sensors
Cylinder force
Cylinder pressure A
Cylinder pressure B
Pump pressure P
Damper pressure A
Damper pressure B
Damper pressure Accu
Fluid temperature
Valve position signal
Output signals
Valve command U
ON/OFF valve A
ON/OFF valve B

## Slide 10: Simulation of dynamics
Phenomena are time dependent
Differential equations are solved
The core of fluid power simulation is solving of the pressure of a fluid volume (pipe, cylinder tms.) by integration
  ”Hydraulic capacitance”

## Slide 11: Simulation of fluid power - variables
Essential variables in fluid power technology are
  Flow Rate qv [m3/s]
  Pressure p [Pa], [N/m2]
The variables in question define the hydraulic power
P= p qv (power of a hydraulic component, pump, valve etc.)
  p pressure difference over a component
  q flow rate through a component

## Slide 12: Modeling of a system
Common way to realize a model of a system is to divide it into
  Fluid volumes (pressure is essential to these volumes)
  Components between fluid volumes (”valves” ja ”pumps”, flow rate is essential to these volumes)
V
qv1IN
qv2IN
pOUT
”Fluid volume”: pressure is solved,
flow rates as inputs
qvOUT
p1IN
p2IN
”Valve”: flow rate is solved,
pressures as inputs

## Slide 13: Building up a system of ”fluid volumes” and ”valves” (flow sources)
V1
V2
”pump” – ”pipe” – ”valve” – ”pipe” – ”valve” – ”actutor”
V3

## Slide 14: Equation for pressure generation - combination
The mechanisms in fluid power which may alter the pressure in a chamber include a) change in fluid amount b) change in volume.
”Equation for pressure generation” may be expressed as follows:
                Ellman & Linjama: Modeling of Fluid Power Systems
Textbook p. 18
Equation 25
a)
b)
Negligible changes in total volume (V0= constant)
Significant changes in total volume (V)
This equation can be applied in hydraulic cylinder calculations.

## Slide 15: Cylinder – variables
qvA
F
qvB
x
xmax
dx/dt, x
pA
pB
Variables
Input
Flow rates
Piston speed
Absolute position of piston
Output
Chamber pressures
Piston force (net pressure force)
LEAKAGE
LEAKAGE
Chamber pressures (time derivatives),
textbook p 75

## Slide 16: Cylinder – parameters
x
xmax
Parameters – constants(?)
A chamber
Beff effective bulk modulus  Kf (new symbol)
  pressure, temperature, free air(!) and elasticity of walls
V0A ”dead volume” of chamber + liquid volume in pipes
AA piston area
B chamber
Beff effective bulk modulus  Kf (new symbol)
V0B ”dead volume” of chamber + liquid volume in pipes
AB difference of piston and piston rod areas (annulus)
LEAKAGE
LEAKAGE
AAx volume in chamber A
x length of liquid column
AB(xmax-x) volume in chamber B
xmax-x length of liquid column

## Slide 17: Cylinder – liquid volumes
x
xmax
Constant and changing volumes
A chamber
V0 ”dead volume” of chamber + liquid volume in pipes
AAx piston position dependent extra volume
  x ”absolute position of piston”
B chamber
V0 ”dead volume” of chamber + liquid volume in pipes
ABxmax B chamber maximum volume (piston at end position)
ABx liquid volume displaced by annular piston
    x ”absolute position of piston”
LEAKAGE
LEAKAGE
pipes
AB(xmax-x) volume in chamber B
xmax-x length of liquid column
AAx volume in chamber A
x length of liquid column

## Slide 18: Chamber A realization, example
1
1
2
2
3
3
4
4
5
5
Piston leakage is not included.
To get absolute position x for piston
integrate piston velocity to get get change in position related to start point
add start position value.
Subsystem  Ctrl + G
“paint this area”
Or …
right mouse button click  Create Subsystem from Selection

## Slide 19: Chamber B realization, example
1
5
Piston leakage is not included.
1
2
2
3
3
4
4
5
(xmax-x) length of liquid piston
AB(xmax-x) volume of liquid piston

## Slide 20: Modeling of a system
Common way to realize a model of a system is to divide it into
  Fluid volumes (pressure is essential to these volumes)
  Components between fluid volumes (”valves” ja ”pumps”, flow rate is essential to these volumes)
V
q1IN
q2IN
pOUT
”Fluid volume”: pressure is solved,
flow rates as inputs
qOUT
p1IN
p2IN
”Valve”: flow rate is solved,
pressures as inputs

## Slide 21: Hydraulic circuit modeling
M
CONTROL
dx/dt, x
qA
qB
U
pA
pB
F
Phase 2
Cylinder
qA, qB, dx/dt
pA, pB, F
Inertia mass
F
dx/dt, x
in
out
in
out
dx/dt
(dV/dt)

## Slide 22: Building up a system of ”fluid volumes” and ”valves” (flow sources)
V1
V2
”pump” – ”pipe” – ”valve” – ”pipe” – ”valve” – ”actutor”
V3
Mechanics

## Slide 23: Net force of a cylinder
Hydraulic force
F= pAAA-pBAB
Net force is affected also by seal forces:
Spring force related to bending of seals
Friction force related to sliding
Seal model will be constructed later!

## Slide 24: Load model
Input: force
  connected to: cylinder net force
Output: state of motion (piston velocity dx/dt and position x)
  Connected to: state of motion  cylinder chambers’ volume change
In our simulation work the load is plainly inertia mass. The state of motion can be calculated by applying Newton’s second law.
where m = mass of an object ja a = acceleration”
In our model we are interested in the state of motion of the load and piston (piston velocity dx/dt and position x). Thus …
At first solve the acceleration of load a
Integrate the acceleration -> velocity (change in velocity)
  Velocity= 0 at the start of the simulation (unless you give it another initial value)
Inegrate velocity or integrate acceleration twice to get the change in position
  At the start of the simulation position = x0 -> take that into account to get the absolute position value
Initial value
Integrating input signal twice
Multiplication/division by a constant
Initial condition can be OR
included

## Slide 25: Cylinder model test
  Test values fo parameters
  Cylinder size 32/201000  AA ja AB (check piston area values in the Matlab workspace)
  B= 1.6109 Pa
  x0= 0.5 m
  Extra liquid volumes at cylinder ends: 3.2 cm3 (piston side), 2.0 cm3 (rod side)
  Pipes d_pipe= 0.012 m and L_pipe= 0.75 m
  1. ”plug cylinder ports” and ”push/pull” piston with rod, use velocities
  a) dx/dt = 110-3 m/s and b) dx/dt = -110-3 m/s
    -> test pressure changes using 10 second simulations
    -> test force changes using 10 second simulations
  2. ”lock” the piston rod (dx/dt= 0) and
    2.1 connect to chamber A flow rate input qA= 110-6 m3/s
    2.2 connect to chamber B flow rate input qB= 110-6 m3/s
    -> test pressure changes using 10 second simulations
    -> test force changes using 10 second simulations
  3. connect the following signal values to piston velocity and flow rates
  dx/dt = 110-3 m/s
    qA= +dx/dt  AA
    qB= -dx/dt  AB
    -> test pressure changes using 10 second simulations
    -> test force changes using 10 second simulations
Attention!
Do not connect seal model!
Benchmarking 1

## Slide 26: Testing of cylinder model
Use for example Display module to check the end values of signals
Attention!
Do not connect seal model!
Test 1a Test 2
p_A= ________ bar p_A= ________ bar
p_B= ________ bar p_B= ________ bar
F= __________ N F= __________ N
Test 1b Test 3
p_A= ________ bar p_A= ________ bar
p_B= ________ bar p_B= ________ bar
F= __________ N F= __________ N