## Slide 1: MEC-E5004 Fluid Power Systems
15.9.2020
jyrki.kajaste@aalto.fi
5 credits

## Slide 2: Structure of studies and Grade components
IN BRIEF
Presentations and lectures
Simulation assignments
  Tuning a hydraulic servo
  Building hydraulic simulation models
    Load Sensing (LS) system
    Direct Drive Hydraulic (DDH) system
  Each student: Individual Reports
Group assignment
  3 calculation assignments
  group’s discussions with the teacher
Common and organized Studies (almost) every Tuesday 16.15-18.00
Simulation (4) and servo simulation (2) exercises on 4 Wednesdays 16.00-18.00 (see detailed schedule)
Student groups arrange their own meetings and teamwork conventions

## Slide 3: Introduction to Energy Efficient Fluid Power
The main theme of Fluid Power Systems course year 2020 is
Energy Efficient Fluid Power
The
Presentations
Lectures
given by our researchers support this main theme
Other relevant topics in modern and future Fluid Power also introduced.

## Slide 4: Schedule
Preliminary schedule
(under construction)
Tuesday sessions could be used also for simulations
3 Calculation assignments
2 Simulation assignments
2 Servo simulations
Group meeting

## Slide 5: Group assignments (group works)
Wish is to … have groups with 3 members
Output
3 calculation assignments
1 group’s meeting with the teacher  plan
Build up your team until Tuesday 15.9.2020
Use MyCourses page Assignments
18 students ?

## Slide 6: Energy Balance of Electro-Hydraulic Powertrain in Micro Excavator
1
2
3
Experimental results ad some simulations as well
Electrified small sized excavator, a 1.1-tonne JCB Micro
Equipped with conventional hydraulics.
The overall energy balance of the electro-hydraulic powertrain.
The power losses in individual components.
Measured energy balance of the electric motor powered system is compared with the simulation data obtained from a preliminary simulation model of the system.
The results will be in future research utilized to discover and compare new alternatives for powertrain architectures.
Boom
Arm
Bucket
The actuators (cylinders) used in the tests.
Based on:
Energy Balance of Electro-Hydraulic Powertrain in a Micro Excavator
Otto Gottberg, Jyrki Kajaste, Tatiana Minav*, Heikki Kauranne, Olof Calonius, Matti Pietola

## Slide 7: The system
1
2
3
Boom
Arm
Bucket
Number | Description | Details
1 | Battery pack | 72V Lead-acid
2 | Motor controller | Sevcon Gen4
3 | Electric motor | 10 kW
4 | Dual pump | Parker PGP511
5 | Pressure relief valve (PRV) | 
6 | Pressure adjustment valve | 
7 | PRV LS-circuit | 
8 | Proportional valve | Danfoss PVG-32
9 | Current sensor | LEM DK 200
10 | Torque and tachometer | Kistler 4502
11 | Flow sensor | Kracht VC 0,4
12 | Pressure sensor | Hydac HDA
13 | Position sensor | Siko SGH10
Batteries (Lead-acid, 72 V) as energy source
Inverter based motor controller
AC motor as prime mover (originally diesel powered)
  Rotational speed can be adjusted/controlled
Hydraulic system
  Two gear pumps
  Constant pump Load Sensing (LS) system

## Slide 8: Power measurements
1
2
3
Boom
Arm
Bucket
Number | Description | Details
1 | Battery pack | 72V Lead-acid
2 | Motor controller | Sevcon Gen4
3 | Electric motor | 10 kW
4 | Dual pump | Parker PGP511
5 | Pressure relief valve (PRV) | 
6 | Pressure adjustment valve | 
7 | PRV LS-circuit | 
8 | Proportional valve | Danfoss PVG-32
9 | Current sensor | LEM DK 200
10 | Torque and tachometer | Kistler 4502
11 | Flow sensor | Kracht VC 0,4
12 | Pressure sensor | Hydac HDA
13 | Position sensor | Siko SGH10
Battery output power
  U and I
  Current clamps for I
Power electronics output NOT measured
Electric motor output power – pump input power
  Shaft torque (T) and angular speed ()
Pumps’ output power
  p and qv
Cylinder input power
  Inlet pressures (A and B chamber)
  Cylinder position
    Filter signal and differentiate for speed
    Speed  input flow rate (estimate)
Proportional valves’ power losses
  p and qv (flow rate estimate from cylinder speed)
LS system’s Pressure Adjustment Valve’s power loss
  Estimate for flow rate (pump qv – actuator qv:s)
  Pump pressure
1
Gear type flow meter
Current clamps
2
3
4
5
5
5
6
6
6
7
http://kracht.eu/en/product-portfolio/flow-measurement/zahnrad-durchflussmesser1/
Wire-actuated encoder for displacement
https://www.siko-global.com/en-de/products/linearline-wire-actuated-encoders/position-sensors-for-hydraulic-cylinders/sgh10

## Slide 9: Constant pump LS system
Pressure adjustment valve (PAV)
PAV (6) senses through shuttle valves the highest prevailing load pressure of the actuators
Adjusts the system pressure to a level that is approximately 20 bar higher than the highest load pressure.
PAV also directs back to tank the portion of the fixed pump flow that is not needed in the actuators.
The pressure relief valves (5, 7) fulfill a safety function preventing the pressure from rising to a dangerous level
The benefits?
The pressure difference over the proportional control valve is always the same p= 20 bars 
Operator will always get the same flow rate and actuator speed with the same valve opening command (U)  linearity and controllability!
The pump flow is always constant (some of the flow unnecessary), but the pump pressure correponds quite well to the actual need in the actuator  energy efficiency!
Maximum pressure of other actuators
Shuttle valve
senses the highest actuator pressure and sends the information to PAV,
which opens to keep the pump pressure about 20 bars higher than the highest (active) actuator pressure.
(Passive actuators = a) closed valve or b) negative load, lowering of load)
Only when the spool is moved from its center position and furthermore only from the port directing the flow to the actuator, which is to be moved.
20 bars
qv pump
qv actuators
qv PAV
Normally
qv pump= qv actuators + qv PAV

## Slide 10: Theoretical power consumption – 2 cases
Constant pump + proportional control valve + PRV
Constant pump + LS: proportional control valve + PAV
Symmetric cylinder for simplicity
The load lifted in these examples is ”lower than maximum” to demonstrate the energy saving potential of the LS system (constant pump LS)

## Slide 11
WASTED IN PRV
LIFTING POWER
Fv
qv
p
Used power
Wasted power in valves
Pump’s operating point
Maximum power, corner power
Pump
A chamber
qv
x
G
pA
pB
M
1
2
Pump
Pipe 1
PCV Control Edge PA
Pipe 2
3
4
Pipe 3
PCV Control Edge BT
Pipe 4 + FILTER
Seal Friction
B chamber
qv
SYSTEM WITH CONSTANT PUMP + PRV
High pressure loss for correct piston velocity
Small opening because high pressure drop
SYMMETRIC CYLINDER
High power losses in PCV (PA and BT) because pressure has to be dropped from pP to pT in the system.
PCV
pB
pA

## Slide 12
WASTED IN PAV
LIFTING POWER
Fv
qv
p
Used power
Wasted power in valves
Pump’s operating point
Maximum power, corner power
Pump
A chamber
qv
Pump
PCV Control Edge PA
Pipe 2
Pipe 3
PCV Control Edge BT
Pipe 4 + FILTER
Seal Friction
B chamber
qv
SYSTEM WITH CONSTANT PUMP + LS
LS pressure
POWER SAVED
PAV
Large opening because smaller (LS) pressure drop
SYMMETRIC CYLINDER
Pipe 1
Other power losses are the same as in PRV system, but PCV losses (PA and BT) are smaller
pLS
 20 bar
pB
pA

## Slide 13: Power consumption - pressure and flow rate
WASTED
Fixed-displacement hydraulic pump with PRV Fixed-displacement hydraulic pump with LS system
Maximum pressure= pressure relief valve setting
USED
qv
p
https://www.hydraulicspneumatics.com/200/TechZone/HydraulicPumpsM/Article/False/6401/TechZone-HydraulicPumpsM
Used power
Wasted power
Pump’s operating point
Maximum power, corner power
Pump
Load Pump
WASTED
USED
Pump
Load Pump
qv
p
p= 20 bar (LS)
USED POWER includes power needed by the load but also losses in control valves, pipes etc.

## Slide 14: Test cycle
Levelling cycle according to standard JCMAS H020:2007 when only boom and arm movements are taken into account
Cylinder displacements
1
2
3
Boom
Arm
Bucket
Levelling
Test procedure and duty cycle defined in the standard H 020:2007 of the Japan Construction Mechanization Association (JCMAS) [4], originally meant for testing the fuel consumption of hydraulic excavators, was applied. The measurements are conducted without external loading as defined in the standard.
Position feedback controllers were used to control the proportional valves via CAN bus. The CAN communication with the valves was implemented with Simulink.
Attention!
The test cycle is basically ”zero net energy cycle”.
The start and end points are the same and the load mass does not change.
For an ideal system the energy consumption would be zero.

## Slide 15: Measurements – energy consumption
Measured and simulated energy consumption of sub-systems for levelling cycle
Battery output
Electronics + e-motor losses
E-motor output
Pump losses
Pump output
Actuator system use + losses
Measured relative energy use in different subsystems of the power transmission

## Slide 16: Energy consumption – saving potential?
Simulated relative energy use in the actuator system for levelling cycle
Friction Hoses PAV Proportional
control valves
Measured and simulated flow rates of pumps and cylinders for levelling cycle
Wouldn’t it be good to get rid of (throttling) valves?
Wouldn’t it be good to diminsh pump flow rate here?

## Slide 17: Electric LS system?
Flow rates of pumps and cylinders
Reduce e-motor speed here
The losses in Pressure Adjustment Valve (PAV) could be remarkably reduced if the pumps’ flow rate would be equivalent to the actual flow rate need of the actuators.
The flow through PAV would diminish.
In the test system the electric motor (+ controller) is fast enough to adjust the rotational in about 1 second.
How to estimate the appropriate rotational speed?
We know the openings of Proportional Control Valves (PCV) -> electric signals, CAN bus
We measure and know the pressure differences over the PCV:s
We can calculate the total flow rate in actuators
We can estimate the pump speed
Variables known
Principle simulated (OK!), but not tested!
Approach similar to (normal) LS system with variable pump.

## Slide 18: Power consumption – electric LS
18
Fixed-displacement hydraulic pump with LS system …. with electric LS system
Maximum pressure= pressure relief valve setting
https://www.hydraulicspneumatics.com/200/TechZone/HydraulicPumpsM/Article/False/6401/TechZone-HydraulicPumpsM
Used power
Wasted power
Pump’s operating point
Maximum power, corner power
Load Pump
WASTED
USED
Pump
Load Pump
qv
p
p= 20 bar (LS)
USED POWER includes power needed by the load but also losses in control valves, pipes etc.
WASTED
USED
Pump
qv
p
p= 20 bar (LS)
Some extra flow

## Slide 19: Conclusions
Excavator’s energy consumption in leveling cycle was measured (and simulated)
Zero energy work cycle  theoretically the energy used for lifting of a load mass or just the boom could be recovered during lowering (potential energy recovery)
  No energy recovery sub-system  kinetic and potential energy  into heat in thottles
  All the energy from battery into heat in
    Electric system (controller + e-motor) 19%
    Pump 13%
    Valves (PAV + Proportional Control Valves (PCV)) 58% [<29% + >29%]
    Hoses/pipes/orifices and cylinder friction 10%
System with Pressure Adjustment Valve is better (energy efficiency) than constant pump + PRV
PAV losses could be dimished by estimating the flow rate and applying e-motor speed control  towards normal LS control with variable pump
Getting rid of PCV losses is hard with this system architecture (always at least 20 bar)