## Slide 1
Vehicle Mechatronics: Control
Lecture 2: Longitudinal and Lateral Control
Slides: Jari Vepsäläinen

## Slide 2
Topics
Control systems basics
Longitudinal control
  PID
  Feedforward PID
Lateral control
  Follow-the-carrot
  Pure pursuit

## Slide 3
Car cabin thermostat
Reference
Actual
Error

## Slide 4
Car cabin thermostat

## Slide 5
Control system - thermostat
PLANT
INPUT
OUTPUT
CABIN
FAN SPEED
TEMPERATURE

## Slide 6
Terminology
Rise time
The time it takes to reach the
Overshoot
How much the reference is surpassed after reaching it
Peak time
Time at the peak of the overshoot

## Slide 7
Terminology
Steady state error
The system is “steady” when the control is stable within tolerance limits
Settling time
The time to reach steady state error

## Slide 8
Control systems
Open loop system
  Based on estimates of how the system behaves
  Estimated input -> hope for the best
Closed loop system
  Based on feedback of how the system behaves
  Measure output, compare to reference -> adjust

## Slide 9
Open vs. closed loop system
PLANT
INPUT
OUTPUT
CABIN
FAN SPEED
TEMPERATURE
INPUT
PLANT
Reference
OUTPUT
PID
-
+
Error
Measurement
TEMPERATURE
TEMPERATURE
FAN SPEED
CABIN

## Slide 10
Vehicle speed control
PLANT
INPUT
OUTPUT
VEHICLE
GAS PEDAL
SPEED
INPUT
PLANT
Reference
OUTPUT
PID
-
+
Error
Measurement
SPEED
SPEED
GAS PEDAL
VEHICLE

## Slide 11
Longitudinal Control

## Slide 12
Longitudinal control
Control: minimize the offset to reference speed or torque
Controllers
  PID controller
  FF-PID controller

## Slide 13
PID control
How the error term is treated?
Proportional – multiplied error
Integral – cumulative error
Derivative – changes in error
The controller is tuned by changing the gains of these error terms:
-
INPUT
Error (e)
+
+
+

## Slide 14
PID – Proportional gain
Directly proportional to the current error
Control tuning typically starts with only tuning the proportional gain

## Slide 15
PID – Integral gain
Helps to get rid of steady state errors

## Slide 16
PID – Derivate gain
Tries to minimize sudden changes
Acts as a damper

## Slide 17
Feedforward PID (FF-PID)
INPUT
PLANT
Reference
OUTPUT
PID
-
+
Error
Measurement
+
+
FF
FF - A proportional gain to the reference itself
Often referred to as predictive control
Makes the controller more aggressive on higher speeds and steadier in lower speeds

## Slide 18
Lateral Control

## Slide 19
Lateral control
Waypoint-based reference path
Straight line segments
Parametrized curves
Control: minimize the offset to reference path

## Slide 20
Lateral errors
Heading error, ε
The difference between path heading and vehicle heading at a reference point
Crosstrack error, e
Perpendicular distance from the path and a reference point (closest distance)

## Slide 21
Lateral controllers
Geometric controllers
  Bang-Bang control
  Crosstrack PID
  Follow-the-carrot
  Pure pursuit
  Stanley
Dynamic controllers
Model predictive control (MPC)
Notes: Stanley controller differences to Pure pursuit (in the bicycle model case):
- Pure pursuit uses rear wheel as reference, Stanley the front wheel.
- Pure pursuit only based on the heading error, Stanley also takes into account crosstrack error
- Stanley has steadier control in turns than pure pursuit
Model predictive controller (MPC):
- Main purpose is of the system model is to predict the future evolution of the system
- Based on minimizing a defined cost function
--> optimize inputs
- computationally expensive
Good Medium –article fiscussing the pure pursuit, Stanley and MPC controllers: https://medium.com/@dingyan7361/three-methods-of-vehicle-lateral-control-pure-pursuit-stanley-and-mpc-db8cc1d32081
Great video: https://www.youtube.com/watch?v=4Y7zG48uHRo

## Slide 22
Bang-Bang control
Fixed steering
If the vehicle is to the left of the path, it will turn fixed amount to the right and vice versa
Very simple but uncomfortable and oscillating control
Why not steer proportionally?

## Slide 23
Crosstrack PID
Based on crosstrack error, e
The bigger the error, the higher the steering command
Similar concept as longitudinal PID

## Slide 24
Follow-the-carrot (FTC)
Minimize lookahead heading error, α
Nearest point
Travel lookahead to target point
Error angle is between goal point direction and current heading
Requires a proportional controller

## Slide 25
Pure pursuit 1
Calculate goal point the same way as with FTC
Calculate and :

## Slide 26
Pure pursuit 2
Connect vehicle and goal points with an arc
Radius of the arc is defined so that it attaches to the y-axis

## Slide 27
Pure pursuit 3
Three geometric equations from the figure:

## Slide 28
Pure pursuit 4
Curvature γ is the steering command

## Slide 29
Coordinate systems
Different coordinate systems
Vehicle coordinates
World coordinates

## Slide 30
Coordinate transform
goal point in
vehicle coordinates:
Note: negative angles are allowed, thus we can use the clockwise formula

## Slide 31
After coordinate transform
Vehicle perceived goal point is

## Slide 32
Summary
Lateral control
Longitudinal control

## Slide 33
Thank you