## Slide 1
Vehicle Mechatronics: Control
Everybody loves ROS
Slides: Jari Vepsäläinen & Pavithra Gopalakrishnan
July 1, 2020
Notes: Reference: Mike Ross or Ross Geller ;) Or everybody loves Raymond!

## Slide 2
Contents
ROS Basics
  What is ROS?
  ROS Tools
ROS Architecture
  Master, Nodes, Messages, Workspace, Packages and Launch Files
ROS Development
  Packages and ROS program files (Node, launch files, …)
ROS Applications
  Example application
ROS Debug
These lecture slides have been inspired by
ROS wiki (wiki.ros.org)
Stanford ASL course AA274: Principles of Robot Autonomy 1
Robot Ignite Academy: ROS Basics

## Slide 3
ROS Basics

## Slide 4
What is ROS?
A modular system environment for robotics
Robots require a lot of complex software that communicates between computers, actuators and sensors
Modularity: components and processes are independent
Publisher/Subscriber enables modular communication
Notes: Point 2
Would some example help – what is this modularity you are talking about? Not clear.
Point 3
Is it too soon to talk about Pub/Sub at this level – just to introduce up for non beginners

## Slide 5
Modularity
ROS Nodes are independent software building blocks that compose your robot’s perception, path plan and control
Drivers (sensors, actuators,…)
Processes (read sensor data, move forward,…)
Services (fetch a ball, jump and roll in place,…)
Easy to add and remove
Reduces code complexity compared to monolithic systems
Notes: Modify, Produce or Use information
Modularity is still not clear – add a clarifiying picture and/or change the content
Maybe this and the slide before (What is ROS?) could be as a summarying slides for he end of this introductory section.
Modularity: helps people work alongside each other

## Slide 6
Modularity in practice
LiDAR
Odometry
Camera
Components
Processes
Motors
Move forward
Turn
left
Drive in a circle
TurtleBot

## Slide 7
Pub/sub communication
A Topic is a message channel between nodes
Publisher is the “talker” and Subscriber is the “listener”

## Slide 8
Why ROS?
No need to start to build from the ground up
ROS is 12 years old
  Well-known
  Open source
The closest to an “industry standard”
There are alternatives (LCM, YARP, Drake, Player, …)
Notes: May include interesting pictures :)

## Slide 9
Why ROS?
1) Communication
Between PC, robot and nodes (with pub/sub)
2) Packages
Predefined robot functions (sensor drivers, navigation, IMU)
3) Tools and Software
(Gazebo, Rviz, Rqt, OpenCV,…)
Notes: Comments:
Should we have slides of Gazebo abd RViz after this? (slide 6)

## Slide 10
Tools
Gazebo (Simulator)
Real-world physics simulator
Meant for simulating your robot and its behavior with ROS commands
Rviz (Visualizer)
Visualization of what the robot sees and feels
Supports both real robot and Gazebo

## Slide 11
Gazebo example
$ roslaunch turtlebot3_gazebo turtlebot3_world.launch
Starts master
Opens Gazebo
Has a T-bot
T-Bot

## Slide 12
Rviz example
$ roslaunch turtlebot3_slam turtlebot3_slam.launch slam_methods:=gmapping
Requires a simulated (Gazebo) or real robot to show what it sees
Opens RViz
Shows SLAM view
T-Bot
Notes: Secret behind this picture :)

## Slide 13
ROS Architercture

## Slide 14
Main components
  Master
  Nodes
  Topics
  Messages
Notes: Slide has been shifted up.
Question:
Can we rename the slide as ROS Architecture?

## Slide 15
ROS Master
A server that coordinates nodes
Without master, nodes cannot find each other or exchange messages
Start with $ roscore or $ roslaunch
Only one ROS Master can be running
Node1
Node2
ROS Master
Node3
/Topic1
Notes: Update the picture!

## Slide 16
ROS Node
Smallest computation process, written with Python or C++ (rospy or roscpp)
The “fundamental” building block
Enables modularity
$ rosrun <package> <node>
Nodes can act as …
Drivers (LiDAR)
Functions (move forward)
Servers (service server)
Clients (client to a server)
Notes: Comments:
Add a descriptive picture

## Slide 17
Topic communication
Most common type of communication method between nodes
Topic communication is used in continuous data streams
  Sensor data
  Robot state
Topic
Node
Node
Node
Node
Node
Notes: Add more technical details about topic communication

## Slide 18
Publisher/Subscriber
Also referred to as Pub/Sub
Each node can both
  Publish: send information, regardless of who is receiving it
  Subscribe: receive information, regardless who is sending it
Notes: Question:
Point 2 could be placed after a convincing definition of Pub/Sub

## Slide 19
Pub/Sub example
LiDAR node
  publishes laser scan msgs
Motion controller
  publishes odometry values
  subscribes to motion control msgs
Navigation node
  publishes motion control msgs
  subscribes to LiDAR & odometry msgs
LiDAR
Motion Controller (SCB + ECU + IMU)
Navigation
Odometry: coordinates (x,y,z), linear & angular velocities
Msg: short for message
\scan
\odom
\cmd_vel
Notes: Make sure the arrows are connected to the boxes

## Slide 20
Topics
\scan
(LaserScan) – an array of distance data
\odom
(Odometry) – position and orientation data
\cmd_vel
(Twist) – set linear and angular velocities
Notes: Comments:
Conceptual correctness, difference between message and topic could be slightly misleading

## Slide 21
Topic monitoring
$rostopic list
Provides list of active topics
$rostopic info <topic>
Obtain publisher and subscriber information of the topic

## Slide 22
Topic monitoring
$ rostopic echo <topic>
Shows all messages received on <topic>
$ rostopic hz <topic>
Shows the publishing frequency of the <topic>
Notes: Add pictures of terminals

## Slide 23
Message
Topics handle information through messages
.msg files are simple text files that describe the fields of a ROS message
Example
Info in LaserScan msg:

## Slide 24
More communication methods
In addition to Topic communication, these special communication types are all based on Topics
Service – ask for a predefined function
Action – ask for a predefined function
Parameter – set and get global parameters

## Slide 25
Services
Service examples for a drone...
  “Liftoff”
  “Fly in a circle one lap”
  “Land”
Server/Client structure
Services are Synchronous – while active, robot cannot answer to requests/calls/commands to do something else
  While “Liftoff” is happening, cannot start to “Fly in a circle …”

## Slide 26
Actions
Actions are commands
  Liftoff
  Fly in a circle
  landing
Server/Client structure
Actions are Asynchronous – while active, robot can receive more commands and do them while also performing the original action
  While “Liftoff” is happening, can start to also “Fly in a circle …”

## Slide 27
Parameter communication
Parameter server is shared place for global parameters
Nodes can store and retrieve parameters
Meant for configuration parameters, such as PID gains

## Slide 28
End of first ROS session
– Thank you!