## Slide 1: MEC-E5005 Fluid Power Dynamics L (5 cr)
Time: Fridays 11:15-15:00 o’clock
Schedule:
Staff
Jyrki Kajaste
DSc (Tech), University Teacher
jyrki.kajaste@aalto.fi
MEC-E5005 Fluid Power Dynamics L |  |  |  |  | 
Week | # | Day | Time | Room | Milestone check
37 | 1 | 11.9.2020 | Fri 11:15 - 15:00 | R001/U344 | 
38 | 2 | 18.9.2020 | Fri 11:15 - 15:00 | R001/U257 | 
39 | 3 | 25.9.2020 | Fri 11:15 - 15:00 | R001/U344 | Cylinder model
40 | 4 | 2.10.2020 | Fri 11:15 - 15:00 | R001/A046a | 
41 | 5 | 9.10.2020 | Fri 11:15 - 15:00 | R001/A046a | Valve model
42 | 6 | 16.10.2020 | Fri 11:15 - 15:00 | R001/A046a | 
43 |  | 23.10.2020 |  |  | 
44 | 7 | 30.10.2020 | Fri 11:15 - 15:00 | R001/Y344 | Seal model
45 | 8 | 6.11.2020 | Fri 11:15 - 15:00 | R001/Y344 | Personal simulation work
46 | 9 | 13.11.2020 | Fri 11:15 - 15:00 | R001/U351 | 
47 | 10 | 20.11.2020 | Fri 11:15 - 15:00 | R001/U351 | Group assignment check
48 | 11 | 27.11.2020 | Fri 11:15 - 15:00 | R001/U351 | 
49 | 12 | 4.12.2020 | Fri 11:15 - 15:00 | ? | 
50 | 13 | 11.12.2020 | Fri 11:15 - 15:00 | R001/U351 | Group assignment ready
 |  |  |  |  | Asko Ellman, Tampere University ??

## Slide 2: Workload estimate
Workload
  5 cr
  Lectures 2 h (1 x 2 h) and mini-lessons (12 x 0.5 h)
  Modelling and simulation exercises 36 h (12 x 3 h)
  Autonomous studying, working on exercises and assignment 91 h

## Slide 3: Learning Outcomes
After the course the student is able to:
- Describe the principles of modeling and simulation and the potentials of these in system design and analysis
- Use some modeling and simulation environment/software (Matlab ja Simulink)
- Identify (analyze) dynamic structures of hydraulic systems
- Create models for static and dynamic elements (hydraulic and pneumatic components and systems) and run simulations with them
- Identify (analyze) parameter values for models from component catalogs and measurement results
- Analyze dynamic characteristics of hydraulic systems with the help of measurement data (step and frequency responses)
- Analyze the operation of hydraulic systems by modeling and simulation
- Evaluate critically the quality and deficiencies of a component or system model (i.e. validate the model using measurement data)
- Design and tune an electrohydraulic position, speed and force servo by using modeling and simulation
- Estimate the quality of an electrohydraulic position, speed and force servo by modeling and simulation
- Create well-defined and comprehensive modeling and simulation documents
- Describe the principle of real-time simulation and the special demands of it

## Slide 4: Simulation of Fluid Power
Modeling of fluid properties
Modeling of valves
Modeling of actuators
Modeling of fluid power systems

## Slide 5: Simulation work
Cylinder system
  Hydraulic cylinder (actuator)
  Proportional control valve (Regel Ventil)
  Load (mass)
  Control system (open loop control)
Control system
  PID control of systems
    Position control

## Slide 6: Hydraulic circuit to be modeled 1
M
CONTROL
x
p/U
p/U
pA
pB
U

## Slide 7: Hydraulic circuit to be modeled 2
M
CONTROL
x
p/U
p/U
pA
pB
U
POSITION
CONTROL

## Slide 8: Hydraulic circuit to be modeled 3 option 1
M
M
Direct Driven Hydraulics (DDH) system

## Slide 9: Hydraulic circuit to be modeled 3 option 2
HIL CONTROL
,x
p/U
p/U
pA
pB
Ucommand
Fhydr
https://www.bgmotorsport.co.uk/suspension/ohlins-suspension/ohlins-damper-anatomy/
mS
mU
(measured)
Fdamper
virtual mechanics
HYDRAULIC SERVO ACTUATOR
Motion control
Virtual inputs by ”road”
p/U
pP
m
Fdamper
1
2
3
4
5
6
7
8
9
10
A
11
12
Hardware In the Loop testing arrangement
Sensors for HIL
Damper force
Mass position
Mass velocity
Other sensors
Cylinder force
Cylinder pressure A
Cylinder pressure B
Pump pressure P
Damper pressure A
Damper pressure B
Damper pressure Accu
Fluid temperature
Valve position signal
Output signals
Valve command U
ON/OFF valve A
ON/OFF valve B

## Slide 10: Testing of cylinder model
Use for example Display module to check the end values of signals
Attention!
Do not connect seal model!
Test 1a Test 2
p_A= ________ bar p_A= ________ bar
p_B= ________ bar p_B= ________ bar
F= __________ N F= __________ N
Test 1b Test 3
p_A= ________ bar p_A= ________ bar
p_B= ________ bar p_B= ________ bar
F= __________ N F= __________ N

## Slide 11: Cylinder model benchmarking/checking Documenting
Use blank Word document (or another word processor)
Models to be documented (copying: Edit  Copy Model To Clipboard)
  Chamber A
  Chamber B
  Cylinder model ( Force)
Test results:
  End values after 10 second simulation time (pA, pB, F)
This document material is usable in your personal simulation model report!

## Slide 12: Hydraulic circuit modeling
M
CONTROL
x
pA
pB
U
Phase 3
Proportional valve
pA, pB, pP, pT, U
qA, qB, qP, qT
in
out
qA
qB
qP
qT
U
Calculate
qA, qB, qP, qT by
using control edge models

## Slide 13: Directional control valve
Tesxtbook
p. 58, Fig. 56
The model for proportional control valve can be constructed based on an assumption : the valve consists of four (4) orificices (control edges).
PA - PB - AT - BT
Position of spool defines flow areas of orifices.
Spool valve
Proportional control valve

## Slide 14: Turbulent orifice
V2
-q12IN
p2OUT
V1
q12IN
p1OUT
Flow coefficient
Flow coefficient Cq
Orifice area A0
Pressure difference p
Liquid density 
Flow rate
Textbook
Starting form page 24
Reynolds number

## Slide 15: Simulink realization
Useful moduls for Simulink realization
OR

## Slide 16: Control edge model 1
Model for an individual control edge and an alternative Lookup Table for PB and AT control edges (K curve)
With Abs and Sign modules you take care that the input value for Sqare Root function (Sqrt) is always positive.
Problem!
We really do not know the exact sizes of flow paths in the valve (unless we measure them).
Try for example
Ramp simulation 20 s, slope 1, initial value -10
Table data: [0 1 10]
Breakpoints 1: [-10 0 10]

## Slide 17: Control edge model 2 – parameter K10V
Inputs for control edge model are pressures (p1 ja p1) and control voltage (U). Flow rate (q) is the system output. The valve capacity (”K characteristics”) as a function of voltage can be modeled for instance with 1-D Lookup Table. In a symmetrical valve the characteristics of PA and PB as well as AT and BT are similar but mirros images (see figure below).
The parameters for 1-D Lookup Table can be obtained from valve’s datasheet. To form the characteristics only three points are needed.
Input-vector: [-10 0 10]
Output-vector: [0 K_0V K_10V] (control edges PA and BT).
[K_10V K_0V 0] (control edges PB and AT)
With full opening (U= 10 V or U= -10 V) the flow rate is 40 l/min
as the pressure difference is 35 bar (for valve in the modeling case).
Where qv orifice= 40/60000 m3/s and p= 35105 Pa.
 How to calculate K10V

## Slide 18: Control edge model 3 - leakage
Valve lekage at voltage 0 V and parameter K0V
In our case study the leakage (max.) through valve is 0.9 l/min at pressure difference 100 bar. Then the flows P -> A -> T and P -> B -> T are 0.45 l/min which is in SI system 0.45/60000 m3/s. The leakage can be assumed to divide into two similar flow paths (PAT and PBT).
We examine flow path P -> A -> T. The orifices are in series so orifices PA and AT share the same flow rate q and total pressure difference (100 bar) is the sum of individual pressure difference.
The initial assumption is that the pressure losses are identical pPA = pAT= 50 bar.
With zero control signal
In this leakage case
Qv orifice= 0.45/60000 m3/s and p= 50105 Pa. We can start with these parameters and tune the values based on measurement results. This means for example that PA ja AT leakage orifices can have different parameter values.

## Slide 19: K values for orifices from valve data sheet
K_10V=(40/60000)/sqrt(35e5); %full opening (10 V)
K_0V=(0.45/60000)/sqrt(50e5); %leakage at ”closed”position (0 V)
About the leakage
It can be assumed that all of the four orifices are similar as the valve is in central (”closed”) position. However the valve is of spool type and there is some leakage.
100 bar
Spool at center position: from the data sheet
Pump pressure 100 bar
Total flow below 0.9 l/min
0.9 l/min
0.45 l/min
0.45 l/min
50 bar
50 bar
Actuator channels A and B blocked, no flow.
0 bar
0 bar
All orifices (K_0V):
0.45 l/min @ 50 bar

## Slide 20: Flow rates in a proportional control valve
Model for control edge P -> A
The glow rates of control edges are combined (addition) to get the net flow rates for cylinder chambers qA ja qB as well as for pump and tank flow (qP ja qT ). As the control edges are: PA, PB, AT and BT,
qA= qPA- qAT chamber A qP= qPA+ qPB pump
qB= qPB- qBT chamber B qT= qAT+ qBT tank
qPA
qAT
qA= qPA- qAT
70 bar
35 bar
35 bar

## Slide 21: Wiring the signals in valve model
P the first signal
A the second signal
etc.
Signal U is common for all of the blocks
Attention!
After the block ”Spool Dynamics” signal U describes the relative position of the spool (-10 V – 10 V)
B the first signal
T the second signal
The signs (+ or -)
PA -> fluid into chamber A
AT -> fluid form chamber A

## Slide 22: System control
Valve voltage range is
-10V … +10V
In the test case
Voltage -2 V at t1=2.923 s
Voltage 0 V at t2=4.117 s
Instructions p. 4
At instant t = 2.923 s voltage –2 V is connected to the valve and at instant 4.117 s valve control is set to zero.
System is controlled with proportional control valve
Voltage U connected ON at time t_1 (U)
Voltage U connected OFF at time t_2 (-U)

## Slide 23: Calculation of valve parameters
%Valve
%venttiilin K_10V value for valve (capacity)
K_10V=(40/60000)/sqrt(35e5);
%K_0V value for valve (leakage)
K_0V=(0.45/60000)/sqrt(50e5);

## Slide 24: Turbulent orifice
V2
-q12IN
p2OUT
V1
q12IN
p1OUT
Flow coefficient
Flow coefficient Cq
Orifice area A0
Pressure difference p
Liquid density 
Flow rate
Textbook
Starting form page 24
Reynolds number

## Slide 25: Proportional control valve model
Use blank Word document (or another word processor)
Models to be documented (copying: Edit  Copy Model To Clipboard)
  Orifice model PA (BT)
  Orifice model PB (AT)
  Overall valve model ( A and B chamber flow rates)
Include parameter values and test results:
  Valve parameters K_10V and K_0V (full capacity and leakage)
  Flow rate response (qA, qB) plot, with control -10 V -> +10 V (ramp)
This document material is usable in your personal simulation model report!
Benchmarking 2
Assignment 2

## Slide 26: Valve Model Benchmarking
  Simulation
  As a fucnction of control voltage U
  flow rates into cylinder chambers A and B
  flow rate a) from pump and b) into tank
  20 second simulation
  Valve input -10 V -> +10 V (ramp)
figure
plot(out.U(:,2), out.qv(:,2))
hold on
plot(out.U(:,2), out.qv(:,3),'r')
plot(out.U(:,2), out.qv(:,4),'k')
plot(out.U(:,2), out.qv(:,5),'m')
Benchmarking 2
Input pressures
Pump 70 bar
Cylinder chambers (A,B) 35 bar
Tank 0 bar
Assignment 2

## Slide 27: Spool system dynamics
The dynamics of the proportional valve’s spool can be described (for example) with first order dynamics.
System time constant () defines the dynamics. Appropriate value for it can be found by comparing the magnitude and phase shift of the frequency response (Bode plot) of the model and the actual valve.
After tuning of the time constant also the time domain response should match relatively well with the step response data found in the datasheet (0-> 100 %, 10 ms).

## Slide 28: First order dynamic system, liquid volume and orifice (linear flow restrictor)
What is the transfer function for the system in the figure?
Input: flow rate qv (flow rate in)
Output: pressure p (pressure in volume).
Liquid volume V= 210-3 m3
Bulk modulus Kf= 1.6109 N/m2
Hydraulic resistance R= 1.0109 Pa s/m3
qv

## Slide 29: From differential equation to transfer function
The system is modeled as a hydraulic capacitance and a resistance.
Hydraulic capacitance describes the relation between change in pressure and in flow rate as follows (in Laplace domain).
.
Qv,1
Qv,2
Qv,1 is the flow rate inpout and Qv,2 is the flow rate out of the volume. The difference between the flow rates is the net flow into the volume and it describes the accumulation of liquid in the volume (”accumulation rate”).
The accumulated new volume of fluid
In time domain and In Laplace domain
Qv,1
P
In Laplace domain
p  P
qv  Qv

## Slide 30: Hydraulic capacitance
The hydraulic capacitane is
.
The mathematical model for the valve is
It may be assumed that the pressure downstream of the valve is constant (e.g. p= 0  p= p). The equation for the valve can be combined with the equation on the previous page.
Qv,1
Qv,2
Qv,1
P

## Slide 31: Combining the equations
The transfer function for the system is
Qv,2 is replaced with this.

## Slide 32: Transfer function
,
First order system,
with a transfer function
where
K is the static gain and
 is the time constant for the system.
Time constant defines the system dynamics.
In stationary applications (frequency domain s  j = 0) and pressure upstream of the valve is P= RQv,1. In time domain p= Rqv,1.
With step input the response (step response) is in time domain
where
p is the asymptotic pressure (p= RQ1)
 Is the time constant for the first order system (RC)
First order system 
power here for s is 1 (s(1)).

## Slide 33: Bode plot - Simulink
Input
Output
Mouse right click
Linear Analysis Points
Open-loop Input
Open-loop Output
Menu
APPS
Model Linearizer
OLD:
Analysis
Control Design
Linear Analysis
  New Bode
  Linearize
Bode
Open-loop Input
Open-loop Output
Run the test in time domain  simulate

## Slide 34: Step response
As t = , pressure as risen to value 0.6321 (63.2%) of the end value.
p
[Pa]
Pressure response (step response), as flow rate is altered with an instantaneous stepwise change and point (, 0.6321 p)
t [s]

## Slide 35: Bode plot
Frequency response for first orders system with  =1 s
Magnitude as a function of angular velocity
Phase change as a function of angular velocity
[rad/s]
 =1 s  = 1/ = 1/1 rad/s
-45
Asymptotes
Slope -20 dB/ decade

## Slide 36: Frequency response
Frequency response describes the magnitude and phase shift as a function of frequency (angular velocity).
Magnitude is the relation of output and input signal amplitudes (esim. p / q) as a function frequency
Phase shift is the difference of output and input signal phases as a function of frequency
The same information can be gained experimentally for example by giving sinsoidal inputs to the system and measuring the amplitudes and phases of input and output signals and comparing them with each other.
Spool valve dynamics:
Amplitude of displacement does not equal the desired value and
There is a phase shift between the actual sinusoidal movement and the command signal
Bogth (manitude and phase shift) are (e.g.) frequency dependent.

## Slide 37: Bode plot
For example.
Simulink model with name ’Bodetest’
  Include ”In”- and ”Out”-blocks
[A,B,C,D] = linmod('Bodetest');
sys = ss(A,B,C,D)
figure
h=bodeplot(sys)
setoptions(h,'FreqUnits','Hz','PhaseVisible','off');
setoptions(h,'FreqUnits','Hz','PhaseVisible','on');
grid

## Slide 38: Plot (measured and simulated pressure data)
figure
plot(out.p_a(:,1), out.p_a(:,2)*1e-5,'b')
hold
plot(t_mit,pA_mit,'r')
title(’A volume’)
figure
plot(out.p_b(:,1), out.p_b(:,2)*1e-5,'b')
hold
plot(t_mit,pB_mit,'r')
title(’B volume’)