## Slide 1
Vehicle Mechatronics: Control
Everybody loves ROS
Slides: Jari Vepsäläinen & Pavithra Gopalakrishnan
July 1, 2020
Notes: Reference: Mike Ross or Ross Geller ;) Or everybody loves Raymond!

## Slide 2
Contents
ROS Basics
  What is ROS?
  ROS Tools
ROS Architecture
  Master, Nodes, Messages, Workspace, Packages and Launch Files
ROS Development
  Packages and ROS program files (Node, launch files, …)
ROS Applications
  Example application
ROS Debug
These lecture slides have been inspired by
ROS wiki (wiki.ros.org)
Stanford ASL course AA274: Principles of Robot Autonomy 1
Robot Ignite Academy: ROS Basics

## Slide 3
ROS Application

## Slide 4
An example project
Creating a package
Creating a node
Creating a launch file
Creating a service server
  Calling the server
Creating an action server
  Calling the server

## Slide 5
Example project video
[INSERT VIDEO HERE]

## Slide 6
ROS Debug

## Slide 7
ROS Debug methods
ROS WTF $roswtf
ROS Logs
RQt (Qt-based GUI framework)
  CONSOLE - show logs $rqt console
  PLOT - plot data $rqt plot
  GRAPH - check connections $rqt graph
Record data $rosbag

## Slide 8
ROS WTF (What the F*ck)
Seems like a joke, but it is actually a useful tool
A general firsthand approach $ roswtf
Prints out a message, which helps you in two ways:
  File system issues
    Packages, launch files, environmental variables, …
  Connection issues
    Nodes, topics, services, actions, …
Can also be used to check individual files:
$ roswtf <yourlaunchfile>.launch

## Slide 9
ROS Logs
ROS publishes a lot of information in logs
Severity levels: DEBUG, INFO, WARN, ERROR, FATAL
Print all log messages with $ rostopic echo /rosout
Problem: a lot information
  Level of severity can be set initializing a node
  rospy.init_node(<‘name’>, log_level.rospy.DEBUG)

## Slide 10
RQt Console $rqt console
Graphical user interface to display ROS logs
Enables you to filter messages by name, topic, etc...
All log msgs
Filtered logs
Highlighted logs

## Slide 11
RQt Plotter $rqt plot
Real-time running plotter
Select variables that are plotted by topic
  From command line: $ rqt_plot /turtle1/pose/x:y
  From GUI:

## Slide 12
RQt Graph $rqt graph
Helps you visualize how are topics connected
Helps to spot missing links in the communication network

## Slide 13
ROS Bag $rosbag (1/2)
Record data to later use…
  analysis of a test, making plots
  recreating a scenario for a new test or checking how it worked
When bag data is replayed, the same topics are subscribing and publishing as it was when recorded

## Slide 14
ROS Bag $rosbag (2/2)
Record data
  ALL data:
  $ rosbag record -a <name_of_bag_file>.bag
  Topic based:
  $ rosbag record -O <name_of_bag_file>.bag topic1 topic2 topicN
General info of .bag file: $ rosbag info <name_of_bag_file>.bag
Replay data: rosbag play <name_of_bag_file>.bag

## Slide 15
End of third ROS session
– Thank you!