## Slide 1: MEC-E5005 Fluid Power Dynamics L (5 cr)
Time: Fridays 11:15-15:00 o’clock
Schedule:
Staff
Jyrki Kajaste
DSc (Tech), University Teacher
jyrki.kajaste@aalto.fi
MEC-E5005 Fluid Power Dynamics L |  |  |  |  | 
Week | # | Day | Time | Room | Milestone check
37 | 1 | 11.9.2020 | Fri 11:15 - 15:00 | R001/U344 | 
38 | 2 | 18.9.2020 | Fri 11:15 - 15:00 | R001/U257 | 
39 | 3 | 25.9.2020 | Fri 11:15 - 15:00 | R001/U344 | Cylinder model
40 | 4 | 2.10.2020 | Fri 11:15 - 15:00 | R001/A046a | 
41 | 5 | 9.10.2020 | Fri 11:15 - 15:00 | R001/A046a | Valve model
42 | 6 | 16.10.2020 | Fri 11:15 - 15:00 | R001/A046a | 
43 |  | 23.10.2020 |  |  | 
44 | 7 | 30.10.2020 | Fri 11:15 - 15:00 | R001/Y344 | Seal model
45 | 8 | 6.11.2020 | Fri 11:15 - 15:00 | R001/Y344 | Personal simulation work
46 | 9 | 13.11.2020 | Fri 11:15 - 15:00 | R001/U351 | 
47 | 10 | 20.11.2020 | Fri 11:15 - 15:00 | R001/U351 | Group assignment check
48 | 11 | 27.11.2020 | Fri 11:15 - 15:00 | R001/U351 | 
49 | 12 | 4.12.2020 | Fri 11:15 - 15:00 | ? | 
50 | 13 | 11.12.2020 | Fri 11:15 - 15:00 | R001/U351 | Group assignment ready
 |  |  |  |  | Asko Ellman, Tampere University ??

## Slide 2: Workload estimate
Workload
  5 cr
  Lectures 2 h (1 x 2 h) and mini-lessons (12 x 0.5 h)
  Modelling and simulation exercises 36 h (12 x 3 h)
  Autonomous studying, working on exercises and assignment 91 h

## Slide 3: Learning Outcomes
After the course the student is able to:
- Describe the principles of modeling and simulation and the potentials of these in system design and analysis
- Use some modeling and simulation environment/software (Matlab ja Simulink)
- Identify (analyze) dynamic structures of hydraulic systems
- Create models for static and dynamic elements (hydraulic and pneumatic components and systems) and run simulations with them
- Identify (analyze) parameter values for models from component catalogs and measurement results
- Analyze dynamic characteristics of hydraulic systems with the help of measurement data (step and frequency responses)
- Analyze the operation of hydraulic systems by modeling and simulation
- Evaluate critically the quality and deficiencies of a component or system model (i.e. validate the model using measurement data)
- Design and tune an electrohydraulic position, speed and force servo by using modeling and simulation
- Estimate the quality of an electrohydraulic position, speed and force servo by modeling and simulation
- Create well-defined and comprehensive modeling and simulation documents
- Describe the principle of real-time simulation and the special demands of it

## Slide 4: Simulation of Fluid Power
Modeling of fluid properties
Modeling of valves
Modeling of actuators
Modeling of fluid power systems

## Slide 5: Simulation work
Cylinder system
  Hydraulic cylinder (actuator)
  Proportional control valve (Regel Ventil)
  Load (mass)
  Control system (open loop control)
Control system
  PID control of systems
    Position control

## Slide 6: Hydraulic circuit to be modeled 1
M
CONTROL
x
p/U
p/U
pA
pB
U

## Slide 7: Hydraulic circuit to be modeled 2
M
CONTROL
x
p/U
p/U
pA
pB
U
POSITION
CONTROL

## Slide 8: Hydraulic circuit to be modeled 3 option 1
M
M
Direct Driven Hydraulics (DDH) system

## Slide 9: Hydraulic circuit to be modeled 3 option 2
HIL CONTROL
,x
p/U
p/U
pA
pB
Ucommand
Fhydr
https://www.bgmotorsport.co.uk/suspension/ohlins-suspension/ohlins-damper-anatomy/
mS
mU
(measured)
Fdamper
virtual mechanics
HYDRAULIC SERVO ACTUATOR
Motion control
Virtual inputs by ”road”
p/U
pP
m
Fdamper
1
2
3
4
5
6
7
8
9
10
A
11
12
Hardware In the Loop testing arrangement
Sensors for HIL
Damper force
Mass position
Mass velocity
Other sensors
Cylinder force
Cylinder pressure A
Cylinder pressure B
Pump pressure P
Damper pressure A
Damper pressure B
Damper pressure Accu
Fluid temperature
Valve position signal
Output signals
Valve command U
ON/OFF valve A
ON/OFF valve B

## Slide 10: Hydraulic circuit modeling
M
CONTROL
x
pA
pB
U
Phase 3
Proportional valve
pA, pB, pP, pT, U
qA, qB, qP, qT
in
out
qA
qB
qP
qT
U
Calculate
qA, qB, qP, qT by
using control edge models

## Slide 11: K values for orifices from valve data sheet
K_10V=(40/60000)/sqrt(35e5); %full opening (10 V)
K_0V=(0.45/60000)/sqrt(50e5); %leakage at ”closed”position (0 V)
About the leakage
It can be assumed that all of the four orifices are similar as the valve is in central (”closed”) position. However the valve is of spool type and there is some leakage.
100 bar
Spool at center position: from the data sheet
Pump pressure 100 bar
Total flow below 0.9 l/min
0.9 l/min
0.45 l/min
0.45 l/min
50 bar
50 bar
Actuator channels A and B blocked, no flow.
0 bar
0 bar
All orifices (K_0V):
0.45 l/min @ 50 bar

## Slide 12: Flow rates in a proportional control valve
Model for control edge P -> A
The glow rates of control edges are combined (addition) to get the net flow rates for cylinder chambers qA ja qB as well as for pump and tank flow (qP ja qT ). As the control edges are: PA, PB, AT and BT,
qA= qPA- qAT chamber A qP= qPA+ qPB pump
qB= qPB- qBT chamber B qT= qAT+ qBT tank
qPA
qAT
qA= qPA- qAT
70 bar
35 bar
35 bar

## Slide 13: Valve leakage parameters, tuning
Leakage parameters for (PA and PB) and (AT and BT) can have different values!
Previously
%K parameter for leakage
K_0V=(0.45/60000)/sqrt(50e5);
New version
%K parameters ofr leakage
K_0V1=(0.45/60000)/sqrt(60e5); %K value, leakage, orifices PA and PB
K_0V2=(0.45/60000)/sqrt(40e5); %K value, leakage, orifices AT and BT
The sum of pressure differences remain the same (100 bar). Also the total leakage (0.9 l/min) is the same.
In this case the first orifice is ”tighter” and the second one is ”wider”  pressure in cylinder chamber becomes lower.
K_0V1 for
PA and PB blocks
K_0V2 for
AT and BT blocks

## Slide 14: System control
Valve voltage range is
-10V … +10V
In the test case
Voltage -2 V at t1=2.923 s
Voltage 0 V at t2=4.117 s
Instructions p. 4
At instant t = 2.923 s voltage –2 V is connected to the valve and at instant 4.117 s valve control is set to zero.
System is controlled with proportional control valve
Voltage U connected ON at time t_1 (U)
Voltage U connected OFF at time t_2 (-U)

## Slide 15: Plot (measured and simulated pressure data)
figure
plot(p_a(:,1),p_a(:,2)*1e-5,'b')
hold
plot(t_mit,pA_mit,'r')
title(’A volume’)
figure
plot(p_b(:,1),p_b(:,2)*1e-5,'b')
hold
plot(t_mit,pB_mit,'r')
title(’B volume’)

## Slide 16: Valve Model Benchmarking
  Simulation
  As a fucnction of control voltage U
  flow rates into cylinder chambers A and B
  flow rate a) from pump and b) into tank
  20 second simulation
  Valve input -10 V -> +10 V (ramp)
figure
plot(out.U(:,2), out.qv(:,2))
hold on
plot(out.U(:,2), out.qv(:,3),'r')
plot(out.U(:,2), out.qv(:,4),'k')
plot(out.U(:,2), out.qv(:,5),'m')

## Slide 17: Seal model for hydraulic cylinder
Stribeck curve
Velocity [m/s]
Friction force [N]

## Slide 18: Friction in lubricated contact
Relative velocity*viscosity/load
v/Fn
Friction factor
I Lubricant and contacts between surface roughness peaks, very thin lubricant film
II Both boundary and hydradynamic lubrication prevail, thin lubricant film
III Lubricant film separates surfaces from each other, thick lubricant film

## Slide 19: Static friction model
Pressure dependence
Substitute for Sgn function

## Slide 20: Realization of static friction model
Piston velocity as input
dx/dt -
Divide by constant vs Gain block -> 1/ vs
Square Math function -> square
Change the sign Gain block -> -1
Exponential function Math function -> exp
Subtraction, two constants (FS and FC ) Subtract
Multiplication Product
Addition (FC and expression) Add
Signum function Sgn
Multiplication Product
Multiplication with a constant (b) Gain block -> b
Addition Add
Parameters
vs describes the velocity realated to minimum force
FS static friction force
FC Coulomb friction force
b viscous friction coefficient
Testing:
vs n. 0.02 m/s
FS 1000 N
FC 500 N
b 1000 N/(m/s)

## Slide 21: Dynamic seal model
LuGre model

## Slide 22: Seal parameters
Include these in your parameter file
z_max=0.1e-3; maximum bend (0.1 – 1 mm)
sigma_0= F_s/z_max; spring constant
sigma_1=1*sqrt(sigma_0*m); damping constant

## Slide 23: How to build the simulation model
Input
Stribeck
Time derivative of seal deformation (bending rate) is integrated and used as an input (bend)
z bend of the cylinder seal [m]
0 spring constant of the cylinder seal [N/m]
1 damping constant of the cylinder seal [Ns/m]
b viscous friction coefficient [Ns/m]
Integrate
Input from Load model
Inputs from the model above
Seal force equation
Seal state of deformation

You can take the effect of chamber pressures into account with this. We can disable it for this case.

## Slide 24: Dynamic Friction in Simulink

## Slide 25: Including pump model
in
qA
qB
qP
qT
out
qOUT
p1IN
p2IN
V
q1IN
q2IN
pOUT
V
q=f(p)
T
q
Dp
w
qS
qPRV
P=Tw
Tehty työ saadaan integroimalla teho
Simulink

## Slide 26: Pressure controlled pump
The dynamics of a pressure controlled pump can be described by using a) an integrator or b) first order system (Viersma).
Laplace domain
Time constant  describes the dynamics. Pump has typically meaningful inertia masses (related to a PRV).
Look http://www.eaton.com/ecm/groups/public/@pub/@eaton/@hyd/documents/content/pll_1439.pdf p. 13
Input P
Pressure setting value
Actual pressure value
p_set

## Slide 27: Cylinder end forces
Cylinder ends can be modeled as stiff springs and dampers
Recommendations for parameter values
Kend – maximum force (pressure) of cylinder causes an ”appropriate” deformation (e.g. 0.2 mm)
Damping coefficient
m is the effective inertia load
”left” end
free motion area
”right” end
Inputs
x
x
xmax
Implementation by using Switch blocks

## Slide 28: Parameter values for cylinder end model
m= 234; %load mass
%Ends
K_end= A_a*p_P/0.2e-3; %spring constant
b_end= 0.5*sqrt(K_end*m); %damping coefficient

## Slide 29: Performance of pumps and motors 1
Wilson’s model
Flow rate (output)
Pump torque (input)
Ideal pump and motor
Pump angle set value (0 - 1)
Vi displacement (per revolution)
n rotational speed (1/s)
Cs laminar flow loss coefficient
p pressure difference over pump
fluid kinematic viscosity
fluid density
Cf Coulomb friction coefficient
Cv viscous friection coefficient
Tc constant torque loss
Reference:
Ellmann, A., Kauranne, H. Kajaste, J. & Pietola, M.
EFFECT OF PARAMETER UNCERTAINTY ON RELIABILITY OF HYDRAULIC TRANSMISSION SYSTEM SIMULATION
Proceedingsof IMECE2005 2005 ASME International Mechanical Engineering Congress and Exposition November 5-11, 2005, Orlando, Florida USA
PUMP

## Slide 30
Performance of pumps and motors 2
Wilson’s model
Flow rate (input)
Motor torque (output)
Ideal pump and motor
Motor angle set value (0 - 1)
Vi displacement (per revolution)
n rotational speed (1/s)
Cs laminar flow loss coefficient
p pressure difference over motor
fluid kinematic viscosity
fluid density
Cf Coulomb friction coefficient
Cv viscous friection coefficient
Tc constant torque loss
Reference:
Ellmann, A., Kauranne, H. Kajaste, J. & Pietola, M.
EFFECT OF PARAMETER UNCERTAINTY ON RELIABILITY OF HYDRAULIC TRANSMISSION SYSTEM SIMULATION
Proceedingsof IMECE2005 2005 ASME International Mechanical Engineering Congress and Exposition November 5-11, 2005, Orlando, Florida USA
MOTOR

## Slide 31
figure
plot(t_mit,x_mit)
hold on
plot(x_sim(:,1),x_sim(:,2),’r’)
figure
plot(t_mit,pA_mit,’b’)
hold on
plot(pA_sim(:,1),pA_sim(:,2)*1e-5,’r’)
figure
plot(t_mit,pB_mit,’b’)
hold on
plot(pB_sim(:,1),pB_sim(:,2) *1e-5,’r’)
PLOTS