## Slide 1
Model solution for a much simpler case: Separate molecules A and B from each other as well as possible with a single symmetric H filter. A is much larger than B.
inlet
outlet
Channel
This inlet is the sample
100% A
100% B
0% A (this inlet is just buffer)
0% B
Q
2Q
100% A
50% B
0% A
50% B
Q
Q
Q
This is the optimum solution for single symmetric H filter.
The filter channel with flow 2Q is designed so that A does not mix at all and B mixes completely (if diffusion coefficient allow this neat separation)
Here liquid splits evenly to both outlets after the H filter due to symmetry,
To calculate the Hydraulic resistance, you could get an upper limit estimate by just calculating the single flow path with highest hydraulic resistance.
(Here that would just mean e.g. the path marked red into the image. ΔP =< Q*R1 + 2Q*R2 +Q*R3)
R1
R2
R3

## Slide 2
100% C
100% E
100% M
Step 1: basic architecture, make drawings and investigate how they should be connected.
Step 2: design the geometries and the flow rates of the H filters to achieve suitable separation. (there are at least 2 H filters). The length and cross section of the filter channel are free parameters to be tuned.
Step 3: How to deal with pressure? This should be the last consideration and it is for 2 things: 1. to get the liquid to go in the correct proportions where you want it (symmetry can always help) and 2. to check that the pump pressure capability is not exceeded at the very end.
For pressure the general case might be mathematically challenging…but there is a trick that simplifies the pressure situation a lot. You have seen it on the course in one of the exercises.
Q
C = cells
E = exosomes
M = metabolites
0% C
0% E
0% M
… what next?
Q
2Q
Your design could start like this…you can add more inlets (for buffer presumably) if you want.
What happens next?

## Slide 3
2Q
Q
Q
Q
2Q
Q
Q
R
R
R
2Q + 1Q = 3Q
Q
Q
Q
R
R
R
This is a familiar looking structure with the outlets
I redrew it like this to highlight that in a very clear sense this is just a situation where 3Q is coming in, almost to an intersection, and we want to eventually split it evenly into three outgoing channels.
IF there is a fluidic resistor, that is clearly larger than any resistance in the channel network, then that fully determines where the liquid flows out of the chip. Since in the basic design 3Q is going in, and we want 1Q from each outlet, we put the same R before each outlet.
The advantage is that you can then design the channel dimensions only for filters since their hydraulic resistance is not relevant (as long as it is small enough) The only cost of doing this is that there is extra resistance in the system.