## Slide 1: Process Integration
Timo Laukkanen

## Slide 2: Process Integration
An approach to make process industry processes more efficient
This is done by heat and/or mass integration
Heat integration is done by integrating streams that need heating or cooling using heat exchangers to save energy
Two main approaches:
  Pinch technology
  Mathematical Programming (optimization)

## Slide 3: Heat Integration with Pinch Technology
Targeting before Design

## Slide 4: Phases in Pinch based HEN-Synthesis
Data Extraction
Performance Targets
  Energy, Area, Units, Total Annual Cost
Process Modifications
Design of Maximum Heat Recovery Network
Improvement (tuning)

## Slide 5: Basic Equations for a Countercurrent Heat Exchanger
0
L
A = Area
U = Overall Heat
Transfer Coefficient
Th,in
Th,out
Tc,in
Tc,out
T
x
A=Q/(Utot* ΔTLMTD)
1/U = 1/h1+1/h2
Heat
Specific enthalpy
Specific heat capacity
Mass flow
Specific heat transfer
coefficient

## Slide 6: Data Extraction
Process Streams
  Flowrates
  Temperatures
    Start (Supply) and End (Target)
  Specific Heat Capacity
    Incl. Latent Heat
  Film Heat Transfer Coefficient (for U-estimate)
Utility System/Streams
  Temperature(s)
  Heat Content
  Cost per unit
Heat exchangers
  Cost function(s)

## Slide 7: Data extraction: Small Example
Reactor with two reactants and one product stream
Necessary Data
m cp = 1 kW/K
m cp = 2 kW/K
m cp = 3 kW/K
40°C
300°C
40°C
300°C
315°C
90°C
Reactor
C1
C2
H1

## Slide 8: Data extraction: Stream mixing
Existing system
m cp = 1 kW/K
40°C
80°C
m cp = 1 kW/K
60°C
120°C
C1
C2
m cp = 2 kW/K
100°C
200°C
Pinch streams
C3
Stream | Supply Temp. [⁰C] | Target Temp. [⁰C] | mcp [kW/K]
C1 | 40 | 200 | 1
C2 | 60 | 200 | 1

## Slide 9: Data extraction: Nonlinear Cp
T
Q
Real stream (in blue)
A bad linear approximation of the real stream,
A bad pinch stream approximation
Cp= Q/(m*DT)
A piece-wise linear approximation of the real stream
with two linear stream, a better pinch approximation
Important that the amount of heat and the temperature levels of the pinch streams
are close to the real stream

## Slide 10: Data extraction: Nonadiabatic reactor
Reactor, Q= 100 kW ( f.ex. in AspenPlus positive value stands for endotermic reactor)
Mass flow=1 kg/s,T= 300 C
Mass flow=1 kg/s,T= 300 C
In Aspen a positive value +100 kW stands for an endotermic reaction. In pinch analysis this can be modelled as an isothermic cold stream
Tstart=300, Tend=300, Q=100 kW, cp= infinity
In the enthalpy flow-temperature diagram this is shown as a horizontal stream at 300 C, having 100 kW of heat
If you don’t like these isothermic streams, you can change it to a ”normal” stream
Tstart= 299.9 C, Tend=300 C, Q= 100 KW, cp=Q/(m*DT)= 100/(1*(300-299.9)))= 1000

## Slide 11: Trial and Error: Alternative Networks
Reactor
C1
C2
H1
40°C
300°C
40°C
300°C
315°C
90°C
228°C
210°C
115°C
180 kW
-75 kW

## Slide 12: Trial and Error: Alternative Networks
Reactor
C1
C2
H1
40°C
300°C
40°C
300°C
315°C
90°C
120°C
142°C
180 kW
-75 kW
115°C

## Slide 13: Trial and Error: Alternative Networks
Reactor
C1
C2
H1
40°C
300°C
40°C
300°C
315°C
75°C
75°C
70 kW
35 kW
315°C
90°C
90°C

## Slide 14: Pinch analysis Minimum Qc and Qh?
 | Tsupply (°C) | Ttarget (°C) | m cp (kW/K)
H1 | 400 | 120 | 1.0
H2 | 250 | 120 | 2.0
C1 | 160 | 400 | 1.5
C2 | 100 | 250 | 1.3

## Slide 15: Composite Curves
 | Tsupply(°C) | Ttarget (°C) | m cp (kW/K) | Qtotal (kW)
C1 | 50 | 110 | 1 | 60
H1 | 100 | 60 | 2 | 80
Qc,min = 40kW
Qh,min = 20kW
∆Tmin = 15°C

## Slide 16
 | Tsupply(°C) | Ttarget (°C) | m cp (kW/K) | Qtotal (kW)
H1 | 80 | 20 | 1.0 | 60
H2 | 120 | 40 | 0.5 | 40

## Slide 17
 | Tsupply (°C) | Ttarget (°C) | m cp (kW/K)
H1 | 400 | 120 | 1.0
H2 | 250 | 120 | 2.0
C1 | 160 | 400 | 1.5
C2 | 100 | 250 | 1.3
 | ∆T (°C) | m cp (kW/K) |  |  | Q (kW)
 |  | H1 | H2 | HC | 
400 |  |  |  |  | 
 | 150 | 1.0 |  | 1.0 | 150
250 |  |  |  |  | 
 | 130 | 1.0 | 2.0 | 3.0 | 390
120 |  |  |  |  | 
400
120
250
120

## Slide 18
 | ∆T (°C) | m cp (kW/K) |  |  | Q (kW)
 |  | H1 | H2 | HC | 
400 |  |  |  |  | 
 | 150 | 1.0 |  | 1.0 | 150
250 |  |  |  |  | 
 | 130 | 1.0 | 2.0 | 3.0 | 390
120 |  |  |  |  | 
Q (kW) | T (°C)
0 | 120
390 | 250
540 | 400

## Slide 19
 | Tsupply (°C) | Ttarget (°C) | m cp (kW/K)
H1 | 400 | 120 | 1.0
H2 | 250 | 120 | 2.0
C1 | 160 | 400 | 1.5
C2 | 100 | 250 | 1.3
 |  | m cp (kW/K) |  |  | 
 | ∆T (°C) | C1 | C2 | CC | Q (kW)
400 |  |  |  |  | 
 | 150 | 1.5 |  | 1.5 | 225
250 |  |  |  |  | 
 | 90 | 1.5 | 1.3 | 2.8 | 252
160 |  |  |  |  | 
 | 60 |  | 1.3 | 1.3 | 78
100 |  |  |  |  | 
Q (kW) | T (°C)
0 | 100
78 | 160
330 | 250
555 | 400

## Slide 20
Q (kW) | T (°C)
0 | 100
78 | 160
330 | 250
555 | 400

## Slide 21
∆Tmin=50°C
Qc,min = 200kW
Qh,min = 220kW
heat available
for recovery

## Slide 22
pinch point
heat
deficit
heat
surplus
minimum driving force
pinch
temperature

## Slide 23: Optimal ∆Tmin
Trade-off between utility consumption and driving forces

## Slide 24
 | Tsupply(°C) | Ttarget (°C) | m cp (kW/K) | Qtotal (kW)
H1 | 110 | 50 | 1.0 | 60
C2 | 60 | 100 | 2.0 | 80
∆T | Qc (kW) | Qh (kW) | Qutil (kW) | Th,in | Th,out | Tc,in | Tc,out | ∆Tlm | Q | A
0 | 10 | 30 | 40 | 110 | 60 | 60 | 85 | - | 50 | -
10 | 20 | 40 | 60 | 110 | 70 | 60 | 80 | 18 | 40 | 3.3
20 | 30 | 50 | 80 | 110 | 80 | 60 | 75 | 27 | 30 | 1.9
40 | 40 | 60 | 100 | 110 | 90 | 60 | 70 | 35 | 20 | 1.2
These are now correct

## Slide 25: Optimal ∆Tmin
∆Tmin optimal
min total costs

## Slide 26: Summary Composite Curves
Visualising the system
Key information about the system
  minimum utility consumption, hot and cold (given ∆Tmin)
  pinch point
    decomposition (areas of heat surplus and deficit)
    Temperature of min. driving forces for heat exchange

## Slide 27: 3 Pinch Rules For Maximum Energy Recovery
“Pinch Violations”

## Slide 28: Heat transfer through the Pinch
Heat Deficit
Q
T
pinch temperature
QS, min
Heat Surplus
QW, min
Q
+ Q
+ Q
Q?

## Slide 29: Cooling above and heating below the Pinch
Heat Deficit
Q
T
pinch temperature
QS, min
Heat Surplus
QW, min
Q
+ Q
Q
+ Q

## Slide 30: Summary 3 Pinch Rules
Never transfer heat through the pinch
  Penalty: Increased both hot and cold utility
Never cool (with external cooling) above the pinch
  Penalty: Increased hot utility
Never heat (with external heating) below the pinch
  Penalty: Increased cold utility