## Slide 1: Pinch + LP transshipment
Timo Laukkanen

## Slide 2: What was important in previous Lecture
Data extraction
CC (Composite Curves)
Pinch violations

## Slide 3: Review: Pinch Analysis
A systematic method for saving energy in processes and targeting them by minimizing energy loss in heat exchangers
Based on thermodynamic principles(The first and second laws of thermodynamics) –> clear with no guess or uncertainty.
Define appropriate changes in the process and structure of heat exchangers.

## Slide 4: Philosophy of Pinch Technology
Traditional design:
Three-step design in pinch technology
Problem definition
Design
Problem definition
Design
Targeting
Capital cost
Energy Targeting
Number of units

## Slide 5: What is important in this Lecture
Problem Table Algorithm (PTA)
Heat Cascade
Grand Composite Curve (GCC)
Stream grid
Maximum Energy Recovery (MER) Network
LP Model: Minimum Utility Consumption (Transshipment Model)

## Slide 6: PROBLEM TABLE ALGORITHM
Composite curves are inconvenient. Thus a method based on tables was developed.
STEPS:
Divide the temperature range into intervals and adjust the cold and hot temperature.
Make a heat balance in each interval.
Cascade the heat surplus/deficit through the intervals.
Add heat so that no deficit is cascaded.

## Slide 7: Numerical Method(s) for Energy Targets
Problem Table Algorithm,
Heat Cascade,
Grand Composite Curve

## Slide 8: Step 1 (adjust temperatures)
 | Tsupply (°C) | Ttarget (°C) | m cp (kW/K)
H1 | 400 | 120 | 1.0
H2 | 250 | 120 | 2.0
C1 | 160 | 400 | 1.5
C2 | 100 | 250 | 1.3
∆Tmin = 50°C
Hot streams: T*hot = Thot - ½∆Tmin
Cold streams: T*cold = Tcold + ½∆Tmin
 | T*supply (°C) | T*target (°C) | m cp (kW/K)
H1 | 375 | 95 | 1.0
H2 | 225 | 95 | 2.0
C1 | 185 | 425 | 1.5
C2 | 125 | 275 | 1.3

## Slide 9: Step 2 (temperature intervalls)
 | T*supply (°C) | T*target (°C) | m cp (kW/K)
H1 | 375 | 95 | 1.0
H2 | 225 | 95 | 2.0
C1 | 185 | 425 | 1.5
C2 | 125 | 275 | 1.3
425 °C |  |  |  | 
 | TI 1 | ∆T=50°C |  | 
375 °C |  |  |  | 
 | TI 2 | ∆T=100°C |  | 
275 °C |  |  |  | 
 | TI 3 | ∆T=50°C |  | 
225 °C |  |  |  | 
 | TI 4 | ∆T=40°C |  | 
185 °C |  |  |  | 
 | TI 5 | ∆T=60°C |  | 
125 °C |  |  |  | 
 | TI 6 | ∆T=30°C |  | 
95 °C |  |  |  | 
H1
H2
C1
C2

## Slide 10: Step 3 (enthalpy balance)
425 °C |  |  |  | 
 | TI 1 | ∆T=50°C |  | ∆H1 = 50 * (0.0 - 1.5) = -75
375 °C |  |  |  | 
 | TI 2 | ∆T=100°C |  | ∆H2 = 100 * (1.0 – 1.5) = -50
275 °C |  |  |  | 
 | TI 3 | ∆T=50°C |  | ∆H3 = 50 * (1.0 – 1.5 - 1.3) = -90
225 °C |  |  |  | 
 | TI 4 | ∆T=40°C |  | ∆H4 = 40 * (1.0 + 2.0 – 1.5 – 1.3) = 8
185 °C |  |  |  | 
 | TI 5 | ∆T=60°C |  | ∆H5 = 60 * (1.0 + 2.0 – 1.3) = 102
125 °C |  |  |  | 
 | TI 6 | ∆T=30°C |  | ∆H6 = 30 * (1.0 + 2.0) = 90
95 °C |  |  |  | 
H1
1.0
H2
2.0
C1
1.5
C2
1.3

## Slide 11: Step 4 (cascade the heat flow)
-75
-125
-215
-207
-105
-15
425 °C |  | 
 | TI 1 | -75
375 °C |  | 
 | TI 2 | -50
275 °C |  | 
 | TI 3 | -90
225 °C |  | 
 | TI 4 | 8
185 °C |  | 
 | TI 5 | 102
125 °C |  | 
 | TI 6 | 90
95 °C |  | 
215
140
90
0
8
110
200
200
Hot Utility
Pinch Point
Cold Utility

## Slide 12: Summary Problem Table Algorithm
Adjust (shift) the temperatures
Find the temperature intervals
Calculate the enthalpy balance for each interval
  heat surplus (+) and deficit (-)
Cascade the enthalpy
  add large deficit at the top
Make the heat cascade thermodynamically feasible

## Slide 13: Grand Composite Curve
A graphical representation of heat cascade
It gives clear visualization of hot and cold utilities within each temperature interval
provides an easy approach to use multiple utilities in the process.
Highlights the process utility interface.

## Slide 14: Grand Composite Curve
425 °C |  | 
 | TI 1 | 
375 °C |  | 
 | TI 2 | 
275 °C |  | 
 | TI 3 | 
225 °C |  | 
 | TI 4 | 
185 °C |  | 
 | TI 5 | 
125 °C |  | 
 | TI 6 | 
95 °C |  | 
215
140
90
0
8
110
200
200
50
100
150
200
Q (kW)
T(°C)

## Slide 15: Grand Composite Curve (GGC)
Visualizes the surplus and deficit heat at different temperature intervals
Provides an visual tool for integrating
  Different utilities
  Different processes
  Heat pumps
  Other thermodynamic cycles
50
100
150
200
Q (kW)
T(°C)
Other process
Heat integration possibility
between processes
HP steam
LP steam

## Slide 16: Information Available from Grand composite curve (Example)
Heat sink
Heat Source

## Slide 17: Heat Exchanger Network Design
Stream Grid,
MER Network

## Slide 18: Stream Grid
 | Tsupply (°C) | Ttarget (°C) | m cp (kW/K)
H1 | 400 | 120 | 1.0
H2 | 250 | 120 | 2.0
C1 | 160 | 400 | 1.5
C2 | 100 | 250 | 1.3
∆Tmin = 50°C,
Tpinch = 225°C
Qh = 215 kW, Qc = 200 kW
Tpinch, cold = 200°C
Tpinch, hot = 250°C
H1
C1
H2
C2
1.0
2.0
1.5
1.3

## Slide 19: Stream Matches
Qh = 215 kW, Qc = 200 kW
Tpinch, cold = 200°C
Tpinch, hot = 250°C
H1
C1
H2
C2
1.0
2.0
1.5
1.3
400°C
120°C
120°C
400°C
160°C
250°C
100°C
QH1 = 1.0 * (400 – 250) = 150kW
QC1 = 1.5 * (400 – 200) = 300 kW
Q = 150 kW
Q = 150 kW
QC2 = 1.3 * (250 – 200) = 65 kW
Q = 65 kW

## Slide 20: Stream splitting
When Stream splitting is necessary?
  When it is not possible to match streams around the pinch point.
Two main reasons for the stream splitting:
  1. Number of hot and cold streams
  2. Heat capacity of hot and cold streams

## Slide 21: Stream splitting
Qh = 215 kW, Qc = 200 kW
Tpinch, cold = 200°C
Tpinch, hot = 250°C
H1
C1
H2
C2
1.0
2.0
1.5
1.3
120°C
120°C
160°C
100°C
1.0
0.5
1.3
0.7
Q = 40 kW
QH = 130kW
QC = 40kW
QH = 91kW
QC = 20kW
Q = 20 kW
QH = 169kW
QC = 130kW
Q = 130 kW
Q = 90 kW
Q = 110 kW

## Slide 22: Summary Stream Grid and MER-Network
Draw the Stream Grid
  draw the pinch(es)
  draw the streams above and below the pinch
Match streams starting at the pinch
  (m cp)out >= (m cp)in
  Split streams if necessary
Calculate the heat exchanger duty
  Remember hot and cold streams have different pinch temperature!

## Slide 23: Sequential Heat Exchanger Synthesis
LP Model:
Minimum Utility Consumption (Transshipment Model)

## Slide 24: Temperature Intervals
 | Tsupply (°C) | Ttarget (°C) | m cp (kW/K)
H1 | 400 | 120 | 1.0
H2 | 250 | 120 | 2.0
C1 | 160 | 400 | 1.5
C2 | 100 | 250 | 1.3
∆Tmin = 50°C
Hot Utility: Steam at 450°C
Cold Utility: Water at 20°C
Find the starting temperatures of all streams (and utilities)
Keep one column for hot temperatures and one for cold
  Add ∆Tmin to get hot, substract to get cold

## Slide 25
 | 450 |  | 400 |  |  |  |  | 
 |  | TI 1 |  |  |  |  |  | 
 | 400 |  | 350 |  |  |  |  | 
 |  | TI 2 |  |  |  |  |  | 
 | 250 |  | 200 |  |  |  |  | 
 |  | TI 3 |  |  |  |  |  | 
 | 210 |  | 160 |  |  |  |  | 
 |  | TI 4 |  |  |  |  |  | 
 | 150 |  | 100 |  |  |  |  | 
 |  | TI 5 |  |  |  |  |  | 
 | 70 |  | 20 |  |  |  |  | 
 | Tsupply (°C) | Ttarget (°C) | m cp (kW/K)
H1 | 400 | 120 | 1.0
H2 | 250 | 120 | 2.0
C1 | 160 | 400 | 1.5
C2 | 100 | 250 | 1.3
∆Tmin = 50°C
Hot Utility: Steam at 450°C
Cold Utility: Water at 20°C
H1
120
H2
120
C1
C2
250

## Slide 26
 | Tsupply (°C) | Ttarget (°C) | m cp (kW/K)
H1 | 400 | 120 | 1.0
H2 | 250 | 120 | 2.0
C1 | 160 | 400 | 1.5
C2 | 100 | 250 | 1.3
∆Tmin = 50°C
Hot Utility: Steam at 450°C
Cold Utility: Water at 20°C
 | 450 |  | 400 |  | H1 | H2 | C1 | C2
 |  | TI 1 |  |  |  |  | 75 | 
 | 400 |  | 350 |  |  |  |  | 
 |  | TI 2 |  |  | 150 |  | 225 | 65
 | 250 |  | 200 |  |  |  |  | 
 |  | TI 3 |  |  | 40 | 80 | 60 | 52
 | 210 |  | 160 |  |  |  |  | 
 |  | TI 4 |  |  | 60 | 120 |  | 78
 | 150 |  | 100 |  |  |  |  | 
 |  | TI 5 |  |  | 30 | 60 |  | 
 | 70 |  | 20 |  |  |  |  | 
H1
120
H2
120
C1
C2
250

## Slide 27
TI 1
H1
H2
TI 2
C1
C2
TI 3
TI 4
TI 5
150
40
60
30
80
120
60
75
225
60
65
52
78
R1
R2
Qs
Qw
R3
R4

## Slide 28
R1 + 75 = Qs
R2 + 225 + 65 = R1 + 150
R3 + 60 + 52 = R2 + 40 + 80
R4 + 78 = R3 + 60 + 120
Qw = R4 + 30 + 60

## Slide 29
R1 + 75 = Qs
R2 + 225 + 65 = R1 + 150
R3 + 60 + 52 = R2 + 40 + 80
R4 + 78 = R3 + 60 + 120
Qw = R4 + 30 + 60
Min Z = Qs + Qw
s.t. R1 – Qs = 75
R2 - R1 = -140
R3 - R2 = 8
R4 - R3 = 102
Qw - R4 = 90
Qs, Qw, R1, R2, R3, R4 ≥ 0

## Slide 30: General Formulation
Sets
index
Variables
Parameters

## Slide 31
Interval k
hot process
cold process
hot utility
cold utility

## Slide 33: Sequential Heat Exchanger Synthesis
Optimization of utilities consumption
LP-transshipment model
Minimization of number
of units
MILP-transshipment model
Optimization of network cost
NLP-superstructure
Result OK?
YES, STOP
NO, new DTmin value
Problem Data
(streams, cost)
DT min value

## Slide 34: Summary LP-transhipment model
Find the starting temperatures of all streams (and utilities)
One column for hot and cold streams
  Add ∆Tmin to get hot, substract to get cold
Define which streams are active in each temperature interval and calculate their heat amount
Draw the cascade diagram
Formulate the model