## Slide 1
Antti Vepsäläinen
Lecture notes on PHYS-C0254 Quantum Circuits

## Slide 2
9.Single-qubit operations:
  Initialization 2nd DiVincenzo criteria
  Readout 5th DiVincenzo criteria
  Control:T1, T2 measurements, Randomized benchmarking 3rd DiVincenzo criteria
a.
b.
c.
reset
Qubit signal (a.u.)
0
50
100
150
200
250
300
Time (ns)
natural qubit decay
Qubit in state
Qubit in state
Short recap from last week

## Slide 3: Agenda for lectures 7-12
7. Quantization of electrical networks
  a. Harmonic oscillator: Lagrangian, eigenfrequency
  b. Transfer step: LC oscillator, Legendre transform to Hamiltonian
  d. Quantization of oscillators
8. Superconducting quantum circuits
  a. Qubits: Transmon qubit, Charge qubit, Flux qubit 1st DiVincenzo criteria
  b. Circuit-QED: Rabi model
  c. Rotating Wave approximation: Jaynes-Cummings model
9.Single-qubit operations:
  Initialization 2nd DiVincenzo criteria
  Readout 5th DiVincenzo criteria
  Control:T1, T2 measurements, Randomized benchmarking 3rd DiVincenzo criteria
10. Two-qubit operations: Architectures for 2-qubit gates 4th DiVincenzo criteria
  a. iSWAP
  b. cPhase
  c. cNot
11. Quantum algorithms
  a. Deutsch-Josza Algorithm
  b. Parameterised circuits and VQE
12. Challenges in quantum computing
  a. Scaling
  b. SW-HW gap
  c. Error-correction

## Slide 4: General approach: Two-qubit gates
The 4th DiVicenzo criterion is being able to generate entanglement via two-qubit gates (operations)
Three favorite gates with transmon qubits are:
  iSWAP & entangling sqrt(iSWAP)
  CPhase
  CNOT
They are realized by creating a mutual interaction between the qubits, either directly or through a coupling element.

## Slide 5: Short intro: The basic elements of quantum algorithms
time

## Slide 6: Agenda for today
10. Two-qubit operations: Architectures for 2-qubit gates 4th DiVincenzo criteria
  a. iSWAP
  b. cPhase
  c. cNot
a.
b.
c.

## Slide 7: General approach: iSWAP gate
A general task in (quantum) logic is to swap states. By adding a phase factor, one can create an iSWAP gate.
Since this is a two-qubit gate, we realize it by coupling two qubits mutually on a chip.
By controlling the interaction time, we can also implement sqrt(iSWAP) gates.

## Slide 8
The swap gate exchange the state of two qubits. With respect to the basis , , , , it is represented by the matrix:
The swap gate between two qubits
Applied to two qubits, the input-output relations are given as
Since the swap gate is hard to realize, we first focus on the iSWAP gate.

## Slide 9
The iSWAP gate is a 2-qubit XX+YY interaction and a Clifford and symmetric gate. Its action is to swap two qubit states and puts phase of -i on the swapped elements.
The iSWAP gate between two qubits
-
-
The matrix representation of this system is given as

## Slide 10
The iSWAP gate with tunable qubits
To realize the target unitary of the iSWAP gate, we consider two capacitively coupled transmon qubits in the limit Cg << C1, C2:
Similar to qubits coupled to resonators, the interaction is given by the respective voltage coupled through a mutual capacitance:
Here the voltage is proportional to the excitation number in the non-linear oscillators:

## Slide 11
The iSWAP gate with tunable qubits
The total system Hamiltonian therefore reads as
In the language of second quantization we have
and after Taylor expansion of the cosine:
This capacitive coupling is called transversal, it couples energy levels to each other, but not to itself. I.e. the operator is zero along the diagonal (like the X and Y operators).
Physically this is like a photon exchange between the two systems where one qubit loses a photon and the other one gains. When the coupling is to the environment such processes are responsible for energy loss of the system described by the T1 time.

## Slide 12
The iSWAP gate with tunable qubits
As earlier, we can apply a rotating-wave approximation (RWA) to ignore fast rotating terms like
Here we have used the detuning of the two qubits
This means that we get significant interaction only if the two qubits are on resonance. For large detuning, the interaction averages out due to the fast-rotating terms proportional to d.
Truncating the system Hamiltonian to 2 levels (qubit approximation) yields

## Slide 13
The iSWAP gate with tunable qubits
From this notion and assuming we are on resonance, we can derive the unitary expression
To obtain the iSWAP gate, we need sin(gt ) = 1 and cos(gt )=0. This is the case for

## Slide 14
The sqrt(iSWAP) gate with tunable qubits
SQRT(SWAP) is an important entangling gate, yet so non-intuitive. Here we use the fact that U=exp(iHt) so H is the log of U. That makes a sqrt in the U into a simple division by 2 in the time.
To obtain the iSWAP gate, we need sin(gt ) = 1 and cos(gt )=0. This is the case for

## Slide 15: Review: iSWAP gate
A general task in (quantum) logic is to swap states. By adding a phase factor, one can create an iSWAP gate.
Since this is a two-qubit gate, we realize it by coupling two qubits mutually on a chip.
By controlling the interaction time, we can also implement sqrt(iSWAP) gates.

## Slide 16: Agenda for today
10. Two-qubit operations: Architectures for 2-qubit gates 4th DiVincenzo criteria
  a. iSWAP
  b. cPhase
  c. cNot
a.
b.
c.

## Slide 17: General approach: cPhase gate
The cPhase gate is a diagonal and symmetric gate that induces a phase on the state of the target qubit, depending on the control state.
Since this is a two-qubit gate, we realize it by coupling two qubits mutually on a chip.
By controlling the interaction time and coupling strength, we can control the exact phase induced to the target qubit.

## Slide 18
The controlled phase (cPhase) gate is a diagonal and symmetric gate that induces a phase on the state of the target qubit, depending on the control state:
The cPhase gate between two qubits
Applied to two qubits, the input-output relations are given as
There are no swap operations involved in this gate.

## Slide 19
The cPhase gate with tunable qubits
To realize the cPhase gate, we need longitudinal interaction.
A longitudinal interaction is purely diagonal (like the Z operator, i.e. magnetic dipole coupling, i.e. inductive coupling) and affects the energy level splitting, but does not couple states to one another. This kind of coupling is responsible for the T2 time of the system when there is a magnetic coupling to an environment.
To implement this interaction, we consider two qubits inductively coupled to each other
It can be shown that they follow a ZZ interaction:

## Slide 20
The cPhase gate with tunable qubits
In matrix form, the bare qubit terms read:
In a similar fashion, the interaction term is proportional to
Hence, the total system Hamiltonian is given as
https://inst.eecs.berkeley.edu/~cs191/fa14/lectures/lecture5.pdf

## Slide 21
The cPhase gate with tunable qubits
Then, by controlling the qubit frequencies we set
Which leads to
Hence, the cPhase gate is achieved by choosing

## Slide 22: Review: cPhase gate
The cPhase gate is a diagonal and symmetric gate that induces a phase on the state of the target qubit, depending on the control state.
Since this is a two-qubit gate, we realize it by coupling two qubits mutually on a chip.
By controlling the interaction time and coupling strength, we can control the exact phase induced to the target qubit.

## Slide 23: Agenda for today
10. Two-qubit operations: Architectures for 2-qubit gates 4th DiVincenzo criteria
  a. iSWAP
  b. cPhase
  c. cNot
a.
b.
c.

## Slide 24: General approach: cNot gate
In computer science, the controlled NOT gate (also C-NOT or CNOT) is a quantum logic gate that can be used to entangle and disentangle qubits.
The CNOT gate operates on a quantum register consisting of 2 qubits. The CNOT gate flips the second qubit (the target qubit) if and only if the first qubit (the control qubit) is | 1 ⟩.
Any quantum circuit can be simulated to an arbitrary degree of accuracy using a combination of CNOT gates and single qubit rotations.

## Slide 25
Controlled-NOT gate applies a swap to the target qubit if the
control qubit is in state |1〉
The cNOT gate between two qubits
Applied to two qubits, the input-output relations are given as

## Slide 26
It can be shown that a cNOT gate can be implemented as a series of Hadamard and cPhase gates
The cNOT gate between two qubits
Altogether, we can now create a universal quantum gate set
Informally, a set of universal quantum gates is any set of gates to which any operation possible on a quantum computer can be reduced, that is, any other unitary operation can be expressed as a finite sequence of gates from the set.

## Slide 27: Short review: cNot gate
In computer science, the controlled NOT gate (also C-NOT or CNOT) is a quantum logic gate that can be used to entangle and disentangle qubits.
The CNOT gate operates on a quantum register consisting of 2 qubits. The CNOT gate flips the second qubit (the target qubit) if and only if the first qubit (the control qubit) is | 1 ⟩.
Any quantum circuit can be simulated to an arbitrary degree of accuracy using a combination of CNOT gates and single qubit rotations.

## Slide 28
Example: How to generate a Bell state
The Bell states are four specific maximally entangled quantum states of two qubits. They are in a superposition of 0 and 1, their entanglement means the following:
The first qubit can be 0 as well as 1 and measuring the qubit in the standard basis, the outcome would be perfectly random, either possibility 0 or 1 having probability 1/2.
If the second qubit is measured, the outcome would be random on first sight. But if the results are communicated, they would find out that, although their outcomes seemed random, they are perfectly correlated.
This perfect correlation at a distance is special: maybe the two particles "agreed" in advance, when the pair was created (before the qubits were separated), which outcome they would show in case of a measurement.
Hence, following Einstein, Podolsky, and Rosen in 1935 in their famous "EPR paper", there is something missing in the description of the qubit pair given above—namely this "agreement", called more formally a hidden variable.

## Slide 29
Example: How to apply a SWAP gate

## Slide 30: Review: Two-qubit gates
The 4th DiVicenzo criterion is being able to generate entanglement via two-qubit gates (operations)
Three favorite gates with transmon qubits are:
  iSWAP & entangling sqrt(iSWAP)
  CPhase
  CNOT
They are realized by creating a mutual interaction between the qubits, either directly or through a coupling element.

## Slide 31: Agenda for today
10. Two-qubit operations: Architectures for 2-qubit gates 4th DiVincenzo criteria
  a. iSWAP
  b. cPhase
  c. cNot
a.
b.
c.