## Slide 1: WAT-E1100 Water and Environmental Engineering
Geospatial Information Systems (GIS)
Teemu Kokkonen
Email: firstname.surname@aalto.fi
Tel. 09-470 23838
Room: 272 (Tietotie 1 E)
Water Engineering
Department of Built Environment
Aalto University School of Engineering
Pixabay CC0

## Slide 2: What do we mean by GIS?
GIS is a tool (hardware, software, data) for storing, analysing and visualising geographically referenced information
  ”Mapping Engine”
  Geographically Referenced Data
  Data that has a defined location expressed by coordinates

## Slide 3: Two Types of Spatial Data
Figure: vimeo

## Slide 4: Raster Data
The region of interest is divided into a grid of regular rectangles
  Typically squares having an equal spacing in x and y dimensions
Building blocks of raster data
  Cell values
  Data type
    Integer, floating number
  Size of the raster
    Number of rows, number of columns, cell size
  Location of the raster
    Coordinates of a give cell (e.g. the lower left corner)
  NoData value

## Slide 5: Grid coordinates vs. map coordinates

## Slide 6: Vector Data
Features of the real world (e.g. cities, rivers, country borderes…) are respresented a set of x,y coordinate pairs that can be joined in a given order
  Points, lines, polygons
Building blocks of vector data
  Point coordinates, information how the coordinates connect to each other
  Extent: specifies the region within which the vector features are located
  Field values: information about the location that the vector represents on the map
    E.g. if a point represents a city, a field called CityName could have a value of Helsinki

## Slide 7: Raster or Vector Representation?
Figure: Ayyappan

## Slide 8: Raster Data: Pros and Cons
Data analysis is easy to programme and quick to perform
  Position in the grid implies the geographic location
Representation of continuous data (e.g. elevation) is just as easy as representation of discrete data (e.g. location of national parks)
Each location (grid cell) is included in the raster irrespective wheter it is relevant or not => inefficient storage
Inaccurate scaling in space (zooming), linear features become ’zigzagged’
Representing topological information is not straigtforaward (needed e.g. in network anaysis)

## Slide 9: Vector Data: Pros and Cons
Can be represented in the resolution of the original data
Describing complex geometries is easy and does not consume much space
Continuous data is not efficiently represneted
Geospatial analyses for continuous variables (such as elevation) are inefficient

## Slide 10: Efficient Analysis (Raster Data)
  Compute slope and aspect from elevation data.

## Slide 11: Efficient Storage (Vector Data)

## Slide 12: Geoprocessing
Geoprocessing is a GIS operation used to manipulate spatial data. A typical geoprocessing operation takes an input dataset, performs an operation on that dataset, and returns the result of the operation as an output dataset.
      Wikipedia –
Common geoprocessing tools
  Clip, buffer, intersect…
  ArcGIS Pro Online Manual
  Map algebra
  Projections

## Slide 13: Map Algebra
Map algebra refers to applying arithmetic and logical operations to GIS layers
According to the spatial neighbourhod operations are categorized to:
  Local operations: operations are applied on per-cell basis
    E.g B = tanA, C = B + A, B = IF (A > 100; 1; 0)
  Focal operations: operations are applied to the given cell and its neighbourhood
    E.g. B = slope A, B = FlowDirection A
  Zonal opetaions: operations are applied on given sub-region (zone) basis
    E.g. B = sum A in zones defined by C
  Global operations: operations are applied to the entire layer
    E.g. global summary statistics (mean, max, min of a layer)

## Slide 14: Geographic Coordinate Systems
Coordinate system allowing specifying every location on the Earth by a set of numbers
  A common pair of coordinates is the latitude and the longitude
Latitude
  Angle between the equatorial plane and the straight line that passes through the given location and through center of the Earth
Longitude
  Angle east or west from a reference meridian and the meridian that passes through the given location
Figure: Wikipedia

## Slide 15: Cartographic Projections
Method to represent the 3-dimensional surface of the earth on a 2-dimensional plane in cartography (mapmaking)
Projecting the 3D surface of the Earth on a 2D plane inevitably leads to distortion in e.g.
  Shape
  Distance
  Area
Map projections can preserve at least one of these properties
Figure: Strebe CC BY-SA 3.0

## Slide 16: Coordinate Systems
Geographic coordinate systems use a three-dimensional spherical surface to define locations on the Earth
  In brief: a location is represented by a pair of latitude and longitude values
  A widely used geographic coordinate system is WGS84
  In WGS84 the Water Laboratory is located at 60.186N 24.819E (60˚11'10.2"N 24˚49'09.4"E)
Projected coordinate systems are defined on a flat, two-dimensional surface
  In brief: a location is defined by x and y coordinates on a grid, with the origin at the center of the grid
  The National Survey of Finland currently uses the ETRS-TM35FIN coordinate system
  In ETRS-TM35FIN the Water Laboratory is located at N 6674143 E 379071
Figure: Strebe CC BY-SA 3.0

## Slide 17: Conversion Between Coordinate Systems
There are a lot different coordinate systems at use
  Different systems in different regions of the world
  Different systems also within the same region e.g. due to historical evolution of the preferred systems
If your data layers that should be from the same area do not overlap it is most likely due to different coordinate systems and lacking projection information!
  Either reproject all data sets to the same coordinate system (safest way)…
  …or make sure that you have assigned the correct projection to all you data layers so that your GIS software can show them in the correct location

## Slide 18: GIS courses in Aalto
Master's Programme in Geoinformatics