## Slide 1: MEC-E5004 Fluid Power Systems
22.9.2020
jyrki.kajaste@aalto.fi
5 credits

## Slide 2: Structure of studies and Grade components
IN BRIEF
Presentations and lectures
Simulation assignments
  Tuning a hydraulic servo
  Building hydraulic simulation models
    Load Sensing (LS) system
    Direct Drive Hydraulic (DDH) system
  Each student: Individual Reports
Group assignment
  3 calculation assignments
  group’s discussions with the teacher
Common and organized Studies (almost) every Tuesday 16.15-18.00
Simulation (4) and servo simulation (2) exercises on 4 Wednesdays 16.00-18.00 (see detailed schedule)
Student groups arrange their own meetings and teamwork conventions

## Slide 3: Introduction to Energy Efficient Fluid Power
The main theme of Fluid Power Systems course year 2020 is
Energy Efficient Fluid Power
The
Presentations
Lectures
given by our researchers support this main theme
Other relevant topics in modern and future Fluid Power also introduced.

## Slide 4: Schedule
Preliminary schedule
(under construction)
Tuesday sessions could be used also for simulations
3 Calculation assignments
2 Simulation assignments
2 Servo simulations
Group meeting

## Slide 5: Group assignments (group works)
Wish is to … have groups with 3 members
Output
3 calculation assignments
1 group’s meeting with the teacher  plan
Build up your team until Tuesday 15.9.2020
Use MyCourses page Assignments
18 students ?

## Slide 6: Boundary conditions in calculations
Fluid Power Systems

## Slide 7: Directional control valve (ON/OFF) - case
A
B
C
M
D
E
F
G
G
P
T
A
B
M
H
Reference system
A mass (gravitational) load
B differential cylinder
C directional control valve (ON/OFF)
D pump
E electric motor
F pressure relief valve
G reservoir/tank
H filter
These lines missing -> valve is ON/OFF
Closed OR
Fully open
Some leakages, if spool valve
IF the PRV pressure is high enough, the cylinder piston will be lifted with speed determined by
Pump’s flow rate
  Note pump leakages!
The boundary condition is
Pump’s flow rate qv.pump
Pressures in the system and also pump pressure depend on
Load (gravity load) + seal friction
Flow friction
  In valve
  Pipe system
  Filter
qv.pump
qv.pump  vcylinder  psystem
Note!
If piston hits the cylinder end  boundary condition  pPRV
If ON/OFF valve is closed  cylinder pressures depend on load and leakage
Pressure increasing
Pressure increasing
Pressure increasing
Pressure (and flow rate) transformation
Load
Differential cylinder
CASE 1
FOR TRADITIONAL HYDRAULICS with CONSTANT DISPLACEMENT PUMP
IF pP > pPRV  next page

## Slide 8: Proportional directional control valve - case
A
B
C
M
D
E
F
G
G
P
T
A
B
M
H
These lines present -> valve is proportional
Closed  Fully open
Some leakages, if spool valve
IF the LOAD pressure OR/AND the pressure losses in valves etc. are high enough, the cylinder piston will be lifted with speed determined by
Pump’s (PRV’s) pressure
  Pump leakages NOT relevant!
Proportional control valve’s opening (area)
The boundary condition is
Pump’s (PRV’s) pressure (pP)
Pressures in the system and also pump pressure depend on
Load (gravity load) + seal friction
Flow friction
  In valve
  Pipe system
  Filter
qv.pump
ppump  vcylinder
CASE 2
Pressure decreasing
Pressure decreasing
Pressure decreasing
Pressure (and flow rate) transformation
Load
Differential cylinder
Equations
Cylinder’s force balance
  Load force
  Pressure A
  Pressure B
  (Friction)  equation
Cylinder pressures related to
  Pressure losses in proportional control valve’s control edge pressure losses
  E.g. Lifting equations for
  BT: v and U  pB equation
  PA: pB, v and U  pA equation
Solve v (equation)
FOR MODERN HYDRAULICS with CONSTANT DISPLACEMENT PUMP
IF
Load force is the same
Pump pressure is the same  better controllability
IF pP < pPRV  previous page

## Slide 9: Example, part 5
Solution 2a
HYDRA concept – Multi-pressure system
(Tampere University of Technology and Aalto University)
The pump flow is directed into pressure accumulator
The system is controlled by using (”large”) ON/OFF valves to (1) allow or (2) prohibit flow (not to throttle flow)  pressure losses are small
Also the potential energy of the load can be utilized by directing flow of high pressure fluid into the accumulator
The power of the electric motor and pump can be small (average power)
Peak power is provided by the accumulator
9
x
G
pA
pB
M
N2
CONTROL (ON/OFF)
VALVES
SMALL ELECTRIC MOTOR AND PUMP
(AVERAGE POWER)
CONTROL BY USING (LARGE AREA) ON/OFF VALVES
ONLY MINOR PRESSURE LOSSES
N2
ON
OFF
N2
N2
N2
20 – 40 – 60 – 80 – … bars
Pick the proper pressure!
Multiple pressure levels to choose from

## Slide 10: Example, part 6
Solution 2b
HYDRA concept
Accumulator provides power peaks, the pressure must be adapted by using pressure transformers  input pressure corresponds to the pressure needed by the actuator
The pressure losses in valves are small because a) provided pressure and actuator pressures are close to each other b) valve capacities are high (ON-OFF, NOT proportional control valves)
Potential energy and kinetic energy can be stored in accumulator and utilized/reused ()
Very good energy efficiency!
STORE
accumulator
POWER SOURCE
pump
ADAPTATION OF PRESSURE
Pressure transformers
p1 A1 = p2 A2
DIRECTING OF FITTED PRESSURE
on/off valves
USE OF POWER
actuator
TO ENERGY STORE
ADAPT
DIRECT
ACTUATOR
APPLICATION OF DIGITAL HYDRAULICS
1
2
3
4
5
6
Multi-pressure system (6 pressure levels) – only 1 (or 2) accumulators

## Slide 11
Video
https://www.youtube.com/watch?v=qEUYtT-CWuo
https://www.youtube.com/watch?v=egS1m3Qz_FM
Business talk in Finnish
https://www.youtube.com/watch?v=PMw8OVV-KSs
https://www.sijoittaja.fi/66653/analyysissa-norrhydro-tutustu-houkuttelevaan-osakeantiin
Multi chamber cylinders
Norrhydro’s multi chamber cylinder system
Cylinder with 4 chambers and piston areas
2 forces in plus direction
2 forces in minus direction
D 
C 
A 
B 

## Slide 12
D1
d1
d2
D2
M. Linjama, H.-P. Vihtanen, A. Sipola and M. Vilenius, “Secondary Controlled Multi-Chamber Hydraulic Cylinder,” in The 11th Scandinavian International Conference on Fluid Power, SICFP '09, June 2-4,2009, Linköping , 2009.
LP
HP
Multi chamber cylinder system
Piston areas AA and AC  Force UP
Piston areas AB and AD  Force DOWN
AA:AB:AC:AD  8:4:2:1
4 chambers  16 forces
Two pressure sources
HIGH
LOW

## Slide 13: Force distribution
Test pressures
phigh= 200 bar
plow= 20 bar

## Slide 14: Test environment
Test bench in Tampere University of Technology (2009)
Comparison of systems’ energy losses
a) flow losses in valves, b) flow losses in hoses, and c) compressibility losses. The compressibility losses: energy stored in hydraulic capacitance is lost when the chamber switches from HP to LP

## Slide 15: Multi chamber cylinder (NorrDigiTM)
The system is based on multi-chamber hydraulic cylinders. Also a digital control system is needed. Feedback from the accumulators controls the power utilization on the vehicle and optimizes the performance.
The combination of chambers allows the system to use the smallest possible area to move the load.
16 area combinations in cylinder are available.
Functions can share energy through the common pressure rail  multiple actuators with common accumulators
Excess energy (potential, braking) can be stored in accumulators. The prime mover doesn't need to run continuously (engine-off). It can recover and store energy with up to 80% efficiency (manufacturer’s numbers).
Particularly efficient in applications with high inertia loads, both linear and rotary, such as lowering or braking.
Manufacturer’s numbers: Fuel efficiency improvements by 45-60% and productivity increase by up to 12% were achieved in side-by-side tests with professional operators.
The system is consuming less energy than in the conventional systems. The prime mover (engine or electric motor + battery) can be down-sized.
  For electric vehicles  longer service time between charges.
  Vehicles with engines  engine is running in the “sweet spot” (manufacturer’s terminology), affects both noise and emissions + engine efficiency.
Flow rate is smaller compared with traditional systems. Pumps can be downsized.
Less power losses and heat  hydraulic cooler may be down-sized or eliminated.
http://www.oamk.fi/~eeroko/Opetus/AnturitJaOhjausjarjestelmat/Smart_Vision_NorrHydro_18112010.pdf

## Slide 16: Hydac WS08W-01
2/2 Solenoid Directional Valve
Poppet Type,
Direct-Acting
Normally Closed
SAE-08 Cartridge
250 bar
Energized: approx. 35 ms
De-energized: approx. 50 ms

## Slide 17: Bucher WS22 ON/OFF valve (digital)
Pressure loss
Maximum pressure 350 bar
Excitation voltage 48 V (DC)
Length of over-excitation 4…5 ms (boosting)
Supply voltage 12 V (DC)
Nominal power 15 W @ 12 V (DC)
Switching time 6 … 20 ms (energizing)
5 … 20 ms (de-energizing)
Poppet/Seat (minimum leakage)
Cartridge valve (e.g. M20x1.5)
Solenoid operation boosting
High voltage
Energizing the coil
Low voltage
During holding phase
Current control method
Peak-and-hold
Coil inductance resists the change in coil current. This operation can be accelerated by using temporary high voltages (larger than solenoid’s nominal voltage).

## Slide 18: Variation 1
PARALLEL PUMP-CONTROLLED MULTI-CHAMBER CYLINDER
In this architecture 3 fixed displacement pumps in parallel connection are used to control the velocity of a multi-chamber cylinder piston. The basic principle is to combine
discrete flow supply control of parallel pumps with
discrete effective area control of a multi-chamber cylinder
to produce a speed control resolution for accurate velocity tracking and positioning.
Some throttling is used in the return line to control the system with overrunning loads.
7 discrete flow rates
Bypass function:
Pumps’ flow rates to tank

## Slide 19: Test set-up
Available forces and velocities with 180 bar pressure

## Slide 20: Multi-pressure actuator in enhancing the energy balance of mICRO-excavator
Husnain Ahmed1, Otto Gottberg2, Heikki Kauranne3, Jyrki Kajaste2, Olof Calonius2, Mikko Huova1, Matti Linjama1, Juha Elonen3, Pertti Kahra3, Matti Pietola2
1)Tampere University, Automation and Hydraulic Engineering, Tampere, Finland
2)Aalto University, Mechanical Engineering, Espoo, Finland
3)Fiellberg Oy, Vantaa, Finland
Speaker:
DSc Jyrki Kajaste
1.1 tonne JCB Micro-excavator

## Slide 21: Content of the presentation
Hydraulic systems and excavator used in the study will be introduced
Main interests of the study
Functionality of multi-pressure actuator in excavator application
    Boom inertia can change considerably
      High Inertia (extended boom) versus Low Inertia (folded boom), inertia ratio (10:1)
    Application is Boom swing motion – turning of boom back and forth around vertical axis
      Acceleration – steady velocity: winning of small friction forces - deceleration
Energy efficiency comparison
  Comparison with load-sensing system (LS) based on
    Pressure adjustment valve
    Constant pump
  Analysis of differences in systems
    Origins of power losses

## Slide 22: Multi-Pressure System
Actuator
Multi-Pressure unit
Accumulator
Pressure converters
ON/OFF valves
Pressure relief valves
Pump system
Electric motor
Inverter
Pumps
  2 in parallel
  Pressure relief valve
Low pressure accumulators
  Pressure relief valve
Unloading valve (option)
24 ON/OFF valves, 12 control edges
2
3
4
5
6 pressure levels — for cylinder
HP accumulator  piston / rod
4 pressure converters  piston / rod
LP accumulator  piston / rod
1
6
EPEC 5050
Control unit
42-55 bar
1
6
SYSTEM 1
8 bar

## Slide 23: Operation – short version
Control unit
Controls the valves and operation
Motion controller
Outer loop
Force controller
Inner loop
6 pressure levels available
Controller selects valves (ON/OFF)
Cost function used for valve selection
Hydraulic power from accumulator(s)
High power available
Pump system
Pump(s) used to recharge the HP accumulator (pressostat)
Average power needed (OFFLINE)
1
2
3
4
5
6
EPEC 5050
Control unit
42-55 bar
8 bar

## Slide 24: Load Sensing system, valve-based
Pressure adjustment valve
takes care of 20 bar pressure difference over proportional control valve
Inverter operated
e-motor and pumps
(constant rotational speed during tests)
2
1
1
3
4
4
20 bar
3
During motion excess flow is directed through pressure adjustment valve  remarkable power losses
During actuator standstill flow can be directed through unloading valve  reduces power losses
The pump flow rate could also be adapted to system’s flow need by rotational speed control (to emulate pump controlled LS)  reduces power losses
  This was not done in this case
  It has been simulated  OK
3
2
SYSTEM 2

## Slide 25: Test machine
Micro-excavator
3 pump operated Direct Drive Hydraulics (DDH) systems for other boom functions
Boom
Stick
Bucket
3
3
1
1
1
Multi-Pressure system placed on the back of the cabin
Swing cylinder for turning of the boom
2
2
1.1 tonne JCB Micro-excavator (electric motor operated)
1

## Slide 26: Position control
Low inertia case -1 | High inertia case – 10
DHMPA
system
LS
system
Boom swing - both directions
Can we control the system with changing inertia with simple constant gain P control?
Low and high inertia cases – relative inertia ratio 1/10
Position trajectory command signals
Actual actuator outputs
Constant gain for position control (P control)  OK
Inertia dependent gain  could be even better
Controllability OK

## Slide 27: Multi-pressure system hydraulic variables during swing
High-pressure accumulator pressure
Dual pump flow rate
Boom swing actuator position
DHMPA system in low inertia case
Cylinder piston movement starts
Flow from accumulator, pressure decrease
Pressure reaches lower limit
Pump flow starts, accumulator is charged
Accumulator pressure rises, higher limit
Pump flow stops
Cylinder piston is back in start position
1
2
3
4
5
6
7
p [MPa]
HP
accumulator
qv [l/min]
pump
x [m]
actuator

## Slide 28: Power usage of multi-pressure and LS systems
DHMPA system
LS system
Low inertia case - 1 | High inertia case - 10
DHMPA system
Pump power is needed only when the accumulator is charged
Accumulator(s) provide(s) the high power peaks (HP + LP)
LS system
Pump provides hydraulic power throughout the back and forth movement
Power usage for
Low (folded) - high inertia (extended) boom
Electric motor input
Electric motor output
Pump
Different scales
Motion
Motion
Motion
Motion
1.4 kW
4.5 kW
Charging
Charging
t [s]

## Slide 29: Cumulative energy consumption
Energy type | Low inertia case |  | High inertia case | 
 | DHMPA (kJ) | LS system (kJ) | DHMPA (kJ) | LS system (kJ)
Electric energy | 4.09 | 14.92 | 4.01 | 15.43
Mechanical energy | 3.01 | 12.91 | 2.95 | 13.33
Hydraulic energy | 2.66 | 10.14 | 2.66 | 10.48
Energy
[kJ]
t [s]
With creeping
Motion
Charging Motion Charging Motion
Motion
LS system energy used during motion
DHMPA energy used during accumulator charging
Straight comparison not meaningful because of Pressure Adjustment Valve losses etc. !!

## Slide 30: Origins of energy consumption differences
Function of valves
DHMPA
  Logic valve operation  pressure difference not needed for functionality
  You can have even more parallel valves
  Cartridge valves possible for high flows
LS
  Constant pressure difference (20 bar) for functionality
”Regenerative braking” in DHMPA
  Deceleration is realized by accumulators’ (HP or LP) counter pressures  acceleration
  Potential energy recovery in many cases
DHMPA
2 parallel ON/OFF
LS
Proportional valve
ON/OFF
pvalve
[bar]
N2
Friction
losses
Thermal
losses
Accumulator - Pressure Converter
DHMPA related losses
small
larger (pHP= 55 bar)
LP
8 bar
PRV
REMEDY
Get rid of
PRV!
20% losses OFF
LP  PUMP
HIGH POWER

## Slide 31: Performance comparison?
Power demand (Some of the power lost in pressure adjustment valve!)
  The peak powers for LS were high (acceleration)
  The power can be substantially lower in DHMPA system for
    Electric motor and Pump(s)  these are used OFFLINE
Rough calculations (measured results, including actuator ”work”)
  Energy consumption of DHMPA only 25 - 26% of LS system’s
More analytical version of the results, hydraulic power need during motion
  If hoses & PRVLP included and actuator ”work” excluded, power need DHMPA 30% of LS system’s
  If hoses included and PRVLP & actuator ”work” excluded, power need DHMPA 14% of LS system’s
Observations
  The bucket movement is FAST but the cylinder piston velocity is LOW.
  The hoses are of small diameter (6 mm)!
Different systems
What to compare?
Huova et al. 2017
Comparison of measured energy losses in fast velocity trajectory
2.18 kJ (DHMPA)  9.30 kJ (LS)
Energy consumption ratio 23.4%
Study of Energy Losses in Digital Hydraulic Multi-Pressure Actuator
SICFP’17, Linköping, Sweden
Pressure adjustment valve losses excluded here for LS system

## Slide 32: Conclusions
Two hydraulic systems in boom swing operation of 1.1 tonne JCB Micro excavator were tested
  Digital hydraulic multi-pressure actuator (DMHPA) system, second prototype
  LS system with constant pump and pressure adjustment valve
The controllability of both of the systems was adequate even though boom inertia changes (1:10)
Straight comparison of the energy efficiencies of the systems is not fair (LS system was valve controlled)
  Rough comparison gives 74% savings in energy consumption if DHMPA system is used
More detailed analysis gives conclusions as
The control valve (ON/OFF and proportional) power losses are of another magnitude since
  a) ON/OFF valves are doubled and b) cylinder piston velocity is moderate
  However, in high power applications the DHMPA system’s
    a) Amount of parallel valves can be multiplied or b) cartridge valves can be used instead
The low pressure PRV can be removed (tested) which enhances the energy efficiency
Estimated hydraulic system power consumptions of DHMPA are around 14 – 30% of LS system’s
Final conclusion: “Huge potential with low-cost components”
Large energy efficiency improvements possible!

## Slide 33: Pressurized tank line
Pressure and power losses (p) in PRV
Design ideas
Tested system
Technical challenge in options c) and d)
Both channels (LP and HP) pressurized
How to avoid in
  Gear pumps  shaft seal’s exit
  Piston pumps  high case pressure
Tested
  Special seal in gear pump