## Slide 1: ELEC-E8423 - Smart Grid Demand response in industrial loads
Elina Kauppinen
Aino Summanen
03.03.2020

## Slide 2: Introduction
"Demand response can be defined as the changes in electricity usage by end-use customers from their normal consumption patterns in response to changes in the price of electricity over time."
Demand for more flexibility in power system increases
Industry sector consumes 47 % of all electricity in Finland

## Slide 3: Current situation of demand response
Fingrid coordinates but only fraction of the all potential has been used
Forest industry has a lot of flexible loads already in balancing power markets and fast disturbance reserves

## Slide 4: Increasing need of DR
Variable and distributed renewable energy production increases
Storing methods are more expensive
Notes: vasemman puoleinen: data https://www.irena.org/-/media/Files/IRENA/Agency/Publication/2019/Mar/IRENA_RE_Capacity_Statistics_2019.pdf, tehty excelillä
oikean puoleinen kuva https://www.waaree.com/solar-wind-hybrid-plant.htm Löytyisikö Suomen tiedoilla vastaavaa?

## Slide 5: Principles of Demand Response
Notes: •Why?
oImprove demand & supply matching
oAvoid costly new investments in power plants
oImprove power system reliability
•How?
oAffects demand profile and magnitude
oDifferent time scales (fast-slow)
oAffects power and/or energy

## Slide 6: Potential in industry
In Finland technical potential of DR in industrial sector is 1360 MW (2018) which is 9% of peak load
The focus of demand-side load participation is primarily on the industrial sector due to
  inherently large loads
  existing sensors and metering technologies available
  existing staff of competing plant managers and energy buyers
Industrial processes are integrated systems and thus changing electricity loads may cause harm for the total process
Shutting and restarting of process machinery may result in increased production costs and diminished quality or loss of products
Notes:   grinderies in pulp and paper industry correspond to 6%
  electrolysis, electric arc furnaces and rolling mills in metal industry 2%
  electrolysers, extruders, and compressors in chemical industry 1%
  and mills in cement, lime and gypsum production 0.04%

## Slide 7: Benefits of industrial demand response
Industrial demand response can react to either electricity market price or frequency of electricity network
  The stability of grid is maintained more effectively
  Savings to participants and lower market prices
The high emission production decreases
Avoided infrastructure and storage costs

## Slide 8: Smart grid in demand response
Smart grid helps coordinate demand response and balance grid more easily
-Two-way data transfer
-Automation
-Metering
-Generation and load forecast system

## Slide 9: Conclusions
• Potential of industrial demand response is high but it has not been fully utilized at the moment
• Demand response is limited by the special characteristics of the industrial sector
• Less expensive to adjust a load, than to build a new power plant or energy storage device

## Slide 10: Source material used
Albadi, MH & El-Saadany, EF. 2007. A summary of response in electricity markets. Electric Power Systems Research. V:78. P. 1989-1996. doi:10.1016/j.epsr.2008.04.002
Gelazanskas, Linas & Gamage, Kelum A.A. 2014. Demand side management in smart grid: A review and proposals for future direction. Sustainable cities and society. V.11. P. 22-30. doi: 10.1016/j.scs.2013.11.001.
Official Statistics of Finland (OSF): Energy supply and consumption [e-publication].
ISSN=1799-7976. 4th Quarter 2017, Appendix figure 22. Electricity consumption by sector 2017* . Helsinki: Statistics Finland [referred: 28.2.2020].
Access method: http://www.stat.fi/til/ehk/2017/04/ehk_2017_04_2018-03-28_kuv_022_en.html
Söder, Lennart & et al. 2018. A review of demand side flexibility potential in Northern Europe. Renewable and Sustainable Energy Reviews. V:91. P. 654-664. doi: https://doi.org/10.1016/j.rser.2018.03.104
Fingrid. Demand-side management. Website. [Referred 28.2.2020]. Access: https://www.fingrid.fi/en/electricity-market/market-integration/the-future-of-the-electricity-markets/demand-side-management/.
International Renewable Energy Agency. 2019. Renewable Energy Statistics 2019. [Referred 1.3.2020]. Access: https://www.irena.org/-/media/Files/IRENA/Agency/Publication/2019/Mar/IRENA_RE_Capacity_Statistics_2019.pdf