## Slide 1: ELEC-E8423 - Smart Grid Fuel cells as a part of power system
Filip Österholm & Patrick Nortamo
31.03.2020

## Slide 2: Introduction
The goal of this presentation is to introduce fuel cell technologies and their potential use cases as energy storages in modern power systems.
Fuel Cell - any of a class of devices that convert the chemical energy of a fuel directly into electricity by electrochemical reactions. A fuel cell resembles a battery in many respects, but it can supply electrical energy over a much longer period of time. This is because a fuel cell is continuously supplied with fuel and air (or oxygen) from an external source, whereas a battery contains only a limited amount of fuel material and oxidant that are depleted with use.
https://www.britannica.com/technology/fuel-cell

## Slide 3: What are fuel cells and why are they needed?
High speed and high capacity storage is needed for the grid to function.
07/17-06/20 Fingrid will pay for high capacity reserves to be available:
  Coal, 308+110MW, 18.35+5.50M€
  Gas, 129MW, 6.75M€
  Oil, 160MW, 9.58M€
Fuel cells combine the speed of a battery and last longer, therefore making larger scale operations more economic. While potentially being very environmentally friendly (depends on hydrogen production).
Varying electricity prices make it possible to produce hydrogen at lower cost than before.
Methane gas contains 3.2 times more energy per volume unit than hydrogen.
  https://www.fingrid.fi/kantaverkko/tehoreservi/kaudet/kausi-72017---62020
  http://afdc.energy.gov/files/pdfs/hyd_economy_bossel_eliasson.pdf

## Slide 4: Fuel Cell Technology
Commonly fuel cells use hydrogen gas and oxygen (usually from air) and output water.
The reaction depends on the electrolyte (different polymers or ceramics for different types).
The table shows some examples, where Proton Exchange Membrane (PEMFC) is most used.
Cells can be stacked like batteries to increase maximum voltage and current.
Efficiency is 50-60%
Note the wide range of temperatures needed for the reactions.
Engineering Energy Storage, Odne Stokke Burheim, 2017

## Slide 5: Hydrogen Production
Almost all Hydrogen is produced from steam reforming (methane and water produces carbon monoxide/dioxide and hydrogen gas).
To make use of the fluctuating energy production of renewables an energy efficient and environmentally friendly method should be used. Such as water-, alkaline water-, or PEM-electrolysis.
PEM reverses the reaction in the PEMFC to create Hydrogen and Oxygen and can be sustained with less energy than water electrolysis.
https://www.sciencedirect.com/science/article/pii/S2589299119300035
Method | Advantages | Disadvantages | Efficiency | Cost [$/kg]
Steam Reforming | Developed technology | Produces CO, CO2 | 74–85 | 2.27
Electrolysis | Zero emission, Existing infrastructure, O2 as byproduct | Storage and Transportation problem | 60–80 | 10.30
PEM Electrolysis | Quick Response, High purity of gases (99.99%) | New and partially established, High cost of components, Acidic environment, Low durability | 80-90 | ?

## Slide 6: Current Technology
Hydrogenic’s MW Power Plant
Container sized 1MW plant
PEM fuel cells
20 years lifetime
50% Efficiency
https://www.hydrogenics.com/hydrogen-products-solutions/fuel-cell-power-systems/stationary-stand-by-power/fuel-cell-megawatt-power-generation-platform/

## Slide 7: Coming Technology
Daesan Hydrogen Fuel Cell Power Plant
Located in Seosan, South Korea
Phosphoric Acid (PA) fuel cells
Uses hydrogen from petrochemical industry
Under construction
https://fuelcellsworks.com/news/south-korea-work-begins-on-worlds-largest-hydrogen-fuel-cell-power-plant-commissioned/

## Slide 8: Plans in Finland
In practice, long-term electricity storage, i.e. balancing of production and consumption at the monthly and yearly level, is not possible with battery technology. The most familiar form of long-term storage in the Nordic countries is hydro reservoirs, but additional construction of them is only possible on a limited basis. In the future, long-term energy storage may also be possible by changing electricity into another form, such as synthetic methane (Power-to-Gas, P2G) or hydrogen (Power-to-Hydrogen, P2H). A general name for these technologies is Power-to-X (P2X). A gaseous fuel can be produced from, for example, excess solar and wind power in the summer or during other periods of low consumption and then turned back into electricity in combined generators, gas turbines or fuel cell power plants when demand is high. The use of natural gas in CHP plants or the use of hydro-gen in high-temperature fuel cells also enables heat utilisation. New reports about the construction of industrial-scale (about 100 MW) pilot P2X plants have been published, especially in Germany. P2X is also an alternative in the electrification of many industrial processes, enabling liquid or gaseous fuel to be manufactured with either grid electricity or procured by means of maritime transport or a pipeline.
-Main grid development plan 2019–2030, Fingrid

## Slide 9: Conclusions
Fuel Cells can theoretically be used for both fast and large-scale energy storage.
Requires a lot of infrastructure but could potentially replace oil and natural gas for vehicles and electricity production.
Has been discussed for a long time but is only now starting to grow as a market.
Widespread small-scale use of hydrogen produced from natural gas is environmentally better than widespread small-scale use of natural gas, as the pollution can be collected at the hydrogen production facility.

## Slide 10: Source material used
https://www.britannica.com/technology/fuel-cell
https://www.fingrid.fi/kantaverkko/tehoreservi/kaudet/kausi-72017---62020
http://afdc.energy.gov/files/pdfs/hyd_economy_bossel_eliasson.pdf
Engineering Energy Storage, Odne Stokke Burheim, 2017
https://www.sciencedirect.com/science/article/pii/S2589299119300035
https://www.hydrogenics.com/hydrogen-products-solutions/fuel-cell-power-systems/stationary-stand-by-power/fuel-cell-megawatt-power-generation-platform/
https://fuelcellsworks.com/news/south-korea-work-begins-on-worlds-largest-hydrogen-fuel-cell-power-plant-commissioned/