## Slide 1: ELEC-E8423 - Smart Grid Communication solutions for SG
Jemina Peltola, Petra Raussi
28.04.2020

## Slide 2: Overview
Introduction
SGAM model
Customers experience: generation + consumption
Power system: protection, control, monitoring
Impact
Standards & Protocols
Challenges: opportunities & possibilities
Conclusions

## Slide 3: Introduction
Communication is an essential part of power systems, the “smart” in smart grid stands for the ICT (Information Communication Technology) systems
Traditional power system (today’s grid in figure) used phone and email communication and the information flows were mainly one-directional
Smart Grid
  has bidirectional information, communication and power flows
  enables distributed resources to be remotely accessible and automated operational tasks
Integrating ICT systems to the power system is currently the best techno-economical solution to implement smart grid
Investing Finland, 2016

## Slide 4: SGAM model
CEN-CENELEC-ETSI, Smart Grid Reference Architecture, 2012
SGAM (Smart Grid Architecture Model)
  provides holistic view of the smart grid
  presents complex structures of smart grids in a simplified manner
Two of the five interoperability layers are directly related to ICT systems
  Communication layer
  Information layer
ICT systems spread out to cover all the parts of the smart grid

## Slide 5: Customers experience: generation & consumption
A Survey on Smart Grid Communication Infrastructures: Motivations, Requirements and Challenge
Before smart grid, customers were able to analyze their use of electricity only by the amount of the electricity bill
  Not an accurate source of information
Today the amount of data shared to the customers has grown largely
Smart Grid gives the customers a new and broader way to monitor their own electricity consumption.
  More up-to-date information at different times of the day
  Providing customers proper tools to understand
and optimize their energy consumption
More information about blackouts and other
disruptions of the network
  More improved notification of electricity network
problems
  Accurate information from peak-times
benefits also the supplier

## Slide 6: Power system: protection, control & monitoring
A Survey on Smart Grid Communication Infrastructures: Motivations, Requirements and Challenge
Technology is progressing and thus customers are demanding more accurate, secured and more detailed information of their consumption
  More pressure and requirements for the supplier concerning security and reliability
  Smart grid is expected to provide protection for the data
Customers also rely on the stability of the grid
  When a power system experience an disturbance, protection and control systems online will restore the system back to stable as soon as possible with minimum control efforts
Security of the smart grid network has become
a discussed topic
A safe and controlled network is expected
The development of smart grids lay more and
more on the cyber security of the systems
Easier to disturb the network, since more of
it is connected online
Many companies and organizations working
on developing the smart grid security

## Slide 7: Impact
Krüger, C. (2019). Development and Testing of Resilience Grid Automation using RT simulations. Smart grid laboratory developments - workshop on co-simulation and hardware-in-the-loop, October 28-29, 2019, Trondheim, Norway.
NERC Steering Group. (2004). Technical analysis of the August 14, 2003, blackout: What happened, why, and what did we learn. Report to the NERC Board of Trustees 13
Notes: This figure is showcasing the impact of the ICT (Information Communication Technology) failure on power systems, in the case of 2003 North American blackout. The event 1, 3 and 4 colored in blue are occuring in the ICT system and the rest in the power system. The green colored state for the ICT and power systems is the normal operation and with each of the events happening in both of the systems, the chain leads to blackout. The left side event chain containing only power system events highlights, which events you would know of if you were not monitoring the ICT system connected to the power system. As you can see, in this case in the beginning there are more events in the ICT system, thus without monitoring them, you have a system suddenly shutting down with a blackout, while with monitoring the ICT system maybe in this case it would have been possible to take some actions on the ICT system side to prevent the power system from deteriorating into blackout.

## Slide 8: Standards & Protocols
IEC 61850 - mapping and protocols for substation automation
  MMS (Manufacturing Message Specification)
  GOOSE (Generic Object Oriented Substation Event)
  SMV (Sampled Measured Value)
IEC 62351 - cyber security of power systems data
IEC 60870-5-101/103/104 - SCADA communication
DNP3 - SCADA communication (mainly US)
Modbus TCP/RTU
Profibus
CANbus - batteries, electric vehicles
IEEE 1855 - time synchronization
CIM (Common Information Model)
  IEC 61970 & IEC 61968
  for exchanging information on the electrical network
  applications: energy market, SCADA, energy and distribution distribution management systems
Figure: IEC 61850
http://smartgridstandardsmap.com/
Notes: One of the main standards for smart grids is the IEC 61850, this standard includes mapping (data model) and protocols for substation automation. Originally IEC 61850 was meant to be only a standard for communication between IEDs (Intelligent Electronic Device) in the primary substations. However, new sections are being added to the standard to cover the entire smart grids, for instance new parts include hydro power plants, DER (distributed energy resources), communication between substations and communication between control centers and substations. One of the main reasons why IEC 61850 is expanding to cover the entire smart grid is the design of the standard. In IEC 61850 the data model and communication protocols are separated, thus it is possible to add new component names etc. to the data model, while still being able to apply the principles of the communication protocols. The three main protocols in IEC 61850 are MMS for process and supervision data, GOOSE for fast peer-to-peer communication (e.g. communicating trip signals between IEDs) and SMV for measurement data transfer. In the figure, you can see the generic data model of IEC 61850, each IED is formed by these five categories, e.g. physical device is a IED relay, logical device is the virtual presentation of the physical device (but one physical device can include multiple logical devices). Logical node is a specific group of functions, e.g. XCBR1 for circuit breaker and MMXU1 for measurement unit. Each logical node contains data objects, which contain data attributes, e.g. Pos for position containing StVal for status value, q for quality and t for time, and TotW for total active power containing Mag for magnitude, q for quality and t for time.

## Slide 9: Challenges: opportunities and possibilities
Huge amount of communication protocols being used for different applications in smart grids creating a highly complex ICT system, more work on interoperability needed.
A lot of legacy devices using old communication protocols still exist in the power systems.
Concerns related to cyber security and data privacy because of expanded online network.
Meeting requirements of various emerging models in the grid

## Slide 10: Conclusions
Interoperability is a key element in smart grid and this can be achieved by communications systems.
Interoperability is still a major challenge and extentensive research required.
Lower peak-hour usage to avoid power quality degradation and blackouts
  More stable networks
Possibility of lowering carbon fuel consumption and greenhouse gas emissions
  A global goal

## Slide 11: References
MARKET OPPORTUNITIES IN THESMARTGRIDSECTORIN FINLAND 2016 , https://www.investinfinland.fi/documents/162753/197730/White+Paper+Smart+Grid/880e1f5b-a78f-4294-bfed-a8037cfa0a9c
CEN-CENELEC-ETSI Smart Grid Coordination Group, “CEN-CENELEC-ETSI Smart Grid Coordination Group Smart Grid Reference Architecture”, 2012
R.E. Mackiewicz, “Overview of IEC 61850 and Benefits”, 2006 IEEE PES Power Systems Conference and Exposition, Atlanta, USA, pp. 623– 630. doi: 10.1109/PSCE.2006.296392
D. Baimel, S. Tapuchi and N. Baimel, "Smart grid communication technologies- overview, research challenges and opportunities," 2016 International Symposium on Power Electronics, Electrical Drives, Automation and Motion (SPEEDAM), Anacapri, 2016, pp. 116-120. doi: 10.1109/SPEEDAM.2016.7526014
Brand, M., Babazadeh, D., Lehnhoff, S. & Engel, D. 2019. Trust in control: a trust model for power system network assessment, EPJ Web Conf. 217 01008 (2019), DOI: 10.1051/epjconf/201921701008
Krüger, C. (2019). Development and Testing of Resilience Grid Automation using RT simulations. Smart grid laboratory developments - workshop on co-simulation and hardware-in-the-loop, October 28-29, 2019, Trondheim, Norway.
NERC Steering Group. (2004). Technical analysis of the August 14, 2003, blackout: What happened, why, and what did we learn. Report to the NERC Board of Trustees 13
Smart Grid Standards Map: http://smartgridstandardsmap.com/
Ye Yan, Yi Qian, Hamid Sharif, and David Tipper “A Survey on Smart Grid Communication Infrastructures: Motivations, Requirements and Challenges”: http://d-scholarship-dev.library.pitt.edu/12508/1/Smart_Grid_Infrastructure_Final.pdf