## Slide 1: ELEC-E8423 - Smart Grid Electric vehicles and their charging systems
Branislav Vavrus
Anssi Reinikainen
14.04.2020

## Slide 2: Introduction
Electric vehicles in Finland
In Finland by end of 2019 4661 (2404) fully electric vehicles and 24704 (13095) plug-in hybrids (previous year)
Target by 2030 is to have 250 000 EV's
Charging in Finland
993 (722) public charging stations
Goal is to have 1 public charging spot per 10 EV,s
  Recommendation to have 1:100 ratio on quick charging point per fully electric vehicles currently ratio at 1:17
  Recommendation to have 1:10 ratio on basic charging points per EV, currently at 9,4
Smart Charging
Controlled charging
V2X (Vehicle2Grid/Home/X)
14.04.2020
Sources: [3][9]

## Slide 3: Electric vehicles
Electric vehicles
Nissan Leaf
  40kWh battery up to 270 km range
Tesla model S
  100kWh battery up to 610 km range
Kia e-Niro
  64 kWh battery, up to 370 km range
Lithium-ion batteries
Commercial EVs
HSL has a goal to have at least 30% of its busses electric by 2025
Batteries in a range of 60 kWh to 280 kWh for city use
14.04.2020
Sources: [4][5][7][8]

## Slide 4: Charging modes of EV’s
Modes 1 and 2 use normal household sockets and plugs 10-55 km of range per hour
Modes 3 and 4 mainly for public charging stations 110-1750 km of range per hour
14.04.2020
Modes​ | Usage​ | Power (max)​ | Voltage​ | Charger ​
Mode 1​ | Light vehicles​ | 2 (3,5) kW​ | AC, 1-ph​ | Uncontrolled, normal cable​
Mode 2​ | Slow charging ​ | 7 (11) kW​ | AC, 1 or 3-ph​ | Cable with control unit ​
Mode 3 ​ | Basic charging​ | 22 (43) kW​ | AC, 3-ph​ | Dedicated EV charger socket ​
Mode 4​ | Fast charging​ | 50 (350) kW​ | DC​ | Special power charger​
Sources: [9]

## Slide 5: Charging systems and methods
Plug-in charging
Europe has its own standardized plugs for EV’s
  Slow and basic charging (AC) -> Type 2
  Quick charging (DC) -> CSS Combo
Other types are used for example Japan and US
Pantograph charging
Mainly used in commercial vehicles
HSL busses use this charging method
Wirelesss charging – inductive charging
Used both commercial and private vehicles
Current technologies align with level 2 chargers and can provide power up to 11 kilowatts.
Sources:[7],[11]

## Slide 6: Smart charging vs. uncontrolled charging
Uncontrolled charging – issues with network transmission constraints (thermal, voltage drop, frequency, overload )
Smart charging – basic approach - charging of the EVs is timed to meet the production, flattening the peak of usage of electricity – avoiding congestion
Smart charging – advanced approach – real time energy balancing of power grid
14.04.2020
Sources:[1], [2]

## Slide 7: Smart charging status and prospects
The industry is still evolving and is being studied and piloted
Need for communication protocols and possibly aggregators to utilize this technology to its potential
Problems possibly with user consent to control of their vehicles charging. Ways to incentivize this must be created
Some standardization is already in place IEC 61851
When using V2G technology (managing EV loads – either by customer response to price signals or by automated response to control signals = reacting to the grid or market situation), charging needs to be convenient for customer (based on needs for vehicle) could be solved by gathering big data and using artificial intelligence
14.04.2020
Sources: [3][8][9]

## Slide 8: Conclusions
EVs and their charging stations are gaining popularity partly due to subsidies.
Increasing penetration of EVs in the systems puts a large stress on the grids which could be unbearable if charging is not controlled
Still lot to be done on standardization and aggregating side to get the benefits of smart charging and V2X
14.04.2020

## Slide 9: Source material used
[1] Smart Charging: parked EV batteries can save billions in grid balancing
https://energypost.eu/smart-charging-parked-ev-batteries-can-save-billions-in-grid-balancing/
[2] Anastasiadis, Anestis G. Kondylis, Georgios P. Polyzakis, Apostolos. Vokas, Georgios. (2019). Effects of Increased Electric Vehicles into Distribution Network. Volume 157. pg 586-593.
[3] Teknologiateollisuus. Visited 12.4.2020. Sähköinen liikenne -tilannekatsaus 2019 Q4. [Link]
[4] Nissan. Visited 12.4.2020. https://www.nissan.fi/ajoneuvot/henkiloautot/leaf.html
[5] Tesla. Visited 12.4.2020. https://www.tesla.com/fi_fi/models
[6] Image. Retrieved 12.4.2020 .https://www.electrive.com/wp-content/uploads/2018/04/ovo-energy-nissan-leaf-v2g-charging- station-ladestation-vcharge-uk.png
[7] HSL. Visited 12.4.2020. https://www.hsl.fi/en [Link1][Link2]
[8] Pihlatie, Mikko; Kukkonen, Samu; Halmeaho, Teemu; Karvonen, Veikko; Nylund, Nils-Olof. (2014). Fully Electric City Buses – The Viable Option. IEEE International Electric Vehicle Conference. [Link]
[9] IRENA (2019), Innovation outlook: Smart charging for electric vehicles, International Renewable Energy Agency, Abu Dhabi. ISBN 978-92-9260-124-9. [Link]
[10] Presentation slides, Herranen, Kopilloff:Electric vehicles and their charging systems 2019
[11] Understanding Electric Cars (vehicles) Wireless Charging, their Advantages and Disadvantages
https://nowireneed.com/ev-wireless-charging-working-advantages-and-disadvantages-explained/
14.04.2020