## Slide 1: ELEC-E8423 - Smart Grid Technical solutions in Micro Grids
Einari Näveri
Joonas Järvinen
21.04.2020

## Slide 2: Introduction
SCOPE OF PRESENTATION
Structure of microgrid
Controlling microgrid
Distributed energy resources
Configuration and operating modes
Issues of microgrid concept
Microgrids?
“electricity distribution systems containing loads and distributed energy resources, that can be operated in a controlled, coordinated way either while connected to the main power network or while islanded” [1]
Notes: Why is the microgrid interesting concept?
improved energy efficiency, minimisation of overall energy consumption, reduced environmental impact, improvement of reliability of supply, network operational benefits such as loss reduction, congestion relief, voltage control, security of supply, and more cost-efficient electricity infrastructure replacement

## Slide 3: Structure of Microgrid
Microgrid as a part of the main power grid
Microgrid structure [2]
Notes: In addition microgrid has of course loads
In this case most likely connected to the common AC bus

## Slide 4: Distributed energy resources
Distributed resources (DR) includes multiple small power units which can be generation or storing:
Energy Storage System (ESS)
Balancing power supply and demand, increases stability, power quality
Microgrid small scale storages are mainly different battery technologies due to small size and usability. In households using electrical vehicle as battery and thermal energy storage is also alternative way of DR
Renewable Energy Source (RES)
Wind, solar and micro-hydro production including line converters
Active loads
Controllable load which can increase or decrease the amount of load based production
Distributed generation
Dispatchable within cycles, seconds or minutes: balancing electric system loads and maintaining grid
For example gas turbine plants, small scale CHP, fuel cells and renewables
Interconnection mostly via power electronic inverter

## Slide 5: Controlling technologies in Microgrids
Point of Common Coupling (PCC)
Link that connects the microgrid to the main grid
Static transfer switch (STS)
Switch that allows instantaneous power transfer between microgrid and power grid
Switching time very fast and it it designed to switch back-up power when power source fails
Supervisory Controller (SC)
Monitoring, communication and control system enables demand response and proactive management of microgrid

## Slide 6: Controlling and monitoring microgrids
Communication network
SCADA-system is crucial for controlling and monitoring overall microgrid
Enable demand response with smart meters
Communication network can quickly become very complex as the number of energy resources increase and failure in control system can be fatal
Centralized control vs Local control
Microgrid central controller (MGCC) communicates with lower level controllers
Voltage/frequency droop control of each distributed energy resource controls the power in its connection point
  Control quality overall microgrid might be reduced
Layered control
Primary level: Local control
Secondary level: Communication network
Tertiary level: Model-based control function
21.04.2020

## Slide 7: Configuration and operation modes
Microgrid configurations
Microgrid configuration can be radial, ring, meshed or mixed
  Possibility to reconfigurable grid boundaries makes the system more resilient
Microgrids can be interconnected to multi-MW microgrid
  higher level grid with larger generation and AC-storage connected to substation as single resource
  Enhances resilience and self healing
AC, DC or hybrid
  AC: most current distribution grids, easy conversion to microgrid
  DC: better power quality, no frequency or reactive power control
  Hybrid: best of both worlds? So far limited possibilities
Operation modes
Grid mode: microgrid works as “model citizen” for distribution grid
Island mode: microgrid can work as individual power system
Seamless changing between modes is ideal

## Slide 8: Issues of microgrid concept
How to implement microgrid concept with current distribution components cost efficiently
For fast communication in microgrids standard supported by all components is needed
  For example IEC61850: not yet supported by commercially available microcontrollers
Seamless transition between operation modes is possible but major challenge
Protection
  Current distribution grid protection strategies doesn’t necessary work on microgrids because of bidirectional power flow and small fault currents
Because DER are mainly inverter fed the microgrid can have very low inertia
21.04.2020

## Slide 9: Conclusions
Smart grid and microgrid: The smart grid is a general concept for improving power system and enabling use of smart entities. Microgrid is one tool to put smart grid into effect.
Microgrid concept can be excellent tool for increasing distributed generation and renewable energy sources to power system
Many of the current distribution components can be used in microgrids, but different level of development still needed
Microgrid research has advanced much in recent years but much development is needed to make microgrids commercially viable
21.04.2020

## Slide 10: References
C. Marnay, S. Chatzivasileiadis, C. Abbey, R. Iravani, G. Joos, P. Lombardi, P. Mancarella, J. Appen. (2015). Microgrid Evolution Roadmap. 2015 International Symposium on Smart Electric Distribution Systems and Technologies (EDST)
Issa, Walid & Elkhateb, Ahmad & Anani, Nader & Abusara, Mohammad. (2017). Smooth Mode Transfer in AC Microgrids during Unintentional Islanding. Energy Procedia. 134. 10.1016/j.egypro.2017.09.592.
Kroposki, B ; Lasseter, R ; Ise, T ; Morozumi, S ; Papathanassiou, S ; Hatziargyriou, N. (2008) IEEE Power and Energy Magazine May 2008, Vol.6(3), pp.40-53
Poh Chiang Loh, Ding Li. Yi Kang Chai, F. Blaabjerg. Hybrid AC–DC Microgrids With Energy Storages and Progressive Energy Flow Tuning. IEEE Transactions on Power Electronics ( Volume: 28 , Issue: 4 , April 2013.
A. Hooshyar, R. Iravani. Microgrid protection. Proceedings of the IEEE ( Volume: 105 , Issue: 7 , July 2017 )
IEEE-PES Task Force on Microgrid Control. Trends in microgrid protection. IEEE TRANSACTIONS ON SMART GRID, VOL. 5, NO. 4, JULY 2014
21.04.2020