## Slide 1: ELEC-E8423 - Smart Grid Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
Miro Lehtimäki
Lauri Ikola
03.03.2020

## Slide 2: Introduction
Demand Response (DR)
Energy flexibility in typical homes
DR potential in residential buildings
Benefits for controlling residential loads
Implementation
Conclusion
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses

## Slide 3: Demand Response
In traditional power system adjustments for demand have been made in hydro and condensing power plants
In the future power system adjustments are not economically or technically viable (wind-, solar- and nuclear power)
Demand provides cost-effective alternative to increase flexibility in the power system (DR = Demand Response)
In addition to hourly demand DR provides significant potential for fast reserve in power system
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
Notes: Electricity production must meet consumption.
Economical demand response and Fault demand response.
shifting loads from peak hours to low-demand hours.

## Slide 4: Energy flexibility in typical homes
Loads:
Space Heating, Water Heating
Ventilation
Sauna
Lighting
Home appliances
Home electronics
Energy storage
Electric vehicle
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
Sources:
Renewables: Solar, wind, hydro
Electricity storage (battery)
Electric vehicle

## Slide 5: Energy consumption in typical homes
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
Data:
https://www.vattenfall.fi/energianeuvonta/sahkonkulutus/

## Slide 6: Energy consumption in typical homes
Heating system and source affects the consumption of electrical energy (direct and indirect electrical heating)
Current trend: Building owners are shifting from district heating to geothermal heating systems
In March of 2019 over one million installed heat pumps in Finland
Peaks in electrical energy demand is higher and profile is “sharper”, peak hours in Finland are in winter
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
Source:
https://www.sahkoala.fi/ammattilaiset/uutiset/fi_FI/201119_Miljoona_lampopumppua_myyty/

## Slide 7: Benefits for controlling residential loads and DR potential in residential buildings
Benefits for the grid users
  Inexpensive electricity (5–10 %)
  Overall reliability
Benefits for the grid
  Stabilization and reliability
  Sizing of the grid
  Cost-effective solution
  Lower CO2 emissions from peak power plants
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses

## Slide 8: Control mechanisms and DR potential
Centralized load control (Distributor, aggregator, etc.)
  Peak shaving
  Prevent disturbances
  Stabilization
Independent load control (Markets)
  Flexibility: increase and decrease in consumption
     Storage systems (e.g. heating)
  Long term user profile changes
     Stabilization
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
Notes: Distribution network company
Transmission system operator company
Electricity vendor
Aggregator 3rd party is needed in order to sell extra energy to grid
consumer, based on electricity price
According to HELEN 5-10 percent savings in annual electricity costs.

## Slide 9: Implementation of DR
IoT (Internet of Things)
Centralized control (e.g. Fortum Smartliving)
Home automation systems
Two-way metering and MID certificate
Possibility to follow the energy consumption in 5 minutes intervals
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
Notes: KNX

## Slide 10: Conclusions
Greatest DR potential:
  Heating (Direct electrical heating & sauna, heat pumps)
  Electrical vehicles (DR and storage)
Automation systems
Demand response can also have negative effects to the power system  e.g. Diversity factor
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
Notes: inexpensive electrictymore demand

## Slide 11: Source material used
Residential buildings electricity consumption:
https://www.vattenfall.fi/energianeuvonta/sahkonkulutus/
Heat pump:
https://www.sahkoala.fi/ammattilaiset/uutiset/fi_FI/201119_Miljoona_lampopumppua_myyty/
Järventausta, P., Repo, S., Trygg, P., Rautiainen, A., Mutanen, A., Lummi, K., ... Belonogova, N. (2015). Kysynnän jousto - Suomeen soveltuvat käytännön ratkaisut ja vaikutukset verkkoyhtiöille (DR pooli): Loppuraportti. 2015. Tampere: Tampereen teknilllinen yliopisto. Saatavilla: http://urn.fi/URN:ISBN:978-952-15-3485-0
Fortum SmartLiving:
https://www.fortumsmartliving.com/fi/
Kysyntäjouston hyödyntäminen älykkäässäsähköverkossa:
https://lutpub.lut.fi/bitstream/handle/10024/158776/diplomityo_siponen_tommi.pdf?sequence=1&isAllowed=y
Electrical energy use in residential buildings, flexibility and DR potential of different energy uses