## Slide 1: ELEC-E8423 - Smart Grid
Demand Response in Power System Energy Balance Management
24.03.2020
Samar Fatima
Ishtiaque Panhwar

## Slide 2: Introduction
Motivations for Energy Balance Management:
Stochastic generation and steep generation ramps.
Need of power sink due to demand-generation mismatch.
Development in ICT and climate change perspective.
Ageing assets of electricity infrastructure.
Increased integration of intermittent RES into power system resulting in need for operating reserves.
Frequency regulation issues due to decreased inertia requiring sophisticated planning.
Need for constant real time balance between supply and demand to ensure system stability.
Potential Solutions For Demand –Supply Balance:
Demand Response, Micro-grid and Virtual Power Plants.
This presentation addresses Demand Response for energy management and reliability of the system, main drivers, benefits, challenges and a brief overview of frequency reserves & markets involved in DR .
Notes: DSM: Demand Side Management, DR: Demand Response, IoT: Internet of things, RES: Renewable Energy Sources, ICT: Information and Communication Technology, TSO: Transmission System Operators, FCR: Frequency Containment Reserves, FRR, Frequency Restoration Reserves, RR: Reserve Replacement, a:Automatic, m;manual, N: Normal, D: Disturbance
Inertia of a power system is defined as the ability of a system to oppose changes in frequency due to resistance provided by kinetic energy of rotating masses in individual turbine-generators.
Traditional method to provide balance in power system: Traditional generators for ramping their power up or down as per the grid requirement which in turn depends on the customer demand. However, complexity of this method has been increased due to increased demand, increased prices of fuels and integration of RES. Moreover, frequent ramping has resulted in decreased inertia leading to unstable power system.
Demand Response: DR refers to a change in electric consumption pattern by end-use customers from their normal pattern in response to changes in price of electricity over time, or to incentive payments designed to promote lower electricity use at times of high wholesale market price or when system reliability is jeopardized. Not a new concept and was referred to as two-time tariff previously.

## Slide 3: Demand Response and Load Management
Flattens load curve by shifting some part of loading from peak power period to other time period.
Shiftable loads
Curtailable loads
Interplay between Supply and Demand Side by two way flow of power and information. **
Notes: Shiftable loads can be consumed any time and the total energy consumption is not dependent on the time when it is consumed, which make possible to reduce peak load periods.
Curtailable loads can only be used at certain time. For example, lighting cannot be shifted to another period without sacrificing user's comfort.
**This feature of two way communication between users and supply system is the essential characteristic of Smart Grid enabled through installing smart meters at user’s premises.

## Slide 4: Main Drivers of Demand Response
Demand Flexibility enables the power system energy balance management by increasing the frequency regulation of power system by designing approaches that maximize the efficiency and utilization of controlled loads.
Economic/Market Driven:
To increase Reserve Margin and mitigate price volatility.
Environmental Driven:
Climate change perspective by decreasing energy usage or reduction
of greenhouse gas emissions leading to energy efficiency.
Network Driven:
Decreasing the demand in short period and thereby ensuring
system reliability. Alleviating from grid congestion.
Strategies of Demand Response:
Based on:
Scheduling and control of DR.
Different markets and power balance maintenance process.
Notes: Basic Principles of DR:
Peak Clipping, Valley Filling, Load Shifting, Strategic Conservation, Strategic Load growth and Flexible Load Shape and the purpose of all these methods is to flatten the load curve, balance out the peaks and avoid the burden on power system. The main motivation is the timely shifting of electrical load from high demand and expensive power to lower demand and affordable hours.
Economic/Market Driven:
Increase Reserve Margin and mitigate price volatility by smart term responses to electricity market conditions.

## Slide 5: Frequency Control: Manifestation of Real Power Balance
The Supply-Demand balance is indicated by the frequency of the system that can be compromised due to decreased inertia of power system.
Generation > Consumption, frequency increases
Due to large generation deficiencies, frequency decreases and the rate depends on the stiffness.
Frequency Regulation: Main concern during contingencies and DR scheduling provides system stability.
The ultimate goal is to achieve supply-demand balance at the moment of electricity delivery.
Motivation for Power Balance Management in terms of Frequency Control:
Improvement in economic operation of system.
System reliability due to rapid reaction to disturbances.
Increased system inertia.
Control Strategies For Frequency:
Decentralized
Centralized
Notes: Centralized Strategies offer an increased level of controllability but the required communication system and vast amount of data may burden implementation and operation.
Decentralized Approaches reduce the dependency on information exchange but local frequency measurements may be erroneous and the installation of devices causes its cost.
Motivation for Power Balance Management in terms of Frequency Control:
Improvement in economic operation of system due to replacement of partially loaded generation.
Positive influence on system reliability due to rapid reaction to disturbances.
Increasing system inertia by reacting towards rate of change of frequency.

## Slide 6: Frequency Control and Reserves
Reserves are needed due to:
Increased penetration of RES.
Error prone forecasting of RES.
Power system retailers have to buy power from
balancing power market.
TSO employs certain reserves to balance
the deviations between supply and demand.
Demand response reserves and balancing markets are
mainly used for the maintaining hourly power balance.
Combination of synchronised and standing
reserves increase system reliability.
Demand Side Management acts as standing reserve and improves system performance.
System frequency is the direct measure of the balance between generation & system demand at any instant.
Notes: DSM acts as standing reserve and improves system performance by increasing the amount of wind power that can be absorbed as fewer generating units are scheduled to operate, which is particularly relevant when high wind conditions coincide with low demand.
Reserves are power plants and consumption resources which either increase or decrease their electric power according to the need of the power system.
Necessity of Reserves:
Due to
Increased penetration of RES.
Deviations in forecast despite full planning regarding consumption and production profiles.
Power system retailers have to buy power from balancing power market to meet demands due to error prone forecasting of RES.
TSO employs certain reserves to balance these deviations. Demand response reserves and balancing markets are mainly used for the maintaining hourly power balance.
Combination of synchronised and standing reserves increase system reliability.

## Slide 7: Grid Imbalance and Reserves
Frequency control can be classified as
Frequency Containment:
Stabilizes the system frequency.
FCR-N and FCR-D.
Primary frequency control.
Frequency Restoration:
Activation of FRR to restore the system
frequency to its nominal value (50 Hz).
Control of the reserves is centralized.
Secondary and tertiary controls.
Fast response market rely on demand response for being able to switch the devices on and off to provide fast response (few milli seconds) to stop the frequency deviation.
Notes: A general pattern of grid imbalance and activation of reserves:
The grid imbalance and balancing markets are closely interlinked and different stages of the deployment of these reserves is explained as follows.
As soon as the grid imbalance occurs, the TSOs first prioritize to avoid any further deviation is frequency and this is done using FCR. The task of FCR is to makes changes in load or production thus stabilising the system frequency. After this FCR activation, the TSO focus to free the capacity of FCR to be used in case of other imbalance situation. It is accomplished by replacing FCR by aFRR that restore frequency to its nominal value. Of 50 Hz. mFRR is activated in case of very large system imbalance. RR capacity is employed some times by TSO to free up the mFRR capacity and finally financial settlement is done for the final electricity price.
Frequency control can be classified as
Frequency containment: Stabilizes the system frequency after a disturbance as well as reacts to natural and minor frequency variations.
FCR-N and FCR-D
Primary frequency control due to their first reaction to frequency variations.
Frequency Restoration:
Activating FRR to restore the system frequency to its nominal value.
Control of the reserves is centralized and it is either automatic or manual.
Secondary and tertiary controls.
Fast response market rely on demand response for being able to switch the devices on and off to provide fast response (few milli seconds) to stop the frequency deviation. This enables to come online and ranking the mechanisms that the transmission operators have available with them to keep the power system in balance.

## Slide 8: Indispensable Physical DR For Grid Stability
Market DR: Real-time pricing, price signals and incentives
Depends on market places where prices are formed and products are traded.
Due to slow response of these markets, mostly transactions are done on a day ahead market.
Physical DR is necessary because grid congestion and excess generation leads towards the fact that grid relief cannot be achieved via market prices alone.
Physical DR: Grid management and emergency signals
Binding requests for demand management when supply system or its infrastructure are in a reduced performance due to maintenance or failure. [Or when system reliability is jeopardized]
An interconnection of Market and physical DR is necessary for the optimal performance of supply system in terms of Energy Balance Management.
Spinning Reserves in DSM enables that load on the demand side can be reduced or increased when the grid frequency drops or rises.

## Slide 9: Benefits & Challenges
Benefits:
It resolves the voltage-constrained power transfer problems.
Relieves from grid congestion and enables integration of RES into existing system
without loading the system and thereby deferring new network investment. **
Reduce Carbon Footprint due to penetration of RES.
Challenges:
Lack of ICT infrastructure and complexity in operations.
Inappropriate market structure.
Disturb natural Diversity of loads.
Implementation of real-time power generation and forecasting methods.
Privacy issues emerging from management of consumers’ metering data.
Smart Grid; A Solution towards Challenges
Implementation of a secured communication infrastructure of the Smart Grid.
Notes: Lack of ICT infrastructure: Advanced metering, communications, control & automation methods and IOT are largely absent from existing electricity systems. The power system needs upgrading to deploy such solutions for grid reliability as the technologies do not replace technologies rather systems replace systems.
** (This statement is objective as sometimes the systems are not well equipped with advanced technologies to house the RES to practice DR. This is because of the fact that there are physical limits, thermal and stability, and the transmission grids were not originally designed for a liberalised market, where anyone can order power from anywhere. Moreover, integration of RES is subject to the availability of appropriate design and control technologies to incorporate the RES without risking system reliability. )
Challenges in Implementation of real-time power generation and forecasting methods for the utility to schedule the consumer demands.
Diversity Factor: is the ratio of the sum of the individual maximum (peak) demands of the various subdivisions of the system to the maximum(peak) demand of the whole system.
Smart Grid as a solution to the challenges:
Implementation of a secured communication infrastructure for the smart grid is indispensable that mitigates cyber security issues.

## Slide 10: Conclusions
Demand Response efficiently lower the prices, reduce price volatility, optimize the grid performance and aids integration of RES.
Future power markets managing the distributed generation potential largely depend on the demand/production forecast accuracy to guarantee the operational safety of the power system that is prone to intermittent demands and production patterns.
Frequency regulation is the main aspect for determining the stability of the system and DR improves the system reliability through frequency control and by relieving transmission network congestion.

## Slide 11: References
1: Albadi, Mohammed & El-Saadany, Ehab. (2008). A summary of demand response in electricity markets. Electric Power Systems Research. 78. 1989-1996. 10.1016/j.epsr.2008.04.002.
2: Aghaei, J. & Alizadeh, Mohammad Iman. (2013). Demand response in smart electricity grids equipped with renewable energy sources: A review. Renewable and Sustainable Energy Reviews. 18. 64-72. 10.1016/j.rser.2012.09.019.
3: Soares, João & Fotouhi Ghazvini, Mohammad Ali & Borges, Nuno & Vale, Zita. (2016). A stochastic model for energy resources management considering demand response in smart grids. Electric Power Systems Research. 143. 10.1016/j.epsr.2016.10.056.
4: R. Deng, Z. Yang, M. Chow and J. Chen, "A Survey on Demand Response in Smart Grids: Mathematical Models and Approaches," in IEEE Transactions on Industrial Informatics, vol. 11, no. 3, pp. 570-582, June 2015.
5: M. Ghorbanian, S. H. Dolatabadi, M. Masjedi and P. Siano, "Communication in Smart Grids: A Comprehensive Review on the Existing and Future Communication and Information Infrastructures," in IEEE Systems Journal, vol. 13, no. 4, pp. 4001-4014, Dec. 2019.
6: J. S. Vardakas, N. Zorba and C. V. Verikoukis, "A Survey on Demand Response Programs in Smart Grids: Pricing Methods and Optimization Algorithms," in IEEE Communications Surveys & Tutorials, vol. 17, no. 1, pp. 152-178, Firstquarter 2015.
7: P. Palensky and D. Dietrich, "Demand Side Management: Demand Response, Intelligent Energy Systems, and Smart Loads," in IEEE Transactions on Industrial Informatics, vol. 7, no. 3, pp. 381-388, Aug. 2011.
8: Derakhshan, Ghasem & Shayanfar, Heidarali & Kazemi, Ahad. (2016). The optimization of demand response programs in smart grids. Energy Policy. 94. 295-306. 10.1016/j.enpol.2016.04.009.
9: Power Engineering: Advances and Challenges By Matti Lehtonen, Chapter 17. Demand response.
10: Harnessing Demand Response for Power System Flexibility - Residential Heating and Thermostatically Controlled Loads, Antti Alahäivälä, 2017
11: Power Systems Lecture on Frequency Control of Power System by Matti Lehtonen