## Slide 1: ELEC-E8423 - Smart Grid Smart Meters and their Security Issues
Julia Dippmann and Linus Erbshäuser
28.04.2020

## Slide 2: Introduction
Smart Meter functionality, standards and components
Cyber Security Issues in Smart Meter
Solutions for three categories of cyber attacks
Current implementation in Finland and Europe

## Slide 3: 1. Smart meter technology
Supervisory control
and data acquisition
(SCADA)
SM Components:
network interface
sensors Analog front End (AFE: converts analog into digital data)
Microcontroller Unit (MCU: control inputs and outputs, saves logs of important meter activities)
memory component
LCD component
Advanced Metering Infrastructure (AMI)
→ Smart Meter SM
Production
Consumption & Storages
Two-Way Communication (Wifi/ Radio frequency)
Two types of smart meter: ANSI IEC
communication protocols and standards

## Slide 4: 2. Cyber Security Issues in Smart Meter
Purpose of attacks:
Manipulate/block/steal data transfer between SM and utility company (for health insurance companies, landlords, criminals)
Gain control over certain devices
Affect real-time consumption: manipulating the meter readings
Threaten information privacy Possible consequences  shutting down the entire grid, shutting down servers, damaging network components
 Three categories of security issues: attack on network, attacks on physical hardware, attack on data
→ Network communication as most vulnerable aspect

## Slide 5
Mitigations for attacks on network:
Encryption
Firewall
Secure protocols: IPSec (Internet Protocol Security) SSL (Secure Socket Layer), TLS (Transport Layer Security) SSH (Secure Shell)
User access control mechanisms
Digital signature
Trusted platform
Secure physical locations
Router throttling
3. Solutions for cyber attacks

## Slide 6
  Mitigations for attacks on physical hardware:
  Use of location-based keys and employing a cryptographic related method
  Defend the meter electronics from electromagnetic charges: ferrite beads, capacitor line filters, physically large SMD resistors
  Locked registers for real time clock (RTC)
  Embedded anomaly detection model (clustering-based anomaly detection algorithm)
  Mitigations for attacks on data:
  Protect personal important data by limiting access, data checking technique based on holomorphic encryption, Shamir Secret Sharing (SSS)
  Using multiple keys to encrypt the data
  Monitor power signatures using sophisticated algorithms for Non-Intrusive Load Monitoring (NILM) while batteries charge and discharge
3. Solutions for cyber attacks

## Slide 7
  By 2020, almost 72% of European consumers will have a smart meter for electricity
  In Finland is the smart meter penetration close to 100% (over 97%) after the government mandated a SM roll-out for 80% until 2014
  One of the leading EU countries regarding implementing SM technologies
  Benefits for costumers and distribution system operator could be seen, especially the possibility for remote reading and possibility for hourly pricing
  Data protection impact assessment DPIA gives since 2018 a template for smart grid security in EU countries without legal obligation
4. Current implementation in Finland and Europe

## Slide 8: Conclusions
Security can never be 100% garanted only be mitigated
SM as an entrance gate: A secured smart meter leads to a secured smart grid
All three subsections (attack on network, physical hardware and data) have to be evenly secured for a secured smart grid system

## Slide 9: Source material used
Halim, Yussof & Rusli. (2018). Cyber Security Issues in Smart Meter and Their Solutions; IJCSNS International Journal of Computer Science and Network Security. VOL.18 No.3. Link
Khattak, Asad & Khanji, Salam & Khan, Wajahat. (2019). Smart Meter Security: Vulnerabilities, Threat Impacts, and Countermeasures. 10.1007/978-3-030-19063-7_44.
EUR-Lex. Commission Staff Working Document. Country fiches for electricity smart metering. Link
Joint Research Centre (2020). Smart Electricity Systems and Interoperability. Link
European Commission. Data protection impact assessment for smart grid and smart metering environment. Link