## Slide 1: ELEC-E8423 - Smart Grid Power markets in Nordic Countries: Frequency containment and frequency restoration reserves
Taavi Leikola and Alex Tolonen
3.3.2020

## Slide 2: Introduction
Electricity market structure in Nordic countries
Challenges of balancing markets
Types of frequency reserves

## Slide 3: Electricity market structure in Nordic countries
Notes: This is the basic structure of the Nordic electricity market. Different countries have their own transmission system operators (TSOs). Fingrid controls the finnish transmission system.
The day-ahead and intra-day markets provide a platform for matching consumption and production, by connecting the producers and consumers through hourly pricing for capacity. However, the production and consumption will never match perfectly, thus there is need for balancing small fluctuations and disturbances. Today we will focus on the reserve markets, which comprises of different frequency containment and restoration services.

## Slide 4: Challenges of maintaining frequency quality
Production should match consumption
  Frequency 50±0.1 Hz
  Containment and restoration reserves
Increased undpredictable power generation
  Increased demand for flexibility
  Reduced inertia
Frequency adequacy
  Enough energy but not enough power
Notes: The Nordic electricity frequency is set constant at 50 Hz. There are two ways to maintain the frequency balance. These are containment and restoration reserves. The increasing share of renewables like wind and solar power result in more volatile production and more deviation in the frequency. This is because they do not add inertia to the system like traditional condensing plants with heavy rotating machinery as turbines and generators.
As you can see from the diagram, the annual frequency deviations have risen signifantly in the past years.
As more intermittent renewables are intorduced to the system, the amount of total energy might stay constant but the power demand cannot always be met. Also the unpredictbility of the electricity production will create forecast errors, leading to a bigger need of reserves.

## Slide 5: Nordic frequency reserves
Notes: The nordic frequency reserves can be subcategorized into five catecories by their functions and properties. FCR-N is used constantly to balance constant minor fluctuations in the grid. aFFR is activated automatically during sertain hours in the day during demand peaks. FCR-D acts when there is an interruption in production and the frequency drops suddenly. The reaction for the disturbances has to fast because major frequency deviations may result in broken components or even lead to a major power outage. If necessary there is also a manual restoration reserve, which can be used when required. A new type of fast frequency reserve will be introduced later this year.
Fingrid maintains and develops the marketplaces for reserve and balancing power. Producers can offer their capacity at the reserve markets for a certain price. By activating these bids Fingrid maintains the frequency.

## Slide 6: Nordic frequency reserves
FCR-N
  Aims to enhance the quality of grid in case of variations
  Constantly in use to balance small fluctuations ± 0.1 Hz
FCR-D
  Large frequency deviations, eg. loss of production
  Activation at 49,90 Hz, Full capacity at 49,50 Hz
FFR-A
  Automatic operation activation by Fingrid’s signals
  Purchases capacity usually in the morning and evening demand peaks
FFR-M
  Manual operation
  Participants bid on adjustable capacity when required by Fingrid
Notes: This diagram demostrates the use of frequency reserves
FCR-N is constantly in use.
FCR-D activates linearly in larger frequency deviations. It activates drops more that 0.1 Hz and reaches full capacity at 49,50 Hz.
The aFFR reserve is procured in the hourly market and from other Nordic countries. It is only procured for certain morning or evening hours which are informed in advance. The activation demand is known beforehand.
The Nordic TSOs have agreed that each countries Fast Disturbance Reserve must be able to substitute their own dimensioning fault in the network. For example the loss of a major connection or power plant. In Finland the reserve varies typically between 900 – 1100 MW. These reserve power plants are not in use in electricity market.

## Slide 7: FFR – Fast Frequency Reserve
Newest reserve type
Used to balance frequency due to low inertia levels
Inertia refers to the kinetic energy stored in the rotating masses in the electricity system to resist changes in frequency
Increased share of renewables with low inertia has created demand for FFR
FFR will be implemented in the Nordics in May 2020
Frequency response after a generator trip with high and low inertia
Notes: It has been concluded that underfrequency situations are much more critical than overfrequency situations. Therefore, FFR is defined only for underfrequency situations but only when the system’s inertia is low.
Currently low inertia situations are handled by lowering the power of large production units as precausausion.
FFR is activated under a second, when there is a large frequency deviation and low inertia. The maximum capacity of this reserve is estimated to be from 250 to 300 MW.
Inertia is low and the demand for FFR is typically highest on weekends from spring to autumn i.e when the demand for energy is low.
FFR reserve market will be similar to FCR-D but to participate in FFR market, the provider has to pass certain required qualities, including activation and reactivation speeds.

## Slide 8: Conclusions
The reserve markets are the utilized to match production to consumption
Sufficient frequency reserves are essential to handle variations in the power system
Increased share of renewables requires more flexibility

## Slide 9: Source material used
https://www.fingrid.fi/globalassets/dokumentit/fi/ajankohtaista-tapahtumat/reservipaiva-2019/reservipaiva-2019---uusi-nopea-taajuusreservi-ffr-id-181280.pdf
https://mycourses.aalto.fi/pluginfile.php/1122522/mod_folder/content/0/FingridPresentation260919.pdf?forcedownload=1
https://www.fingrid.fi/globalassets/dokumentit/en/electricity-market/reserves/fast-frequency-reserve-solution-to-the-nordic-inertia-challenge.pdf
https://www.fingrid.fi/globalassets/dokumentit/en/electricity-market/reserves/reserve-products-and-reserve-market-places.pdf