## Slide 1: ELEC-E8423 - Smart Grid Power markets in Nordic Countries: Day ahead market and intra-day balancing
Mikael Väisänen, Annmarie Oksa
05.03.2019

## Slide 2: Introduction
Nordic electricity market is managed by Nord pool and consist of seven countries.
Main electricity generators are hydropower, nuclear power and wind power.
Market operates on day ahead market and intra-day balancing.

## Slide 3: Day ahead market- Elspot
It is the main arena for trading power. Where, contracts are made between seller and buyer for delivery of power the following day
A consumer evaluates its energy need and price for the following day, hour by hour
Generator decides its deliver energy capacity and cost rate hourly
Each order includes the exact electricity volume (MWh/h) at a specific price rate (€/MWh) for every hour in the next day that one is prepared to buy or sell
The whole sale price of electricity (selling price) equilibrium settles where the curves of supply and demand intersect.
Spot-trade is the day before delivery where, offers are given up to 12-36 hours before delivery. The trade for next day closes at noon.
whole sale price
Notes: Electricity producers
Electricity traders
Electricity retailers
Transmission system operators
Consumers
Energy-intensive industry

## Slide 4: Merit order curve
Marginal cost
The cost to produce a unit of electric energy: fuel and variable O&M costs
Profit
Profit=o
whole sale price
Higher cost generators are not used and must wait when demand is higher or the production of e.g. wind power is lower
Economic dispatch
The system operator (an operator that transmits electrical power from generators over the electrical grid) meets the forecasted demand by dispatching generators based on their selling price for electricity, with the lowest cost generators being dispatch first, followed by higher and higher cost generators
Notes: Also a lot of 0 price bids in chp, nuclear, wind solar
Low prices but some high peaks
Effect of renewables – also in elbas
Negative prices – first time in Finland – In Germany 23/24
As a result some condensing plants shutdown and the investors tend to invest less in such plants which will greatly affect the security of the grid which will be dominated by the intermittent and volatile renewable sources

## Slide 5: Transmission
There is a limit to how much power a transmission line can carry, and when that limit is reached, the line is said to be congested.
At these times, generation closer to the given load needs to be dispatched even if it is higher cost.
So transmission congestion forces system operators to dispatch generation not just for the entire grid, but also at areas within the grid in order to meet local demand that cannot be brought in from elsewhere.
Notes: Finland has good transimission grid, so far only one price are – future?
The need for better transmission and larger transmission capacities increases.

## Slide 6: Prices in the same hour 28.02.2020 9-10

## Slide 7: Intraday market- Elbas
Continuous market, with trading taking place until 1h before delivery  Balances the supply and demand.
Increasing interest in intraday market due to volatile renewables.
Reduces the need for reserves and associated costs like penalties.
Prices are set based on a first-come, first-served principle, where best prices come first.

## Slide 8
Kuva intraday marketsista?

## Slide 9: Conclusions
Electricity systems in Nordic Countries are interconnected.
The Nordic Power markets operate mostly in day ahead spot market (ELSPOT) that determines the price by balancing supply and demand
Errors in the day ahead market can be compensated in intra-day balancing (ELBAS) increased interest.

## Slide 10: Source material used
Sanna Syri. Energy Markets.Lecture 5. Nordic Electricity Markets.2019.
https://aleasoft.com/european-electricity-markets-panorama-nordic-countries/. Accessed: 19.2.2020.
https://www.nordpoolgroup.com/the-power-market/Intraday-market/. Accessed: 19.2.2020.
Anders Skajaa, Kristian Edlund, and Juan M. Morales, Member. Intraday Trading of Wind Energy. IEEE. (2015). https://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=7005520.

## Slide 11
Thank you