## Slide 1: ELEC-E8423 - Smart Grid Methods for fault location and detection in Smart Grids
Markus Kivisaari
Joakim Lyyski
27.04.2020

## Slide 2: Introduction
Detecting and isolating a fault in grid operations requires a measurement system, protective equipment and a control system
In smart grids, the power flow is bidirectional which makes the fault location more complex compared to conventional grids
  Measuring and protection equipment designed for conventional grids are not sufficient to operate in all fault scenarios
  Data collection from measurement units and control of protective equipment need to be accurate and fast
Multiple methods can be utilized in fault detection
  Highly dependent on grid infrastructure and system design

## Slide 3: Fault detection and response in grid operation
https://www.google.com/url?sa=i&rct=j&q=&esrc=s&source=imgres&cd=&ved=2ahUKEwii-NKToIjpAhVkl4sKHVumDPIQjRx6BAgBEAQ&url=https%3A%2F%2Fwww.gegridsolutions.com%2Fmultilin%2Fsmartgrid_innovations.htm&psig=AOvVaw27MpTDfl_uoPiA8llOODEg&ust=1588064698880172

## Slide 4: Monitoring of grid operation
Fault detection and protection systems are required in every section of the grid
Measurement units
  Phasor Measurement Units (PMU)
  Power Quality Analyzers (PQA)
  Advanced Metering Infrastructure (AMI)
Operators
  Power plants
  Transmission line operator
  Distribution grid operator
  Consumer/Prosumer
Smart Grids contain large amount of distributed generation
  Increased demand for accurate monitoring data at distribution level
Data collection and handling infrastructure required for reliable operation
https://s3-us-west-2.amazonaws.com/courses-images/wp-content/uploads/sites/3960/2019/01/14192751/graphics4.jpg

## Slide 5: Fault location methods in Smart grids
A fault causes a sudden change in transmission line or grid section
  Changes in impedance, voltage, current or transients can be picked up by measurement system -> multiple detection methods available for grid operators
Impedance based fault location methods [1]
  Compares the voltage, current and impedance to identify the fault distance
Voltage or current phasor measurement methods [3]
Computer algorithm or machine learning analyzation of monitoring data [2][3]
  Examples: IED & DFPI, MPD
  New algorithm analyzation methods expected to be essential in Smart grid fault prediction and detection
  Accurate monitoring data required (sensor network, data infrastructure)

## Slide 6: Fault location by using IED & DFPI [1]
DFPI = Directional Fault Passage Indicators
IED = Intelligent Electronic Devices
ANSI 21 FL = Impedance based fault location method
Method uses DFPI’s with advanced fault location algorithm to estimate the location of the phase and earth faults
Fault locator brick
  identifies faulty section of the network
Distance brick
  detects at which distance is the fault in the faulty section
Flow diagram of the advanced fault location algorithm [1]

## Slide 7: Fault detection based on MPD [2]
FDR = Frequency Disturbance Recorder
MPD = Matching Pursuit Decomposition algorithm
  Extracts the time-frequency features from the voltage and frequency signals
HMM = Hidden Markov Model
  Fault detection and identification
Fault detection and identification by using frequency signals
  Frequency signals are closely related to power balance variations
  Effective way to analyze power system faults
Fault location by using voltage signals
  Voltage and current variations can indicate the fault position.
Data processing flowchart [2]

## Slide 8: Distributed fault detection with wireless sensors
Wireless sensors (WSN) distributed along the grid section [4]
Collected data analyzed with computer algorithms/machine learning
  Data transfer efficiency is a critical factor
Real-time monitoring enables fast and accurate response
Requires a significant sensor infrastructure investment
https://www.mdpi.com/1424-8220/17/5/983, [4] (page 3)

## Slide 9: Conclusions
Smart grids contain distributed generation, and therefore detection of faults becomes more complex
Accurate real-time data collection infrastructure holds a significant role in Smart grid operation
Computer algorithms and machine learning analyzation of monitoring data is essential in the future of Smart grid fault prevention and detection

## Slide 10: Source material used
[1] Silos-Sanchez, A., Villafafila-Robles, R. & Lloret-Gallego, P. 2020, "Novel fault location algorithm for meshed distribution networks with DERs", Electric Power Systems Research, vol. 181.
[2] Jiang, H., Zhang, J.J., Gao, W. & Wu, Z. 2014, "Fault detection, identification, and location in smart grid based on data-driven computational methods", IEEE Transactions on Smart Grid, vol. 5, no. 6, pp. 2947-2956.
[3] Andresen, C.A., Torsaeter, B.N., Haugdal, H. & Uhlen, K. 2018, "Fault Detection and Prediction in Smart Grids", 9th IEEE International Workshop on Applied Measurements for Power Systems, AMPS 2018 - Proceedings.
[4] Sujie Shao, Shaoyong Guo and Xuesong Qiu. 2017, “Distributed Fault Detection Based on Credibility and Cooperation for WSNs in Smart Grids”, Article