## Slide 1: ELEC-E8423 - Smart Grid Power and Energy Balance Management in Micro Grids
Markus Kolehmainen & Patrik Pykälä-aho
23.03.2020

## Slide 2: Introduction
Microgrid may be defined as a system capable of islanded operation consisting of distributed energy resources operating along energy storages.
A microgrid can be operated either on islanded mode or connected to the utility grid.
The generation in future microgrids relies on renewables, mainly wind and solar, and possibly fuel cell or motor-based backup generation units.
The challenge is to preserve power and energy of the system in balance while keeping the cost of the system economically viable.
https://strategicmicrogrid.com/about-microgrids/

## Slide 3: Components of a microgrid
Renewable power sources
  Generate power according to the weather
Energy storages
  Mainly batteries, used for power balancing (frecuency, voltage)
Utility grid connection
  Provides backup most of the time
Backup power sources
  Used for the power and energy balancing by generating power for
  residual loads
Customer loads
  An intelligent system can provide significant demand response (DR) by controlling the loads of e.g. residential heating/cooling and EVs
  DR can be used for system balancing or hedging against price spikes
  User comfort sets limits for DR potential e.g. limits for indoor tempetature
  Some loads are critical and can’t participate in DR e. g. lightning
Primary components
Backup. The more economical or currently available is used

## Slide 4: Island and utilility grid connected modes
A microgrid can be operated conventionally as a radial section of larger distribution network or as a separate island.
The island mode capability provides increased reliability as microgrid stays functional even if the utility grid has black out.
Utility grid connection is beneficial as it decreases the need to operate the generally more expensive backup generators.
Operation of utility grid connected microgrid is optimized considering price of electricity bought and sold to the utility grid.
In connected mode, batteries can be used for energy arbitrage to make profit for microgrid

## Slide 5: Power and Energy Balance Management
Variable renewable generation can't be used for power and energy balance management.
Power balance management time scale spans from milliseconds to minutes.
In microgrids, power quality is managed with converters connected to energy sources, batteries and often also with the connection to the external grid.
Energy balance management time scale spans from hours to longer periods.
Over longer periods, energy balance is managed with utility grid connection or backup generation.
Batteries are too expensive for large scale energy storing over longer periods.
https://www.researchgate.net/figure/Grid-power-control-issue-and-energy-management-timeframes_fig6_265907090

## Slide 6: Demand response
Energy system, for which the main source of energy is wind and solar power, has major volatility in electricity production.
Demand response may significantly reduce the need for often more expensive and polluting backup power generation.
Loads applicable for demand response are for example electric space and water heating, electric vehicles and energy storages.
Demand response enables larger share of intermittent renewable generation and thus decreases system emissions
https://energycentral.com/c/em/key-demand-response-proper-customer-engagement

## Slide 7: Energy storages
Batteries
Batteries are one of the primary components in renewable-based microgrids when considering the power balance.
They are operated based on production and demand predictions. Batteries can also be used to cope with prediction errors.
Batteries provide immediate response to the electricity network as a power imbalance is detected. They maintain the power quality in a microgrid.
Only batteries and external grid connection can provide nearly immediate response to power balance shifts.
For this reason they are often used in conjunction with e.g. fuel cell systems and diesel generators that have slower response time.
Thermal storages
Thermal storage can be used as a longer term energy storage to which excess renewable production can be dumped.
Thermal energy storages are approximately 1000 times less expensive compared to current commercial battery technologies

## Slide 8: Lemene
A concrete example of microgrid is the Lemene demo project driven by Lempäälän energia Oy.
The plan is to implement a microgrid that has 4MW of installed solar, 8.1MW of installed gas motors, two 65kW fuel cell units and a BESS.
The fuel cells provide baseload and gas motors provide more flexible production capacity for contingency and island mode situations, or if the electricity market price is high.
Battery
Gas motor
Gas
Fuel cell
Solar PV plant
Utility grid
Chiller
Customer

## Slide 9: Benefits
Customers of a microgrid capable of island mode operation can avoid contingencies in distribution network.
Microgrid capable of island and grid connected operation has very high security of supply.
A more localized approach to energy system management divides the entirety into many more easily manageable subsystems.
The challenges introduced by distributed generation e.g. voltage rise, can be more efficiently managed by a local aggregator.
Short distribution distances increase energy efficiency.
Distributed generation can reduce need for expensive transmission lines. The distance between production and consumption decreases.
Microgrids can provide flexibility to the external energy system operating as a virtual power plant.

## Slide 10: Challenges
  Economics of scale benefits centralized generation
  Cost of electricity storages is still relatively high
  Space and water heating forms largest demand response potential, however district heating is mostly used in urban areas in Finland
  Operability in island mode requires full back up capacity, which means that the backup generation capacity must cover the maximum power demand of the microgrid. For most time of the year, the capacity is massively overdimensioned.
  Managing the microgrid relies on predicting the renewable energy production, demand and hence the electricity prices. The uncertainties of these factors create challenges considering the optimal system management.

## Slide 11: Conclusions
Power quality and energy management in microgrids is handled by an aggregator that controls energy storages and, to some extent, loads of the customers.
Not economically viable to have microgrids operating in island mode except during contingencies. Otherwise microgrid can be considered as a prosumer system that attempts to optimize its energy flows in most economical way.
Increasing amount of distributed renewable energy requires intelligent management system and flexibility to cope with uncertain nature of renewable energy production. Microgrids enable efficient and flexible locally optimized solutions.

## Slide 12: Source material used
A. A. Bashir, M. Pourakbari-Kasmaei, J. Contreras, M. Lehtonen, A novel energy scheduling framework for reliable and economic operation of islanded and grid-connected microgrids,
Electric Power Systems Research, Volume 171, 2019, pp. 85-96, ISSN 0378-7796, DOI: 10.1016/j.epsr.2019.02.010.
R. H. Lasseter and P. Paigi, Microgrid: a conceptual solution, 2004 IEEE 35th Annual Power Electronics Specialists Conference (IEEE Cat. No.04CH37551), Aachen, Germany, 2004, pp. 4285-4290 Vol.6.
DOI: 10.1109/PESC.2004.1354758
Lempäälän energia, Available from: http://www.lempaalanenergia.fi/content/fi/1/20149/Hanke-esittely.html