## Slide 1: ELEC-E8423 - Smart Grid Topic 46- Sector Coupling of Power and Heat
Hassan Sayed Ahmed
Mikko Hyvölä
21.04.2020

## Slide 2: Introduction
Combining the use of electricity and heat for a sustainable and enviromentally friendly energy system

## Slide 3: Background
Increasing the percentage of variable renewable energy sources (VRE) in producing electricity decreases the flexibility of the grid
  VRE (mainly wind energy and PV) are weather dependent and electric loads are not flexible
Peak power plants and electric energy storages are needed to keep the supply and the demand in balance
Peak power plants and electric energy storages are expensive technologies
Heating Sector produces high greenhouse gas emissions
  The current scheme for producing heat in Finland highly depends on fossil fuel
  In Helsinki, 57% of emissions is produced by heating

## Slide 4: Implementing Sector Coupling
Thermal loads have higher inertia and more flexible than the electric loads
The excess electricity from VRE can be used to produce heat using heat pumps and electric boilers
  The produced heat can be used directly, or stored for later when the demand exists
  Flexible operation of producing heat and storing it ensures no electricity demand peaks due to the coupling
Some technologies can go in both directions "power to heat, and heat to power" such as Advanced Adiabatic Compressed Air Energy Storage (AA-CAES)
AA-CAES is still expensive and there is no existing facilities
  When electricity is available, air is compressed for saving the energy. The process of compressing the air produces heat. When electricity is needed, the air expands to produce electricity by rotating a turbine which rotates a generator. The process of expansion needs heat
  AA-CAES can be connected with the district heating network to decrease its cost, if the electricity and heating peaks are in different times, so heat is produced when electricity is available and heat is needed and heat is consumed when heat is available and electricity is needed

## Slide 5: Feasibility
Sector coupling is very promising compared to other coupling and flexibility options
  Costs of generating and storing heat are relatively low
  Helps in decarbonizing heating and integrating renewables
Can be implemented through centralized or decentralized solutions
Possible to add thermal energy storages to provide increased flexibilty
  A viable option for seasonal storage
  In centralized solution district heating network offers some heat storage capacity
  In decentralized solution some storage capacity from household hot water storages

## Slide 6: Economic and Environmental Impact
Decreases the curtailment of VRE which increases their revenue
Decreases the need for expensive peak power plants and electric storages
Increases the electrification of the heating sector which decreases the greenhouse gas emissions
  Nowadays, electricity production is more environmentally friendly than heating production

## Slide 7: Examples of current uses
OVO Energy in United Kingdom providing grid-balancing services by aggregating smart heating systems used in 1.5 million homes (12 GW peak capacity)
  Benefit to customer through optimizing heating costs
In Finland, Fortum’s virtual battery Fortum Spring utilizes thousands of domestic water heaters to provide demand response
In Denmark, electric boilers and heat pumps are used at district heating level to utilize excess wind generation in western Denmark
  Wind generation typically greatest in winter months when there is high heat demand
During recent years, close to 10% of heat supplied to Swedish DH network has been produced by electric boilers and heat pumps
  35 % during the peak year in 1990, due to low electricity prices

## Slide 8: Challenges
COP of heat pumps much lower with low source temperatures and high output temperatures
  Minimum output temperature restrictions set by e.g. existing DH network and bacteria prevention in domestic hot water supply
  Need for low temperature heat sources to heat pumps such as datacentre waste heat
Large-scale implementation of heat pumps can increase peak electricity demand substantially
  Can be largely mitigated with flexible operation of heat pumps and heat storages
At the moment lower fossil fuel and emission allowance prices holding back investments to clean technologies?
Regulatory barriers such as electricity taxes decrease the economic potential of power to heat
Consumer preferences, space requirements and presence of existing infrastructures keeping investments below economic optimal

## Slide 9: Conclusions
Sector Coupling is an efficient way to increase flexibility in the electrical system
Helps in integrating renewables and increases the use of VRE in the energy system
A cost-effective solution which helps in decreasing emissions in the energy sector

## Slide 10: Source material used
Give the list of references used for the presentation preparation
https://www.sciencedirect.com/science/article/pii/S0196890416307154?via%3Dihub
https://www.irena.org/-/media/Files/IRENA/Agency/Publication/2019/Sep/IRENA_Power-to-heat_2019.pdf?la=en&hash=524C1BFD59EC03FD44508F8D7CFB84CEC317A299
https://www.fortum.com/products-and-services/smart-energy-solutions/virtual-battery-spring
https://www.sciencedirect.com/science/article/pii/S1364032117307839?via%3Dihub
https://carbonneutralcities.org/cities/helsinki/
Power-to-heat for renewable energy integration: A review of technologies, modeling approaches, and flexibility potentials (Andreas Bloess et al., 2018)
Overview of Compressed Air Energy Storage and Technology Development (Jidai Wang et al., 2017)