## Slide 1: ELEC-E8423 - Smart Grid Pumped Hydro Energy Storages
Petra Seppälä & Katri Ruutu

## Slide 2: Introduction
Pumped hydro energy storages store energy in the form of gravitational potential energy of water
Water is pumped from lower elevation reservoir to a higher elevation when electricity demand is low
Energy efficiency 70-80 %
Pumped storage is by far the largest-capacity form of grid energy storage available, about 95 % of all storages are pumped hydro energy storages
185 GW installed (about 25 GW in USA, 20 GW in China)
,

## Slide 3: How it works?

## Slide 4: Applications
Energy balancing
  Storages can be used when the renewable production is low
Load leveling
  Storages can be loaded in night hours to balance the load peaks
Large emergency reserve

## Slide 5: Different types of pumped energy storage:
Pumped storage plant on surface
The most common in use
Requires high elevation difference
Underground reservoirs
One or more reservoirs underground
Can be used in old mines
Usable in flat regions
Underwater reservoirs
Usage of pressure at the sea bootom
When power is needed, water is let in
When there is electricity surplus, water is pumped out

## Slide 6: Potential of pumped hydro energy storage in the future
In Finland:
  Pumped hydro energy storage requires high elevation difference.
    In Finland elevation differences are usually just tens of meters in the hydropower plants
  An underground pump plant and energy storage test facility is planned to be built at the Pyhäsalmi mine
    The deepest mine in Europe
    Could produce 70 MW
China is seeking to build a total of 40 GW of pumped hydro capacity installed, and there are multiple hydro energy storage projects under construction
There is a huge potential for pumped hydro energy storage around the world, as there are hundreds of thousands theoretically possible locations
  Potential for transformation from single dams

## Slide 7
+ Advantages
Helps integrate renewables into power system
Easy energy balancing
Reliable technology
Long lifetime
Quite simple technology
- Disadvantages
High investment costs
Only possible in specific locations
Large use of land
Environmental and social issues

## Slide 8: Conclusions
Pumped hydro energy storage accounts for over 94 per cent of installed global energy storage capacity, and there is great potential for new installations
Helps integrate renewables into the energy system with load-shifting and balancing inflexible sources of power generation
Simple and reliable technology

## Slide 9: Source material used
Arena Wire. What is pumped hydro and how does it work?. 2017. Available at: https://arena.gov.au/blog/what-is-pumped-hydro-and-how-does-it-work/
Energiatalous. Pumppuvoimala on hyvä ja tehokas sähkövarasto. 2016. Available at: https://www.energiatalous.fi/?p=2210
Renewable Energy World. Storing Energy in the Sea — A New Design for Marine Energy Storage. 2016. Available at:
https://www.renewableenergyworld.com/2016/09/09/storing-energy-in-the-sea-a-new-design-for-marine-energy-storage/#gref
The world’s water battery: Pumped hydropower storage and the clean energy transition. IHA working paper, December 2018. Available at: https://www.hydropower.org/sites/default/files/publications-docs/the_worlds_water_battery_-_pumped_storage_and_the_clean_energy_transition_2.pdf
Yle Uutiset. Pyhäsalmen kaivokseen rakennetaan pumppuvoimalan ja energiavaraston testilaitos. 2019.
Available at: https://yle.fi/uutiset/3-11099952