## Slide 1: ELEC-E8423 - Smart Grid Wind farms and their local grids and connections
Alessio Di Renzo
Nuria Esteve
21.04.2020

## Slide 2: Introduction
Overview on wind farms in Europe
Future Expectations
Source: Wind energy in Europe in 2019 - Trends and statistics
Source: IRENA report: Future of Wind, 2019.
Wind share is expected to increase Grid connection is critical

## Slide 3: Wind farms
CAPEX cost breakdown for a wind turbine
Source: Wind Power Engineering, 2012
Rotor blades: 20%
Tower: 25%
Power Converter: 4%
Generator: 3%
Pitch & Yaw Bearings: 2%
Other: 35%
Component description
Rotor blade: converts wind energy into rotor spin.
Gearbox: increases the rotational speed.
Nacelle: Contains the gearbox, generator, controller, etc.
Generator: produces AC electricity.
Tower: supports the structure.
Source: Energy Efficiency and renewable energy, 2020

## Slide 4: Connection to the Power System: example
Example: Offshore Wind Farm
Turbine Transformer
  Responsibility of the plant owner
  Low Voltage (<700 V) power is converted into Medium Voltage (20 kV)
Point of Connection (PoC)
  Responsibility of the public TSO
  Conversion into High Voltage (60-380 kV) in substations
Point of Common Coupling (PCC)
  Power sent to the grid
  Effects on grid stability are evaluated here
Switchgears and protection devices are always required
Onshore wind farms close to load centres require less conversions
Source: Wind Farm Design: Planning, Research and Commissioning - Renewable Energy World, 2020
1
2
3

## Slide 5: Connection to the Power System: optimization
Optimal configuration depends on a trade-off between costs and efficiency:
  Typical output of a wind farm is Alternate Current (AC) at Low/Medium Voltage: if a Low or Medium voltage grid is available in the nearby, an upgrade to High Voltage is not necessary
  For large scale plants located far from the load centres, upgrade to High Voltage or conversion into Direct Current (DC) are common
21.04.2020

## Slide 6: Grid Connection and Investments
Example of costs distribution for a wind farm
Source: Wang et al., 2018
Grid Connection is not the largest cost item in a Wind Farm
What is its relevance for the investors?
It represents a limit in wind farms development:
  Space: adequacy of existing local grid infrastructures must be evaluated Farm siting is affected
  Time: if not carefully considered at the beginning, it can delay the project Investment profitability is affected

## Slide 7: Grid Connection and its effects
Wind farm connection to the power system and related issues are responsibility of the Transmission System Operator (TSO)
Selection of the Point of Common Coupling (PCC) according to:
  Distance of the wind farm from load centres (Low or Medium Voltage grids)
  Wind farm size (small, medium, large)
Fluctuations affect voltage stability and quality
  Difficult management of distribution networks, fault conditions and safety aspects
Grid capacity is limited by grid strength (power in short circuit conditions)
  Risk of grid congestion
  PCC only where grid strenght is sufficient
Wind variability and unpredictability obstacle frequency balancing and inertia requirements

## Slide 8: Future improvements
How to mitigate these problems?
Maximum wind capacity regulated by Grid Codes is expected to rise:
  r = [Range 2-20%]
Addition of capacitive loads to handle reactive power
Investments in grid strengthening and networks integration
Non-grid solutions to mitigate wind variability
  Energy Storage
  Demand Side Management
  Improved forecasting
  Smart grids

## Slide 9: Conclusions
As higher capacities of onshore and offshore wind farms must be achieved in Europe, interest and investments in grid connections aspects are expected to increase accordingly
A compromise between system efficiency and grid investments has to be found depending on the context
Since the effect of high wind shares can be disruptive for the grid, technical and regulatory solutions are expected to change

## Slide 10: Source material used
WindSolarUSA. 2020. Wind Turbine Components - Windsolarusa. [online] Available at: <http://www.windsolarusa.com/wind/wind-turbine-components/>.
Renewable Energy World. 2020. Wind Farm Design: Planning, Research And Commissioning - Renewable Energy World. [online] Available at: <https://www.renewableenergyworld.com/2009/04/02/wind-farm-design-planning-research-and-commissioning/>.
Cronin, T., 2020. Grid Connection Of Wind Farms. DTU Wind Energy, Technical University of Denmark.
Wang, L., Kerrouche, K., Mezouar, A., Van Den Bossche, A., Draou, A. and Boumediene, L., 2018. Feasibility Study of Wind Farm Grid-Connected Project in Algeria under Grid Fault Conditions Using D-Facts Devices. Applied Sciences, 8(11), p.2250.
Uski, S., 2018. Wind Power Grid Connection. Aalto University.
Windeurope.org. 2010. Powering Europe: Wind Energy And The Electricity Grid. [online] Available at: <https://windeurope.org/fileadmin/ewea_documents/documents/publications/reports/Grids_Report_2010.pdf>.
IRENA (2019), Future of wind: Deployment, investment, technology, grid integration and socio-economic aspects (A Global Energy Transformation paper), International Renewable Energy Agency, Abu Dhabi.
Wind energy in Europe in 2019 - Trends and statistics. [online] Available at: < https://windeurope.org/data-and-analysis/product/?id=59>
The Inside of a Wind Turbine, 2019. U.S Department of Energy Efficiency and Renewable Energy. [online] Available at:< https://www.energy.gov/eere/wind/inside-wind-turbine>
Understanding costs for large wind-turbine drivetrains. 2012. [online] Available at:< https://www.windpowerengineering.com/understanding-costs-for-large-wind-turbine-drivetrains/>