## Slide 1: ELEC-E8423 - Smart Grid Interconnection of microgrids to the Power system
Bismoy Jahan
Da Motta Pires Sergio Ricardo
23.04.2018

## Slide 2: Introduction
islanded mode: can be powered by distributed generators, batteries, and/or renewable resources like solar panels.
What is a microgrid?
A network of electricity users with a local source of supply that is usually attached to a centralized national grid but is also able to function independently.
Grid Connected Mode
Islanded Mode
A microgrid consists of DER (Distributed Energy Resources) and loads in a defined electrical boundary; can be controlled as a single unit with respect to the grid. according to IEEE Std 2030.7

## Slide 3: Benefits of microgrid
Access to power in remote location (places of refuge in regional crises and first responders)
Use local energy resources and jobs
Enables the integration of efficient, low-cost, clean energy
Reduce grid “congestion” and peak loads of grid
Deferral of investment in upgrading and renovating distribution grids
Grid resiliency, increased reliability, energy efficiency, Improved power quality, etc..

## Slide 4: Purpose of connecting microgrid to Power System
Microgrids can be designed as fully off-grid or as grid-connected with islanding capabilities
In grid-connected operation, the main grid is used as an alternative power source in the microgrid
The grid connection reduces the storage capacity needed
Connection to the grid through a point of common coupling (PCC)/point of interconnection (POI)

## Slide 5: Interconnection of microgrid to the Main Grid PCC/POI of microgrid Islanding, Synchronization and Dispatch
PCC/POI

## Slide 6: Interconnection of microgrid to the Main Grid
PCC/POI requires:
automatic islanding (separation or decoupling)
synchronization (reconnection)
dispatch controls
The PCC/POI multifunctional relay accomplishes automatic islanding by opening a circuit breaker (or recloser). The relay opens the PCC when it detects Short Circuit/backfeed conditions.
The relay accomplishes synchronization at the PCC by automatically dispatching multiple DER outputs to reduce slip, angle, and voltage amplitude differences.
Active and reactive power dispatch is performed by relay logic, which simultaneously dispatches multiple DERs.

## Slide 7: Challenges and opportunities with microgrids interconnection
Frequency synchronisation during islanded operation
  Loss of reference frequency causes power quality issues
  voltage source converters (VSC) responsible for maintaining power quality
  Low-inertia microgrids
  DC microgrids as a solution?
Black-start capability
Self-healing microgrids
Optimal dimensioning of distributed energy resources
Cost-comparison with grid upgrades
  Who pays for the microgrid?

## Slide 8: Microgrid Energy Management Systems (EMS) and control strategies
Operation strategies and purpose of microgrid EMS
  Self-consumption of DER (reduces grid congestion issues)
  Grid backup (increases grid reliability)
  Local market operation (frequency control for the grid)
  Power restoration during extreme events (resiliency in power systems)
  Proactive scheduling (RES and Demand Response integration)
Cyber-security and communication requirements
  Fast and reliable communication is required to implement the microgrid control
  Edge-computing and 5G as potential enablers?

## Slide 9: The current state of microgrids
Several microgrid integration projects worldwide
  Brooklyn MG, Berkeley, Smart Otaniemi, Puerto Rico
Regulation still unclear for the majority of countries
Uncertainty on the role of the DSO in microgrids
  infrastructure supplier or microgrid operator?
https://www.brooklyn.energy/
https://building-microgrid.lbl.gov/
https://smartotaniemi.fi/
https://www.greentechmedia.com/articles/read/microgrid-project-in-puerto-rico-edf

## Slide 10: The future of Microgrids
Web-of-cells concept
Smart Transformers and Fuzzy Microgrids (dynamic microgrids)
Local Energy Communities (LEC)
Geographical islands
Nanogrids
DC microgrids
Multi-energy microgrids
Hussain, A., Bui, V. H., & Kim, H. M. (2019). Microgrids as a resilience resource and strategies used by microgrids for enhancing resilience. Applied Energy, 240(June 2018), 56–72. https://doi.org/10.1016/j.apenergy.2019.02.055

## Slide 11: Conclusions
Microgrids offer significant potential for improving grid reliability and integration of distributed generation
Microgrids will be a crucial part of the future of power systems
The challenge of microgrid integration is still open and new solutions are being researched

## Slide 12: Source material used
https://building-microgrid.lbl.gov/about-microgrids
https://www.ee.co.za/article/grid-connected-microgrid-local-network-future.html
https://ieeexplore-ieee-org.libproxy.aalto.fi/stamp/stamp.jsp?tp=&arnumber=8038773
https://ieeexplore.ieee.org/iel7/8295081/8295082/08295083.pdf
https://www.ieee.ch/assets/.../IEEE-Swiss-IES-Microgrids-ABB.pdf
ieeexplore.ieee.org/abstract/document/5960751/
https://ieeexplore-ieee-org.libproxy.aalto.fi/stamp/stamp.jsp?tp=&arnumber=7832732
https://www.academia.edu/34678706/Survey_of_Communication_System_for_DGs_and_Microgrid_in_Electrical_Power_Grid
www.ieomsociety.org/paris2018/papers/107.pdf
www.enrauvergnerhonealpes.org/fr/reseaux/.../le-projet-pegasus.htm
Hussain, A., Bui, V. H., & Kim, H. M. (2019). Microgrids as a resilience resource and strategies used by microgrids for enhancing resilience. Applied Energy, 240(June 2018), 56–72. https://doi.org/10.1016/j.apenergy.2019.02.055
Zubieta, L. E. (2016). Are Microgrids the Future of Energy?: DC Microgrids from Concept to Demonstration to Deployment. IEEE Electrification Magazine, 4(2), 37–44. https://doi.org/10.1109/MELE.2016.2544238
Hirsch, A., Parag, Y., & Guerrero, J. (2018). Microgrids: A review of technologies, key drivers, and outstanding issues. Renewable and Sustainable Energy Reviews, 90(March), 402–411. https://doi.org/10.1016/j.rser.2018.03.040
Xu, Z., Yang, P., Zheng, Q., & Zeng, Z. (2016). Study on black start strategy of microgrid with PV and multiple energy storage systems. 2015 18th International Conference on Electrical Machines and Systems, ICEMS 2015, 402–408. https://doi.org/10.1109/ICEMS.2015.7385067
Kroposki, B., Lasseter, R., Ise, T., Morozumi, S., Papathanassiou, S., & Hatziargyriou, N. (2008). Making microgrids work. IEEE Power and Energy Magazine, 6(3), 40–53. https://doi.org/10.1109/MPE.2008.918718