## Slide 1: ELEC-E8423 - Smart Grid Demand response of EV loads
Juho Jalonen & Silja Yli-Juuti
12.04.2020

## Slide 2: Introduction
Electrification of the transport sector is an ongoing megatrend, with estimates for 2050 ranging from 50 to 80% of passenger cars being either battery electric vehicles (BEV) or Plug-in hybrid electric vehicles (PHEV) [1].
This megatrend essentially means coupling the transportation system (now combustion engines) with the power system. In practice this means that a large new load (the transport) is added to the existing electrical power system. This creates both challenges and opportunities for demand side management.
This presentation aims to establish an overview of different demand side management approaches (Demand management DM, Smart charging SC and Vehicle-to-grid V2G) and analyze their benefits/costs for both individual building energy systems and to the wider electric grid.

## Slide 3: Demand management
The graphs above show the simulated added load for scenarios where 1. there is no load management (BEV's are charged when people come home from work) 2. charging is temporarily relocated by timed charging and 3. electricity market price guided smart charging algorithm is applied. [2]
In its simplest form, demand management of BEV loads is a simple timer on the charger, relocating the charging load from the evening demand peak to the night. A very "un-smart" type of demand response
Smart charging is a more refined management style, where the relocation of charging is handled by a smart algorithm to optimize the system. This means demand responding to input from grid (typically price of electricity)

## Slide 4: Vehicle-to-grid
Diagram of grid formed by the electric vehicle and home energy system [3]
V2G means that there exists a two-way charging system, where the electricity from the vehicle’s battery can also be used to power the building, or to be fed into the power grid.
For an individual building, in addition to the benefits of SC, V2G offers a chance to better utilize locally produced renewable energy by acting as a battery for the building.

## Slide 5: Demand response aggregation
As BEV's spend more than 98% of time parked, V2G provides massive potential to produce grid ancillary services by managing multiple car charges at once. By aggregating these loads together, a virtual powerplant is created, capable to act at reserve markets.
Visualization of V2G technology [4]

## Slide 6: Benefits of BEV demand response
SC and even a very rudimentary time-based load management system can greatly reduce the increase to peak demand caused by the electrification of the transport system. Furthermore, they help with limiting the stress at the electricity distribution network level by limiting simultaneous charging.
V2G aggregation can create virtual powerplants, helping provide grid ancillary services (peak demand, frequency control etc.) in a cost effective and CO2 neutral manner
V2G enables the batteries of BEV's to be used to increase the share of renewable energy utilized by energy system (both for individual building and the national grid)

## Slide 7: Costs of BEV demand response
In order to effectively manage the loads, information system needs to be included to enable the input for smart charging and V2G. This incurs investment costs.
V2G infrastructure is more expensive than one directional charging, and this investment cost might make the return on the investment very small/none existent.
V2G consumes the batteries of the vehicles. As batteries are the most expensive part of BEV, it might not make economical sense. Furthermore, battery manufacturing is CO2 heavy activity, lessening the environmental benefist of V2G.

## Slide 8: Conclusions
Electrification of the transport system will increase the load on our power system, generating a need to utilize demand response to avoid negative new high demand peaks for the grid.
V2G aggregation enables both increasing the share of renewables of energy usage as well as to provide economical and environmental grid services.
Cost and environmental benefits should be considered with regards to battery lifecycles, as this is the key attribute in determining whether V2G is economically or environmentally viable.

## Slide 9: Source materials used
[1] Lund H, Mathiesen BV, Hvelplund FK, Østergaard PA, Christensen P, Connolly D, Schaltz E, Pillay JR, Nielsen MP, Felby C, Bentsen NS, Meyer NI, Tonini D, Astrup T, Heussen K, Morthorst PE, Andersen FM, Münster M, Hansen L-LP, Wenzel H, Hamelin L, Munksgaard J, Karnøe P, Lind M. Coherent energy and environmental system analysis. Aalborg University; 2011. Available from 〈http://www.ceesa.plan.aau.dk〉
[2] K. Qian, C. Zhou, M. Allan and Y. Yuan, 2011. Modeling of Load Demand Due to EV Battery Charging in Distribution Systems. IEEE Transactions on Power Systems, vol. 26, no. 2, s. 802-810 ISSN 0885-8950. DOI 10.1109/TPWRS.2010.2057456.
[3] Salpakari, J., Rasku, T., Lindgren, J. and Lund, P.D., 2017. Flexibility of electric vehicles and space heating in net zero energy houses: an optimal control model with thermal dynamics and battery degradation. Applied Energy, 3/15, vol. 190, s. 800-812 ISSN 0306-2619.
[4] Miami Lakes Chrysler Blog, 12.04.2020 Available at: http://www.miamilakesautomall.com/chrysler-blog/chrysler-has-begun-testing-for-vehicle-to-grid-tech/