## Slide 1: ELEC-E8423 - Smart Grid Role of DR, storages and hydrogen in future energy systems
Petteri Värränkivi, Bimal Bhandari
25.03.2020

## Slide 2: Introduction
Demand Response (DR) and Energy Storage Systems are key enablers in the ongoing transformation of energy systems into adaptible, renewable and energy secure systems. DR and ESS are used to compensate the spatial and temporal imbalances in energy demand and production, offsetting the need for on-demand fossil fuel generation.
Presentation Contents:
Demand Response in Smart Grids
Demand Response Technology
Different Roles of Storage Systems in EU
Hydrogen as fuel
Hydrogen energy in future
Conclusions
Source material used

## Slide 3: Demand Response in Smart Grids
DR refers to “changes in electric usage by end-use customers from their normal consumption patterns in response to changes in the price of electricity over time, or to incentive payments designed to induce lower electricity use at times of high wholesale market prices or when system reliability is jeopardized”
Envisioned benefits of DR:
  Participant bill savings – consumption at a lower price
  Bills savings for other customers – DR smoothes price curve for all customers
  Reliability benefits and system security – provides support in contingency
  Market performance – more efficient market
  Improved choice – added cost management options

## Slide 4: Demand Response in Smart Grids
Customers can take part in demand response programs with pre-set tariffs or react to changes in electricity market prices.
There are three general types of DR:
• Foregoing: involves reducing usage at times of high prices or demand response program events without making it up later.
• Shifting: involves rescheduling usage away from times of high prices or demand response program events to other times.
• Onsite generation: some customers may respond by turning on an onsite or backup emergency generator to supply some or all of their electricity needs.
The Electricity customer should take advantage of DR if creates cost reduction (or revenue). However, the consumers are not taking advantage as much as industrial customers. This could be due to lack of knowledge and will or low reward relative to effort.

## Slide 5: Demand Response Technology
Industrial and commercial customers have been using manual demand response as method for cost optimization. In Finland there has been different day and night tariffs consumets, which have been utilized by boilers for example.
Automated demand response is increasing and enabling also consumer with smart applications that adjust and shift electricity consumption for example in HVAC, lighting, EV charging, thermostats, IoT connected appliances etc.

## Slide 6: Different Roles of Storage Systems in EU
Storage Level / Function | Transmission Grid | Distribution Grid | End-User
Balancing demand and supply | -Seasonal/ Weekly -Geographical -Host Variable Wind&Solar | -Daily/Hourly -Peak Shaving | -Daily
Grid management | -Voltage/Frequency control -Complement Peaker Plants -Balancing market & Cross-border trading | -Voltage/Frequency -Substitute Existing Ancillary Services -Balancing market | -Aggregation of small storages for the use of grid management
Energy Efficiency | -Enables Larger Penetration of VRES by load shifting temporally and spatially | -Demand Side management -Integration with District Heating & Cooling? | -Small-scale & Local production and consumption -Behaviour change
Different storages by system level and system function

## Slide 7: Hydrogen as fuel
Why Hydrogen?
  Clean Energy (no pollution)
  High energy density per unit mass
  Lightest and most abundant element in the universe.
  Readily accessible (H2O) and effortless production
Usually in the form of chemical compounds in water and hydrocarbons.
Production and usage
  700 billion Nm3 (2008)
  97% based on natural gas and fossil fuels, mainly methane CH4
  Renewable production biomass and electrolyser
  Mostly used in chemical and petroleum industries.
  Ammonia production (50%), crude oil processing (40)
Surplus electricity can be used to produce hydrogen using electrolyser and transfer back into electricity using Fuel cells while needed.
Various applications (grid, electric transportation, industries, heat: using hydrogen burner)

## Slide 8: Hydrogen Storage System
Hydrogen can be stored in different forms for later use. Storage it is still challenging even using newest technologies because the system must be safe reliable, and cost-effective. Storage system helps to reduce the CO2 emissions (energy efficiency) and to balance the grid. Development on storage system increases the use of hydrogen fuel mainly in transportation sector and in other electricity consuming sectors.
Main storage methods
  Gas, simplest and the most used method. challenges: Required heavy vessels and high pressure due to low energy density by volume.
  Liquid high energy density by mass, challenges: extreme temperatures boiling point 20K(-253C), limited materials/technologies due to the small size of the hydrogen particle.
  Chemical compounds for example ammonia (NH3), metal hydrides: compact and safe also in ambient temperature.
Underground storages can be used to power the grids, small storage tanks (mobility) to power electric vehicles and middle size storage tanks to power electric ships.
Hydrogen storage for grid level electricity production is still in development because of its high costs and low efficiencies compared to other technologies.

## Slide 9: Hydrogen energy in future
Hydrogen is a potential fuel for future applications (sustainable renewable energy)
Abundant resource
Increasing applications and demand specially in transportation
Partly compatible with existing natural gas transmission system and can be mixed with natural gas supply in low shares.

## Slide 10: Conclusions
The increase in variable renewable technologies induce imbalance pressure to energy systems, which creates an increasing demand for balancing technologies, such as Energy Storages and Demand Response.
Demand Response is becoming more common as the price for automated load shifting technologies decrease and price volatility in market creates opportunity for price arbitage.
Compared to other energy storage technologies, hydrogen has benefits, such as long storage time, high energy density, and abundance of electrolysis raw material (H2O), but lacks in competitiviness and efficiency at currently available technologies. Especially

## Slide 11: Source material used
Siano, P. (2014). Demand response and smart grids—A survey. Renewable and Sustainable Energy Reviews, 30, 461–478. doi: 10.1016/j.rser.2013.10.022
DoE (2006) Benefits of Demand Response in Electricity Markets and Recommendations for Achieving Them. A report to the United States Congress Pursuant to Section 1252 of the Energy Policy Act of 2005
European Commission, DG ENER Working Paper: The future role and challenges of Energy Storage.
J.P, Jain.(2009). Hydrogen the fuel of 21st century, International Journal of Hydrogen Energy, 30, 17, 7368-7378. doi: 10.1016/j.ijhydene.2009.05.093
Sunita, S. Sib Krishna Ghoshal. Hydrogen the future transportation fuel: From production to applications, Renewable and sustainable energy reviews, 41, 1151-1158. doi:doi.org/10.1016/j.rser.2014.11.093
C, Koroneos. A, Dompros. G, Roumbas. N, Moussiopoulos. (2004). Life cycle assessment of hydrogen fuel production processes, International Journal of Hydrogen Energy. 29, 1443-1450. doi:doi.org/10.1016/j.ijhydene.2004.01.016