## Slide 1: ELEC-E8423 - Smart Grid Electrical buses and their charging solutions
Johannes Hyvönen
07.02.2018

## Slide 2: Introduction
Electrical buses
Powered only by electricity, which is either stored on board the buses or continuously fed from an external source
Limited by battery range -> mostly used as city buses
Similar charging solutions to other EVs
Already very popular in China and becoming increasingly popular in cities worldwide
Environmentally friendly compared to traditional buses, but requires infrastructure investments in charging stations

## Slide 3: Background
Electric vehicles have been around since the 19th century
Electric buses have become more popular in recent years due to improvements in EV technology and higher fuel prices
Edison electric bus from 1915
Battery electric bus in Hong Kong

## Slide 4: Key differences compared to traditional buses
Buses are battery based (more popular) or use external electricity, such as overhead wires, combined with an electric motor instead of an combustion engine
Aluminum frame with composite and lightweight materials used to reduce vehicle weight. Can be 3000kg lighter than a modern steel-framed bus (weight 9500kg)

## Slide 5: Batteries
Batteries the most common power solution for electric buses
As of 2018, typical battery range around
250-300km per charge
-> often used as city buses
Capacitors can also be used instead of batteries to store energy in specific applications:
- ultracapacitors can store 5% of the energy of Lithium-ion batteries with the same weight, but charge and discharge much more rapidly

## Slide 6: Charging solutions
Similar charging stations as with other EVs
Multiple different charging solutions exist, e.g. ABB and Siemens have their own competing systems
Charging times often short (<10min), city buses can be charges between shifts and during night
ABB charging solution
Siemens charging solution

## Slide 7: Example of a commercial charging solution

## Slide 8: Applications and use
Very suitable for city buses and short transit
Long-range applications highly dependent on charging stations and battery range
As of 2019, 99% of battery electric buses in the world deployed in China with over 420 000 buses on the road, which is 17% of China’s total bus fleet
US has 300 electric buses, Europe 2250
Finland has a handful of E-buses in testing
in larger cities, e.g. Espoo:
- line 11 Friisilä - Tapiola since 2016
- more electric bus stations will be
installed in the future

## Slide 9: Conclusions
Electric buses are becoming increasingly more popular also outside China, with electric city buses becoming a very appealing commuting solution for cities worldwide
Advantages
Lower emissions, no local air pollution
Lower operating costs
Drawbacks
Limited battery capacity and range (280km)
High investment costs

## Slide 10: Source material used
https://en.wikipedia.org/wiki/Electric_bus
https://www.espoo.fi/en-US/Housing_and_environment/Sustainable_development/Sustainable_mobility
https://smarttampere.fi/en/data-helps-to-make-smarter-decisions-about-the-buses/
https://new.siemens.com/global/en/markets/transportation-logistics/electromobility/ebus-charging.html
http://www.abb.com/cawp/seitp202/998b8571f5c23198c12580c60045b738.aspx