## Slide 1: ELEC-E8423 - Smart Grid Compressed Air Energy Storage (CAES)
Emma Sevón
Hugo Morel
30.03.2020

## Slide 2: Introduction
Concept of a compressed air energy storage (CAES)
Different types of processes for compression and discharge​
Potential as an energy storage method
An exergy approach of the CAES
Already existing C​AES plants and projects
Conclusions

## Slide 3: Concept
Electrical power is used to compress ambient air
The pressurized air is stored in an air-tight chamber
The high pressure air released through an air turbine generate the electrical power
Main losses are heat losses during air transformations
Storage is at constant volume or constant pressure
It can be implemented in caverns or underwater with the use of vessels
First big project in 1978, the Huntorf power plant
(Wang, Luo ,Krupke, Dooner. 2017)

## Slide 4: Different types of CAES systems
Diabatic (Heat transfer)
Heat is dissipated with intercoolers as waste into the atmosphere
42-55% efficiency
Adiabatic (No heat transfer)
Capture and release heat during air transformations (compression//expansion)
Use heat exchanger
Approximately 70% efficiency in practice
Isothermal (Constant temperature)
Air transformations are made slowly to keep the temperature near constant
Low power installation
Efficiency estimated to be around 70-80%
Elmegaard, Brix. 2011
Patil and Ro, 2017
Efficiency

## Slide 5: Potential Shares of energy storage technologies
The biggest energy storage is by far hydro. It is still the cheapest energy storage
The Lithium-Ion battery market is booming and the CAES have difficulty to take market shares
The share of pumped hydro has actually decreased in the last few years
Technology Mix in storage installations, excluding hydro (IAE,2019)
Major Energy Storage Characteristics by Technology (Deloitte, 2015)

## Slide 6: Potential Power and discharge times of ES-technologies
CAES has the potential to store energy in a large scale like PHS.
PHS is becoming exhausted as an energy storage system due to the lack of favorable geographical sites. (Sternberg & Bardow, 2015)
Scientific focus has strongly shifted to CAES, especially to the development of AA-CAES (Sternberg & Bardow, 2015)
(Energy storage sense)

## Slide 7: Potential Cost range and potential locations
CAES costs are also in the same range as PHS.
Cost estimates differ a lot by source but are roughly 1000$/kW for diabatic and 1300$/kW for adiabatic CAES.
Potential locations are for example old mining sites
Wang et al. 2017
Potential salt caverns in Europe
Bykov, 2018
Hydrostor Potential Sites in Americas and Australia
Hysdrostar, 2020

## Slide 8: Projects In operation
*estimated time for start of operation
Location | Type | Power | Year | Accumulator
Huntorf, Germany | Diabatic | 290 MW, >2h | 1978 | Salt Cavern
McIntosh, USA | Diabatic | 11 MW, >26h | 1991 | Salt Cavern
Hokkaido, Japan | Diabatic | 2 MW | 2001 | Rock Cavern
Ontario, Canada | Adiabatic | 1 MW | 2015 | Underwater balloons
Goderich, Canada | Adiabatic | 1,75 MW | 2019 | Salt Cavern
Strathalbyn, Australia | Adiabatic | 5 MW | 2020* | Old Mining Site
Chen et al. 2016, Bykov 2018, Hydrostor 2020

## Slide 9: Conclusions
Compressed Air Energy Storage (CAES) is an energy storage method in which air is compressed into to a tank and released later spinning a turbine.
Most potential in Adiabatic CAES which does not require any external fuel.
Can store huge amounts of energy → an alternative for pumped hydro

## Slide 10: Source material used
Wang, J. and Dooner. M,. 2019. Potential Exergy Storage Capacity of Salt Caverns in the Cheshire Basin Using Adiabatic Compressed Air Energy Storage. DOI:10.3390/e21111065
Wang, J. et al. 2017. Overview of Compressed Air Energy Storage and Technology Development. Energies. Vol.10:7. p. 1-22. doi: 10.3390/en10070991
Rogers, A. & Henderson, A. & Wang, X. and Negnevitsky, M. 2014. Compressed air energy storage: Thermodynamic and economic review. doi: 10.1109/PESGM.2014.6939098
Chen, H. & Zhang, X. & Liu, J. & Tan, C. 2013. Compressed Air Energy Storage, Energy Storage - Technologies and Applications. IntechOpen. ISBN: 978-953-51-0951-8.
D. Swider. 2007. Compressed Air Energy Storage in an Electricity System With Significant Wind Power Generation. IEEE Transactions on Energy Conversion. Vol. 22:1. p. 95-102. doi: 10.1109/TEC.2006.889547
Kouksou, T. & Bruel, P. & Jamil, A. 2014. Energy storage, applications and challenges. Solar Energy Materials and Solar Cells. Vol. 120. p. 61-63. ISSN 0927-0248. doi: 10.1016/j.solmat.2013.08.015
Sternberg & Bardow 2014. Power-to-What? – Environmental assessment of energy storage systems. Energy Environ. Sci., 2015, 8, 389. DOI: 10.1039/c4ee03051f
BINE Information Service, Compressed air energy storage power plants: http://www.bine.info/fileadmin/content/Publikationen/Englische_Infos/projekt_0507_engl_internetx.pdf

## Slide 11: Source material used
Energy storage association: http://energystorage.org/compressed-air-energy-storage-caes
Energy storage sense: http://energystoragesense.com/energy-storage-technologies/
IEA 2014: https://www.iea.org/tcep/energyintegration/energystorage/
IEA, "Technology mix in storage installations excluding pumped hydro, 2011-2016", IEA, Paris https://www.iea.org/data-and-statistics/charts/technology-mix-in-storage-installations-excluding-pumped-hydro-2011-2016
Hydrostor: https://www.hydrostor.ca/
Energy Storage Monitor, World Energy Council, 2019
Vikram C. Patil and Paul I. Ro, 2017, Energy and Exergy Analysis of Ocean Compressed Air Energy Storage Concepts. DOI: 10.1155/2018/5254102