## Slide 1: ELEC-E8423 - Smart Grid <Modelling of Electric Vehicle charging load>
<Ramin Ahmadi Kordkheili-Adrian Roos>
14.04.2020

## Slide 2: Introduction
Concept of EV/PHEV
Integration of EV/PHEV in distribution grid
EV/PHEV to mitigate integration of renewable energy resources

## Slide 3: Concept of EV/PHEV
Electric Vehicle (EV): A battery (or fuel cell) as the source of energy
Plug-In Hybrid Electric vehicle (PHEV): Two sources of energy to propel the vehicle include Internal combustion Engine (ICE) and a battery (or fuel cell)
Benefits:
Decrease the rate of oil consumption and green house gas emissions
Increase energy security by shifting demand away from fossil fuels to domestically produced energy supplied from renewable sources

## Slide 4: Concept of EV/PHEV
EV Penetration:
Target for 2030: Estimates range from 250000 to 700000-800000 vehicles
Result in increase of electrical consumption about 0.5-2 Twh
Chart: Electric passenger cars in traffic use
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Battery electric vehicles | 23 | 56 | 109 | 169 | 360 | 614 | 844 | 1449 | 2404 | 4661
Plug-In hybrid electric vehicle | 0 | 0 | 128 | 296 | 569 | 973 | 2441 | 5719 | 13095 | 24704

## Slide 5: Concpet of EV/PHEV
Battery types for EV/PHEV:
Lead-Acid (Pb-Acid), Nickel Cadmium (Ni-Cd), Nickel-Metal Hydride (Ni-MH), Lithium-Ion (Li-Ion), Lithium Polymer (Li-Po)
Charging schemes:
Conventional charging: Plug-in the EV/PHEV to the grid and it charged like other loads
Vehicle to Grid (V2G): Bidirectional power and energy exchange between the power grid and the EV/PHEV

## Slide 6: Concept of EV/PHEV
Battery parameters:
Capacity: Amount of charge that can be drawn from a fully charged battery until it gets fully discharge.
State Of Charge (SOC): Percentage of charge available from a battery to the whole capacity of the battery.
Charging and discharging power (, ): The amount of power to charge/discharge the battery.
Charging and discharging efficiency (): The chemical reactions inside the battery during charge and discharge are not ideal and there are always losses involve.

## Slide 7: Integration of EV/PHEV in distribution grid
Uncontrolled charging:
Voltage drop
Phase imbalance
Overloading of network components
Increase in the peak load of the system
Scheduled charging
Decrease cost of charging
Flattening the load curve
Improvement in the power quality
Lower the need to install new infrastructure

## Slide 8: Integration of EV/PHEV in distribution grid
Uncertainties of EV’s in the simulations
Initial SOC: SOC of electric vehicles
at the beginning of simulation period
Arrival time: Arrival at home
after the last trip of the day
Departure time: Departure from home
just before the first journey of the next day
Daily trip mileage: Electric vehicle driving
distance

## Slide 9: Integration of EV/PHEV in distribution grid
Comparison between scheduled and uncontrolled charging (sample paper):
Uncontrolled: EVs simply start charging on arrival at the maximum charging rate
Opt. Schedule (no mitigation): Optimization of EVs charging under uncertainty
Opt. Schedule (with mitigation): Optimization of EVs charging under uncertainty mitigation
Opt. Schedule (perfect foresight): Optimization of EVs charging using perfect foresight

## Slide 10: Integration of EV/PHEV in distribution grid
Comparison between scheduled and uncontrolled charging (sample paper):
Observations from the figure:
Decrease in the cost of charging with scheduled charging
Decrease in the voltage violation instances
Decrease overloading of the lines
Shifting charging load of EVs from peak hours to off-peak hours

## Slide 11: EV/PHEV to mitigate integration of renewable energy resources
Wind farm example:
: Actual generation of wind farm in time of delivery
: Committed power to the day-ahead market
If > Charging of EV fleet
If < Discharging of EV fleet
Overproduction
Underproduction
Wind farm
Prediction
of generation
Offer
Prediction
Of market price
Day-Ahead market

## Slide 12: EV/PHEV to mitigate integration of renewable energy resources
Sample paper simulation:
Wind power capacity: 10 MW, Number of EV’s: 484
Case I: Wind power is scheduled with no scheme to reduce power imbalance
Case II: EV’s charging/discharging coordinate to minimize power imbalance

## Slide 13: Conclusions
Important role of EV/PHEV to decrease emission in transportation sector
Scheduling EV/PHEV charging lower the need to install new infrastructures, increase power quality and decrease the charging cost
EV/PHEV can assist to increase the share of renewable energy resources in electricity production

## Slide 14: References
1- W. Sun, F. Neumann and G. P. Harrison, "Robust scheduling of Electric Vehicle Charging in LV Distribution Networks under Uncertainty," in IEEE Transactions on Industry Applications.
2-M. Ghofrani, A. Arabali, M. Etezadi-Amoli and M. S. Fadali, "Smart Scheduling and Cost-Benefit Analysis of Grid-Enabled Electric Vehicles for Wind Power Integration," in IEEE Transactions on Smart Grid, vol. 5, no. 5, pp. 2306-2313, Sept. 2014.
3- Sheldon S. Williamson, ”Energy Management Strategies for Electric and Plug-in Hybrid Electric Vehicles”, Springer.
4- Chris Mi, M. Abul Masrur and David Wenzhong Gao,”Hybrid Electric Vehicles Principles and Applications with Practical Perspectives”, WILEY.