## Slide 1: ELEC-E8423 - Smart Grid Smart Grid and Electrical Safety
Markku Mäkinen
Tuukka Sandell
5.5.2020

## Slide 2: Introduction
Finnish legislations
  1135/2016 “Electrical Safety Act” (Sähköturvallisuuslaki)
Finnish Standards
    Standardized guidance must follow the law (1135/2016)
    Standards in the electrical and electronics industry are prepared and confirmed by SESKO ry
    Examples of current standards.

## Slide 3: Electricity legislation
In Finland 1135/2016 “Electrical Safety Act”
§6 demands, that electrical installations and equipment must not endanger:
      Life, Health and Property
Electrical equipment must be designed in such a way that the essential safety requirements are fulfilled
The requirements of the legislation are considered to be fulfilled if the mentioned standards have been followed.
Notes: - §6 also includes requirements for Electromagnetic Compatibility (EMC)

## Slide 4: Standards
Smart Grid and private- / distributed production bring more standards into picture
Standard proposal SFS 6008-2
    Based on standard IEC 60364-8-2: ”Low-Voltage electrical installations: Prosumer’s low-voltage electrical installations”
SFS 6000- series must still be followed for safety reasons
Also, there are more system-specific standards.
Notes: A Finnish standard proposal SFS 6008-2 is based on international standard IEC 60364-8-2. This ”Low-Voltage electrical installations: Prosumer’s low-voltage electrical installations” –standard is more about prosumer system functionality than protection or safety.
SFS 6000 and SFS 6002 standard series still defines the electrical safety aspects of electrical systems and installation work principles. From the point of view of Smart Grid and prosumers, the following parts of SFS 6000 are important:
  Photovoltaic power supply systems (SFS 6000-7-712)
  Charging of Electric Vehicles (SFS 6000-7-722)
  Selection and installation of electrical equipment. Other electrical equipment (e.g. PV panels and integrated batteries) (SFS 6000-5-55)
Applying of standards is only an “recommendation”. It is allowed not to follow standards, if legislation is fully met and it can be proven.

## Slide 5
general principles of the prosumer´s electrical installations (PEI) (IEC 60364-8-2: 5)
Note! In this presentation we are
interested only in key points 6, 7 and 9-10.

## Slide 6: Photovoltaic production
Solar PV production must follow the standard SFS 6000-7-712
”Traditional protection methods” demand protection against:
  Electric shocks, Heat, Overcurrents and Overvoltages
NEW: ”Smart Grid / Prosumer protection methods”
demand also an informing warning of the
photovoltaic system on site
  This ensures the safety of maintenance personnel,
  inspectors, rescue personnel, etc.
A warning of a photovoltaic system in the building

## Slide 7: Electric vehicles
The electric vehicle charging standard SFS 6000-7-722 is applied for protection and charging systems, if electricity can be supplied from the car back to the private or public distribution network.
”Traditional protection methods”:
  Short circuit- and overcurrent protection
  Protection with enclosuring
  (IP code)
  Protection from mechanical impact (IK code)
NEW: The power supply from an electric vehicle to the installation is considered as a voltage generator.
  Allowed only in charging stations equipped with a socket or plug-in accordance with SFS-EN 62196

## Slide 8: Other devices
A standard for "the other electric devices“ SFS 6000-5-55 is applied, for example, for the installations of PV panels and electrochemical batteries
  These systems might be feeding equipment, that is connected to distribution network
”Traditional protection methods” for electric shock and overcurrent:
  Fault protection (e.g. automatic switch-off of supply)
  Isolating devices on either side of the static inverter
  Limiting the effects of harmonic currents.
NEW: If the generator set operates in parallel with the public distribution network:
  It must not interfere with the public distribution network
  Protection devices must prevent it from being connected to the grid in case of distribution failure
  Only qualified or instructed persons have access to system batteries
  Battery connections must be touch-protected.

## Slide 9: Conclusions
The three most important key points of presentation
Electrical installations and equipment must not endanger Life, Health and Property
2. SFS 6000- series must be followed for safety reasons
3. Unqualified persons in a homelike environment must be assisted to use and maintain new prosumer technologies like batteries and charging electric vehicles.

## Slide 10: References
Electrical Safety Act 1135/2016
International standard, IEC 60364-8-2, Edition 1.0, 2018-10, Low-Voltage electrical installations – Part 8-2: Prosumer´s low-voltage electrical installations
Pienjännitesähköasennukset SFS 6000-5-55:2017, Sähkölaitteiden valinta ja asentaminen. Muut sähkölaitteet
Pienjännitesähköasennukset SFS 6000-7-712:2017, Erikoistilojen ja –asennusten vaatimukset. Aurinkosähköjärjestelmät
Pienjännitesähköasennukset SFS 6000-7-722:2017, Erikoistilojen ja –asennusten vaatimukset. Sähköajoneuvojen syöttö
Pienjännitesähköasennukset SFS 6008-2, Osa 8-2: Toiminnallisuus. Tuottaja-kuluttajan pienjännitesähköasennukset Standardiehdotus E605, 2020-02-03.
Sähkölaitteistojen turvallisuutta ja sähkötyöturvallisuutta koskevat standardit, Luettelo S10-2019, Turvallisuus- ja kemikaalivirasto
Valtioneuvoston asetus sähkölaitteistoista 1434/2016