## Slide 1: ELEC-E8423 - Smart Grid Demand response of HVAC loads
Markus Korpinen, Artturi Tilanterä
31.03.2020
HVAC loads
Korpinen & Tilanterä, 2020

## Slide 2: Introduction
Demand Response (DR): modify electricity consumption to match production.
DR offers options to balance and optimize power system operations and it is coming more important because the amount of variable renewable energy sources in power system is increasing all the time.
HVAC: Heating, Ventilation, and Air Conditioning
DR of HVAC: load shifting, prices according to production situation. Offers easy way for residential customers to participate to balancing of power system.
HVAC loads
Korpinen & Tilanterä, 2020
Notes: DR is an umbrella term. HVAC are loads which can be delayed for hours. The limit is people's comfort.

## Slide 3: HVAC in the Big Picture
HVAC loads
Korpinen & Tilanterä, 2020
1. HVAC loads are major
part of household energy consumption
2. Flexible: buildings as energy storages
3. Easy: just a smart
thermostat in some cases
Data: Official Statistics of Finland

## Slide 4: How HVAC DR works
Electric heating & AC
  Buildings as thermal energy storages due thermal inertia of buildings
  Additional hot water storage increases DR capability
Modelling the storage
  Time and temperature comfort zone are parameters
  Outside temperature and consumer's temperature comfort zone affects on how long DR can be activated
Central control
  Power market <=> Aggregator company <=> Households
  Aggregator controls smart thermostats
  Two-way communication via Internet
District heat networks
  Power to Heat: Heat pumps and electrical boilers
HVAC loads
Korpinen & Tilanterä, 2020

## Slide 5: Building as a thermal energy storage
HVAC loads
Korpinen & Tilanterä, 2020
Picture: 2-component model of a
building, heater on at Winter
Heater off: Qhvac = 0, building mass slows decrease of Ta
Ventilation rate (~Hx) affects heating.
Air conditioning: opposite heat flows.
Picture according to Ali (2016)

## Slide 6: Electric heating of a residential house
Simulation of direct electric heating with DR
The resident sets a comfort zone for temperature:
20 ± 1...3 °C -> constraint for demand response
Thermal model: Need for heating varies during the day. Electric heating decreases at DR period of 13:00-16:00 hours -> house cools slowly due to stored heat in walls
Even 100% reduction for several hours:
+ width of temperature zone
+ size of hot water tank (not required)
- Winter hardest case
Increase DR period with Home/Away switch?
HVAC loads​
Korpinen & Tilanterä, 2020
Simulation: load reduction potential at Winter.
Results and figures from Ali, Safdarian and Lehtonen (2014).

## Slide 7: Price-based DR of electric heating
HVAC loads
Korpinen & Tilanterä, 2020
- Aggregator decides cost-minimizing heating for each customer in 24-hour batches.
- Thermal storage increases flexibility and energy savings.
Figure according to principles by Ali et al. (2013)

## Slide 8: Requirements for HVAC demand response
Control in residences
  Currently water heating in residential buildings is usually automatically timed for night when electricity is cheap and there is less demand
  Smart meters enable hourly participation to DR
Price incentives for customers
  Different types of price-based DR programs
  Goal: transfer maximum amount of consumption from peak hours to off peak hours
  Customer willingness to minimize electricity bill
Electricity distribution network
  Need for more distribution capacity when HVAC loads are increased due to DR?
Control and communication: load aggregators
  - Even frequency control possible by real-time communication via Internet
  - Many HVACs on large area + real-time -> Big Data!
  - Solution: Hierarchical control and edge computing?
HVAC loads
Korpinen & Tilanterä, 2020
Notes: Price incentives steer customers: they could still rapid-charge their car at peak time, but it costs extra

## Slide 9: Conclusions
HVAC loads are suitable for demand response, because they allow both upward and downward control.
HVAC loads have significant potential, because they consume major part of energy in residences.
Economical benefits is the reason for residential customers to participate demand response.
HVAC loads
Korpinen & Tilanterä, 2020

## Slide 10: References
M. Ali, J. Jokisalo, K. Siren and M. Lehtonen. (2013) Combining the Demand Response of direct electric space heating and partial thermal storage using LP optimization. DOI 10.1016/j.epsr.2013.08.017
M. Ali, A. Safdarian and M. Lehtonen. (2014) Demand Response Potential of Residential HVAC loads Considering Users Preferences. DOI 10.1109/ISGTEurope.2014.7028883
M. Ali. (2016) Domestic Space Heating Load Management in Smart Grid: Potential Benefits and Realization. http://urn.fi/URN:ISBN:978-952-60-6962-3
Official Statistics of Finland. (2018) Energy consumption in households. http://www.stat.fi/til/asen/index_en.html
Official Statistics of Finland. (2018) Energy supply and consumption. http://www.stat.fi/til/ehk/index_en.html
Y. Shen et al. (2020) State-shift priority based progressive load control of residential HVAC units for frequency regulation. DOI 10.1016/j.epsr.2020.106194
M. Short et al. (2019) Optimal Dispatch of Aggregated HVAC Units for Demand Response: An Industry 4.0 Approach. DOI 10.3390/en12224320
Y. Zhang et al. (2018) The Research on Application of Power-to-Heat (P2H) Technologies Combined into Integrated Energy System. 2018 International Conference on Power System Technology (POWERCON), Guangzhou, 2018, pp. 4537-4543. DOI 10.1109/POWERCON.2018.8601826
HVAC loads
Korpinen & Tilanterä, 2020