## Slide 1: ELEC-E8423 - Smart Grid Battery Energy Storage Systems
Amanda Jokinen
Anni Holmström
10.03.2020

## Slide 2: Introduction
Due to increase of renewable energy sources (wind and solar), the electrical power generation is changing and facing new challenges.
Variable energy sources creates a problem to the power system
  Production and consumption do not match
The mismatch posses a threat to the stability of the system
With Battery Energy Storage Systems (BESS) the impact to the power system can be reduced

## Slide 3: Energy Storage Systems
Energy storage systems can be classified into five major groups:

## Slide 4: Architecture of BESS
BESS consists of the following components:
Battery pack
Battery Management System (BMS)
System Supervisory Control (SSC)
Converter Electronics
Figure on the right presents the structure and relations between components. Solid line means power flow and dashed line information flow.

## Slide 5: Types of Batteries

## Slide 6: Role of BESS in Power Systems
peak load shaving
  power quality
  cost reduction
  RES integration
  emission reduction
  benefits for end users
Using EVs for peak shaving: V2G
Peak shaving using DSM
Frequency regulation

## Slide 7: Development of BESS
Battery energy storage costs are decreasing
Energy densities in all types are still increasing
  Battery sizes more suitable for use
Storage installations are expected to grow significantly worldwide
LCOE may decrease to 100-150 €/MWh in the next decades

## Slide 8: Current Projects - Finland
Helen Oy (2016)
Locates in Suvilahti
Lithium-ion
1.2 MW, 600 kWh
Part of Fingrid’s frequency-controlled operation and disturbance reserve
Balances and optimizes peak power production from solar power plant
TuuliWatti (2019)
Locates in Simo
Lithium-ion
The Largest battery in the Nordic countries
6 MW
Charged by wind power
Investment costs 3.5 million €

## Slide 9: Current projects - Worldwide
Tesla
The plant is located next to wind power plant in Australia.
Lithium-ion
Currently, worlds biggest battery storage
100 MW, 129 MWh
Rongke Power
Largest planned battery storage in the world
Located in Dalian, China
200MW, 800 MWh
Vanadium redox flow battery

## Slide 10: Conclusions
Li-ion batteries the most promising BES technology at the moment, having also the largest market share of BES.
Prices are decreasing exponentially.
BES will have a remarkable role in the future power system.

## Slide 11: Source material used
Ghassan Zubi et al. The lithium-ion battery: State of the art and future perspectives. Renewable and Sustainable Energy Reviews. Vol. 89. 2018. Pp. 292-308. https://doi.org/10.1016/j.rser.2018.03.002
A.R. Dehghani-Sanij et al. Study of energy storage systems and environmental challenges of batteries. Renewable and sustainable Energy Reviews. Vol. 104. 2019. Pp. 192-208. https://doi.org/10.1016/j.rser.2019.01.023
Matthew T. Lawder et al. Battery Energy Storage System (BESS) and Battery Management System (BMS) for Grid-Scale Applications. Invited paper. Vol. 102. Issue 6. 2014. Pp. 1014-1030. DOI: 10.1109/JPROC.2014.2317451
Moslem Uddin et al. a review on peak load shaving strategies. Renewable and Sustainable Energy Reviews. Vol. 82. 2018. Pp. 3323-3332. http://dx.doi.org/10.1016/j.rser.2017.10.056
Daniel-Ioan Stroe. Operation of a Grid-Connected Lithium-Ion Battery Energy Storage System for Primary Frequency Regulation: A Battery Lifetime Perspective. IEEE Transactions on industry applications. Vol. 53. Issue 1. 2017. Pp- 430-438. DOI: 10.1109/TIA.2016.2616319
Energy Storage. Lecture slides. Advanced energy solutions. 2019. Annukka Santasalo-Aarnio.
https://www.solarchoice.net.au/blog/news/are-falling-battery-costs-the-solution-to-solar-pv-ills-310114/
https://www.ostologistiikka.fi/kategoriat/hankinta/tuuliwatille-pohjolan-suurin-sahkoakku
https://www.helen.fi/uutiset/2016/sahkovarasto
https://www.kaleva.fi/uutiset/talous/simoon-nousee-pohjoismaiden-suurin-akku-tuuliwatti-rakentaa-metsan-keskelle-jattikokoista-sahkovarastoa/829975/
https://electrek.co/2017/11/30/tesla-100mw-battery-flexes-muscles-early-this-morning-delivers-70mw-of-stored-wind-energy-shows-off-fast-switching/
https://www.greentechmedia.com/articles/read/report-levelized-cost-of-energy-for-lithium-ion-batteries-bnef