## Slide 1: ELEC-E8423 - Smart Grid Electric trucks and their charging solutions
Aaro Anttila
Mikko Vuorenmaa
14.4.2020

## Slide 2: Introduction
Transportation’s global CO2 emissions are 9 000 billion tons which are expected to grow by 60 % by 2050 due to strong expected growth in demand. This has risen interest for electrification of transportation over the last decade.
Electrification has been only commercially viable for passenger cars which range and haulage requirements are more moderate than medium- and heavy-duty vehicles
Recent developments in battery technologies and expected price decrease of batteries have made electric battery trucks more commercially viable and suitable for truck usage
Notes: From the 9000 billion tons of CO2 freight transportation accounts for nearly half. Freight transportations emissions are expected to grow up to 70 % until 2050. This has risen interest for electrification of transportation over the last decade
Due to high energy requirements of heavy-duty vehicles and batteries’ low energy densities, the weight of the trucks has been so high that the payloads would have been negligible from allowed gross vehicle weight. Besides that the life cycle costs have been commercially unviable compared to diesel trucks.
Automakers have started to develop and offer first generation electric vehicles, for example Mercedes-Benz eActros and Tesla’s Semi

## Slide 3: How to electrify
Battery operated with in-vehicle charging
  Medium-duty
  Heavy-duty (Rigid & Semi trucks)
Alternative electrification methods
  Battery operated with battery swapping
  Electrified road system (ERS)
  Hydrogen + Fuel cell
Notes: Electric truck that operates swappable battery requires needs interchangeable standardized batteries and battery swapping station infrastructure to be realized
However, when alternative electrification methods are considered, it should be noted that these methods need to develop their infrastructure from the ground up which entails lot of investment costs.
Besides that the long-haul freight trucks can only implement these alternative technologies when they are large scale. Hence, policy needs to promote these alternative technologies and their uptake to enable them.
By contrast battery electric trucks with in-vehicle charging don’t require these high initial investments on infrastructure to reach feasibility. Instead scaling up the charging infrastructure can be phased according to state of battery technology, i.e. from short-haul medium duty trucks to long-haul heavy-duty trucks.

## Slide 4: Charging of battery-operated electric trucks
Electric trucks use same standardized charging solutions as other electric cars
Normal charging (mode 3)
  AC – max 43 kW, 63 Amps – currently between 10–22 kW
  Bidirectional data transfer bus between vehicle and charger
  Type 1 plug in North America & Japan and Type 2 in Europe
  AC Charger unit located in the vehicle with separate charging cable
Fast charging (mode 4)
  DC – currently between 22 kW–118 kW, future potential up to 400 kW with liquid cooling
  Bidirectional data transfer bus but its current flow control to both directions more depended on the location
  CCS 1, CCS 2, CHAdeMO & Tesla Supercharger
  Both DC Charger unit and charging cable is part of the charging station, not part of the vehicle
Notes: Most of the public normal charging station are equipped with 22 kW three-phase chargers and in homes 10 kW normal chargers are most typical. Therefore, these chargers aren’t feasible for charging of electric trucks and higher power is needed.
In normal charging data transfer bus monitors vehicle’s state of charge and can control the power flow in both directions. Hence, it enables implementation of smart grid operation in the future.
CCS (Combined Charging System) has two different types: CCS 1 which combines North American Type 1 with two-point DC conductor and CCS 2 which combines European Type 2 with two-point DC conductor.
CHAdeMO is DC charging standard developed in Japan which currently supports 6–200 kW but 350–400 kW charging is in the development. Compared to other standards CHAdeMO is identical allover the world.
Tesla Supercharger is proprietary fast charging standard developed by Tesla Motors which is used in Tesla’s electric vehicles. In North America Tesla Supercharging uses its proprietary plug and Type 2 elsewhere in the world. Latest third generation Supercharger V3 supports charging up to 250 kW.
Currently typical fast chargers are 50 kW DC chargers. For overnight charging, 50 kW is considered as baseline for effective charging rate.
Besides mode 3 & 4 there are mode 2 and mode 3 with lower charging speeds but these aren’t considered as viable charging methods for electric trucks.

## Slide 5: Potential of electric trucks
Case study – A commodity-level analysis between Finland (FIN) and Switzerland (CH) based on the data from continuous road freight surveys carried out according to EU regulation with hypothesis (H#)
  H1: Electric trucks could haul majority of freight with lower gross vehicle weight (GVW) in CH compared to extensive use of truck-trailer combinations in FIN with higher GVW for long-haul freight
  H2: Fast charging network with adequate charging times have major impact on potential of truck electrification
  H3: Grid improvement are necessary due to charging of electric trucks
  H4: Different commodities result crucial differences in potential of truck electrification and commercial potential can be recognized with certain type electric truck with certain type of freight haulage based on commodity
Hypothesis compared in different technology development scenarios
Notes: H1
  FALSE: With current technology only 18 % of the long-haul freight could be hauled in CH even though the share rises to 50 % with improved vehicles
  TRUE: Due to long-haul freight and with high GVW, the share of haulage that could be covered in FIN is low compared to CH. Currently the difference isn’t particularly large but with improved vehicles difference grows greatly.
H2
  TRUE: Electrification potential of majority of the trucks doubles as technology reaches towards full electrification state. Besides that, truck-trailer combinations benefit not just on-road fast charging but also from overnight charging with fast charging technology due to battery capacities up to 800 kWh.
H3:
  Spatial analysis are required in different locations to give detailed answer to the impact of electric truck charging. However, it’s presumable that in depots and in logistics centers the effect on local transmission networks will be large due to number of trucks charging/fast charging simultaneously.
H4:
  TRUE: Electrification potential of trucks vary greatly between different commodities. However, this more location depended due to mileage and GVW differences, e.g. in towards electrification the electrification potential almost diminishes in CH while in FIN they remain. Commodities with great volume but low weight, e.g. textiles and empty containers, hauled with medium duty trucks show largest potential.

## Slide 6: Electrified road system – ERS
Conductive approach
  Overhead catenary lines
  A conductive rail on the road
Inductive approach
  Wireless power transfer through from an elongated magnetic coil in the ground
One big positive side with ERS are the smaller batteries that trucks would require to operate flexibly.
  This would increase the load trucks can carry
Inflexible demand
a high up-front investment cost
  Requires building infrastructure for the whole main road and in larger scale for all main roads to be viable
Emissions:
  19 % reduction potential for road transportation in Sweden
Notes: ERS can be established by two methods
  In-road conductive/inductive power transfer with respective bucking coils in vehicle
  Over road or in-road catenary lines with pantograph collectors placed on top of the vehicle or under the vehicle
Suitable also for bigger vehicles
In ERS with both implementation methods, it’s presumable that ERS infrastructure (at least in initial phase) would cover only main highways due to expenses of building infrastructure. Hence, there’s a need to have a small battery in vehicle to be able drive in urban area.
Inflexible demand could be an issue in case energy is produced with variable renewables.
By electrifying 5 most used roads in Sweden the road transport sector would be able to see -19% reduction in emissions. This would lead to max. 4% increase of energy demand during peak hours (if all vehicles using these roads would be electric vehicles and electricity would be carbon free)

## Slide 7: Swappable batteries and fuel cells
Fuel cells
  Works as auxiliary power unit
  Suitable for medium and heavy-duty vehicles
  Suitable especially for long distances and heavy loads vs. batteries
  Short refueling times and lower weight than batteries
  Requires building of refueling infrastructure
  In terms of costs not yet competitive for long haul trucks vs. diesel trucks
Battery swapping
  An option to reduce charging times
  Requires standardized batteries and battery swapping infrastructure
  High up-front investment costs
  robotic arms to remove and replace depleted batteries of EVs
  From electricity system viewpoint offers more flexibility than fast charging
Notes: The fuel cells could become competitive with higher penetration rates (10 %). However, it strongly depends on how costs can be lowered, how the price of diesel behaves and if infrastructure is available
Electric truck that operates swappable battery requires needs interchangeable standardized batteries and battery swapping station infrastructure to be realized

## Slide 8: Impact on electricity system
Impacts depend on the deployed technology
Additional load around charging stations (resting areas, logistic centers)
  Can local grids handle it?
Big batteries of trucks could be utilized in grid balancing when plugged in
Additionally the battery swapping stations can optimize battery charging and it can be utilized for grid balancing
Growth of demand depend on the penetration rate and size of possible issues depend on technology
In vehicle to grid schemes (V2G) the driving pattern difference between truck and passenger car should be considered carefully
Notes: The impacts and issues depend on the selected technology. If demand is inflexible (fast charging, ERS) the load can increase during peak demand hours. Battery swapping and fuel cell technologies provide more flexibility. The emission reductions depend naturally on the electricity production mix and also with large share of renewables in the mix the time of charging / hydrogen production. Although improved efficiency of electric motors vs. diesel motors already helps to reduce emissions
Increased loads especially around of centralized charging stations can be problematic if the grid hasn’t been planned for the higher load levels
Growth of demand caused by ERS was estimated to be relatively small when compared to the whole electricity consumption of Europe. 800 000 trolley trucks the consumption was calculated to be increased by 115 TWh (max) which would be 3 % of the total electricity consumption and peak demand would increase by 2 %.
In V2G concepts it should be noted that trucks in logistics business are procured according to delivery demand. Hence, their mileage are maximized in order to maximize income and profits and minimize the time they are inactive. Therefore, usage as battery storage can be challenging.

## Slide 9: Conclusions
Investment costs
Emission reduction potential depends on the country and technology
Effect to electricity system is expected to be relatively small in large scale but locally there could be bigger impacts
Notes: ERS, hydrogen fuel cells and BSS require high upfront investment costs. In charge vehicle charging investments can be spaced out by gradually scaling up the charging infrastructure. Technologies requiring high upfront investment costs require help from policies.
Emission reductions depend on the country (what type of trucks are common, what is the electricity mix like, how much traffic) and technology (battery electric vehicles are suitable for medium duty trucks, ERS for example could be utilized by all vehicles).
Demand around charging stations or logistic centers might require extra investments to grid

## Slide 10: Source material used
Liimatainen, H., van Vliet, O. & Aplyn, D. 2019. The potential of electric trucks – An international commodity-level analysis. Applied Energy, 236, pp. 804-814. doi:10.1016/j.apenergy.2018.12.017
Ban, M., Yu, J., Li, Z., Guo, D. & Ge, J. 2019. Battery Swapping: An aggressive approach to transportation electrification. IEEE Electrification Magazine, 7(3), pp. 44-54. DOI:10.1109/MELE.2019.2925762
Plötz, P., Gnann, T., Jochem, P., Yilmaz, H. Ü. & Kaschub, T. 2019. Impact of electric trucks powered by overhead lines on the European electricity system and CO2 emissions. Energy Policy, 130, pp. 32-40. DOI:10.1016/j.enpol.2019.03.042
Jelica, D., Taljegard, M., Thorson, L. & Johnsson, F. 2018. Hourly electricity demand from an electric road system – A Swedish case study. Applied Energy, 228, pp. 141-148. doi:10.1016/j.apenergy.2018.06.047
Kast, J., Vijayagopal, R., Gangloff, J. J. & Marcinkoski, J. 2017. Clean commercial transportation: Medium and heavy duty fuel cell electric trucks. International Journal of Hydrogen Energy, 42(7), pp. 4508-4517. DOI:10.1016/j.ijhydene.2016.12.129
SESKO. 2020. Sähköajoneuvojen lataussuositus, suositus 2019. Available at: https://www.sesko.fi/standardit/standardoinnin_aihealueita/sahkoautot_ja_latausjarjestelmat
Tesla Motors. 2020. Introducing V3 Supercharging. Available at: https://www.tesla.com/fi_FI/blog/introducing-v3-supercharging