## Slide 1: ELEC-E8423 - Smart Grid Power to Gas
Manuel Schwenke, Georg Kordowich
23.03.2020

## Slide 2: Introduction
Power to Gas is an energy storage concept, which comprises the conversion of electrical energy by means of electrolysis into hydrogen. Optionally the H2 can then be methanated to CH4. [1]
Methanation is the conversion of COx (usually CO2) and hydrogen to Methane and water.
Those gases can serve as a chemical long-term energy storage. Large amounts of gas (e.g. for natural gas in Germany 25% of the yearly demand) can be stored in underground caverns. [2]
Can be used for climate neutral fuels, for energy applications or for the industry right now and also to balance seasonal changes in a fully regenerative power grid.

## Slide 3: Power2Gas: System Components
Water separation to and by application of voltage.
Minimum cell voltage needed (in standard conditions) ()
Real system: higher voltage needed, due to overpotentials at electrodes () and ohmic losses in electrolyte ()
water treatment
(removal: ions and suspended matter)
Purification of
(with gas separator or drying process)
compression & storage
electrolysis (AEL)
minimal energy needed: 4.5
Max. theoretical system efficiency: 78,67 % (based on heat of combustion)
optional: methanation
Image: https://en.wikipedia.org/wiki/
Hofmann_voltameter#/media/File:Hofmann_voltameter.svg

## Slide 4: Electrolyser-cell types
AEL
steam
membrane
(solid electrolyte)
HTES
bipolar plates with engraved channels
PEMEL
 | AEL – Alkaline Electrolyser | PEM – Proton Exchange Membrane | HTES – High Temperature Electrolysis of Steam
operation | water-lye-mixture at both electr., forms at cath, diffuses to anode, emits and forms | water is fed to anode and decomposed, diffuses through SPE and forms | overheated steam is fed to cathode, reacts with to , diffuses through membrane
pro | cheap, most proven technology | simple construction, smaller overpotentials, pure at cath. | less electricity consumption, heat is used as energy
con | complex lye cleaning, not very dynamic | expensive materials | separation of steam and hydrogen
 | AEL – Alkaline Electrolyser | PEM – Proton Exchange Membrane | HTES – High Temperature Electrolysis of Steam
operation |  |  | 
pro | cheap, most proven technology |  | less electricity consumption, heat is used as energy
con | complex lye cleaning, not very dynamic | expensive materials | separation of steam and hydrogen
Images: source [1]

## Slide 5: Efficiency
input energy | product | process | efficiency
electricity to gas |  |  | 
electricity | hydrogen | electrolysis | 49–77 %
electricity | bio-methane | methane reformation | 50–65 %
gas to electricity |  |  | 
hydrogen | electricity | fuel cell | 60–65 %
bio-methane | electricity | combined cycle gas powerplant (CCG) | 60–62 %
combined |  |  | 
electricity | electricity | electrolysis  hydrogen  fuel cell | 30–50 %
electricity | electricity | electrolysis   methane  CCG | 30–40 %
input energy | product | process | efficiency
electricity to gas |  |  | 
electricity | hydrogen | electrolysis | 49–77 %
electricity | bio-methane | methane reformation | 50–65 %
gas to electricity |  |  | 
hydrogen | electricity | fuel cell | 60–65 %
bio-methane | electricity | combined cycle gas powerplant (CCG) | 60–62 %
combined |  |  | 
electricity | electricity | electrolysis  hydrogen  fuel cell | 30–50 %
electricity | electricity |  | 30–40 %
table 1: efficiencies of transformation processes [3]
Additional losses – storages and transportation:
  stored as liquid in tanks: boil-off losses, hydrogen has to be released through overpressure valves to keep constant pressure.
  transportation: compression needed when transported over long distances
  losses due to diffusion through transportation/storage materials

## Slide 6: Potentials
Due to low efficiencies of the whole process, at least
  with methanation: 250 % of annual energy consumption has to be produced
  hydrogen use: 200 % of annual energy consumption has to be produced
with renewables to supply whole demand of electrical energy!
Huge electrolyser-capacities needed (a few 100 GW!), because of huge oversizing of installed PV and wind capacities
Existing storage structures (e.g. natural caverns) can be used
Sector coupling: Instead of reconversion to electricity, gas can be used for
  space heating
  mobility
energy produced with renewables
250% (200%)
losses 150% (100%)
usable electrical energy 100%

## Slide 7: Applications
Problem: made from electrolysis is more expensive than the market price
Solution: Cost of Power to Gas will decrease due to “Economy of Scale”: Prices for electrolysis are expected to drop by 75%-85% until 2050 [5]
Higher renewable penetration in the grid leads to low electricity prices more often [2]
H2
CH4
Methanation
Material Use
Energetic Use
Coolant
Methanol-Production
Ammonia synthesis
Heat
Electricity
Mobility
Storage
Feed into Natural Gas Infrastructure (up to 1-10%)
Many more applications in the industry
„Green“ Methane, since CO2 is bound during methanation

## Slide 8: Outlook
P2G is a relatively new Technology, seriously considered only since the late 90s
94 projects are currently installed with a total power of 38.6 MWel, most of them are in research and development or pilot stage [5]
Many projects are currently planned. For example, in February 2020 Shell announced its plan of the project NortH2, which converts offshore wind energy (up to 10 GW) to hydrogen [7]
Power to Gas will become more important:
  P2G plants can generate additional income by offering grid balancing services due to their fast startup time [6]
  Increasing demand of “Green” Hydrogen due to CO2 price certificates [8]
  Importance in grids with high renewable penetration to balance seasonal changes [2]
Globally installed electrical power of electrolyzers [5]

## Slide 9: Conclusions
Hydrogen and Methane made from renewable energy via P2G are carbon neutral and have countless applications
Electrical power can be used to form gas with efficiencies up to 78 %, reconversion to electricity results in efficiency of 40-50 %. In HTEL-cells process heat or heat from solar-thermal collectors can be used to minimize electrical energy needed.
Since gas can be stored in natural caverns for a long period (years), power to gas is necessary for a fully renewable grid, to balance seasonal changes
Power to Gas is in a phase of exponential growth and expected to become a lot cheaper due to economy of scale

## Slide 10: Source material used
[1] Zapf, Martin (2017): Stromspeicher und Power-to-Gas im deutschen Energiesystem. Wiesbaden: Springer Fachmedien Wiesbaden.
[2] Sterner, Michael; Stadler, Ingo (2014): Energiespeicher - Bedarf, Technologien, Integration. Berlin, Heidelberg: Springer Berlin Heidelberg.
[3] Brauner, G.: Energiesysteme: regenerativ und dezentral (Springer, 2016)
[4] Boudellal, M.: Power-to-Gas: renewable hydrogen (De Gruyter, 2018)
[5] Thema, M.; Bauer, F.; Sterner, M. (2019): Power-to-Gas: Electrolysis and methanation status review. In: Renewable and Sustainable Energy Reviews 112, S. 775–787. DOI: 10.1016/j.rser.2019.06.030.
[6] Grueger, Fabian; Möhrke, Fabian; Robinius, Martin; Stolten, Detlef (2017): Early power to gas applications: Reducing wind farm forecast errors and providing secondary control reserve. In: Applied Energy 192, S. 551–562. DOI: 10.1016/j.apenergy.2016.06.131.
[7] https://www.gasunie.nl/en/news/europes-largest-green-hydrogen-project-starts-in-groningen
[8] https://www.pv-magazine.de/2019/11/05/nationale-wasserstoffstrategie-bedarf-an-gruenem-und-blauem-wasserstoff-aus- dem-in-und-ausland/