## Slide 1: ELEC-E8423 - Smart Grid Concentrating solar power and its comparison to photovoltaics
Anna Lagerström
Casper Fagerström
16.04.2020

## Slide 2: Introduction
Technical realization of CSP
Examples of existing plants
Benefits of CSP compared to photovoltaics
Costs of CSP compared to photovoltaics
Study on hybrid system vs pure CSP and PV
Challenges of CSP
Conclusions

## Slide 3: Technical realization of CSP
Mirrors (heliostats) reflect and concentrate sunlight to receivers that collect the solar energy and convert it to heat.
Within the receiver, a fluid of molten salts absorbs the heat and transports it through the system.
The thermal energy is released to a steam turbine that drives a generator to produce electricity.
The molten salt fluid is cooled down in a low temperature tank and then circulated back to the receiver to absorb new heat.
The heated fluid can also be stored in a high temperature thermal storage tank until electricity production is needed.
Four main designs categorized by the way they focus the sunlight:
    Parabolic trough most common

## Slide 4: Examples of existing plants
Worldwide operational CSP capacity over 6000 MW
Most operating plants in Spain, USA, Morocco, China
Gemasolar 20 MW Solar Tower Spain, Andalucía
  Storage capacity: 15 h
  Powers annually 27 500 homes
  Land area: 195 hectares
  Number of heliostats: 2650
  Tower height: 140 m
  Receiver and hot storage tank temperature: 565 C

## Slide 5: Benefits of CSP compared to PV
CSP systems can store excess energy in TES (Thermal Energy Storage) and use it when needed
  this flexibility helps overcome intermittency problems and makes it suitable for large scale
Alternatively, on-site fossil fuel systems can be combined with CSP to form hybrid systems
  existing fossil fuel plants made cleaner with CSP or CSP plants balanced with fossil fuel backup
Storing excess energy for PV systems requires a battery
  more expensive and not a viable option for large scale
The storage capability enables an opportunity of flexible solar energy
  excellent for smart grids

## Slide 6: Cost of CSP compared to PV
Solar PV is cheaper than CSP due to rapid deployment and high learning rates, thus making PV more attractive to investors
Cost reduction potential of CSP is good due to low-cost thermal storage and rising levels of deployment in locations with better solar resources
Hybrid CSP-PV plants could offer up to 50% less LCOE than stand-alone CSP
  In the hybrid, PV contributes with lower cost of daytime power while CSP offers low storage costs, high dispatchability and smooths power generation variations of PV
  Construction and operation costs are lowered in a hybrid

## Slide 7: Study on hybrid system vs pure CSP and PV
Location affects the operation of the plants since CSP uses only direct radiation, while PV uses direct and diffuse radiation.
Parrado et al. (2016) compares the projected LCOE of 50MW CSP, PV and hybrid plants in northern Chile. LCOE is projected in two scenarios with different market expectations.
The hybrid system provides a commercially viable option with 24-h electricity generation and higher capacity factors compared to pure CSP and PV plants in both scenarios.

## Slide 8: Challenges of CSP
High water consumption due to cooling
  dry cooling technologies under development
Dust accumulation on mirrors reduce efficiency
High demands on heat transfer fluid (molten salt)
  balancing between cost and efficiency
Choice of thermal energy storage and heat receiver methods, and sizing of the storage capacity
Environmental issues
  hazardous materials and birds burning to death due to high temperature beams reflected towards receiver
Commercial viability
  costs expected to decrease in near future
  hybridization decreases the costs

## Slide 9: Conclusions
The excellent storage capability (TES) and possibility to flatten the load curve makes CSP a very attractive solar energy production method for smart grids.
The costs of CSP must decrease to make it more competitive with PV  costs projected to decrease (however, PV costs are projected to decrease as well).
Hybridization by combining CSP with PV or existing fossil fuel plants currently seems to be a more commercially viable option of integrating CSP.

## Slide 10: Source material used
F. Wang et al. Progress in concentrated solar power technology with parabolic trough collector system: A comprehensive review. Renewable and Sustainable Energy Reviews. 2017. Volume 79, Pages 1314-1328.
Technology roadmap: Concentrating Solar Power. International Energy Agency. 2010.
HeliosCSP: http://helioscsp.com/concentrated-solar-power-csp-vs-photovoltaic-pv/
SolarPACES: https://solarpaces.nrel.gov/gemasolar-thermosolar-plant
Office of Energy Efficiency & Renewable Energy (EERE), Solar Energy Technologies Office: https://www.energy.gov/eere/solar/concentrating-solar-power
X. Xu et al. Prospects and problems of concentrating solar power technologies for power generation in the desert regions. Renewable and Sustainable Energy Reviews. 2016. Volume 53. Pages 1106-1131.
HeliosCSP: http://helioscsp.com/hybrid-concentrated-solar-power-pv-gains/
IRENA: https://www.irena.org/costs/Power-Generation-Costs/Solar-Power
IRENA (2019), Renewable Power Generation Costs in 2018, International Renewable Energy Agency, Abu Dhabi.
C. Parrado et al. 2050 LCOE (Levelized Cost of Energy) projection for a hybrid PV (photovoltaic)-CSP (concentrated solar power) plant in the Atacama Desert, Chile. Energy. 2016. Volume 94, Pages 422-430.

## Slide 11: Other issues ….
Send the presentation to matti.lehtonen@aalto.fi for check latest the day before the scheduled presentation