## Slide 1: ELEC-E8423 - Smart Grid Electrical energy use in residential buildings, flexibility and DR potential of different energy uses
Juha Myllylä
Tuomas Soinio
07.02.2018

## Slide 2: Introduction
Energy consumption of typical residential buildings
Demand response potential
Possible methods for flexible energy use and their pros and cons
IoT = Internet of things, DR = Demand response, AI= Artificial Intelligence,

## Slide 3: Resindential building energy consumption
Chart: Building energy consumption by energy source 2017
| Electricity | District heating | Wood | Heat pump | Others
GWh | 22513 | 19310 | 14812 | 5815 | 4036
Chart: House (120 m²) heated by electricity, electricity consumption 18 480 kWh/year
| Space heating | Water heating | Refrigerator and freezer | Sauna | Cooking and dishwasher | Home electronics | Washing machine and dryer | HVAC-devices | Car heating | Other consumption
 | 9600 | 3600 | 600 | 1000 | 680 | 700 | 600 | 600 | 400 | 700

## Slide 4: DR potential
Goal is that electricity production must meet consumption, which can be done by shifting loads from peak hours to low-demand hours
Loads can be divided into three groups:
  No DR potential
    Lighting
    Home electronics
  Small DR potential
    Washing machine
    Dishwasher
    Sauna
  Major DR potential
    Heating
    Cooling
    Air conditioning

## Slide 5: Responsibility of load control
Centralized load control – electricity company or distributor
  Easier for the consumer
  Load control is done ”blindly”
  For comfort reasons the load control periods must be kept moderate
Independent load control – consumer, based on electricity price
  Various loads can be flexibly connect
  Tenant knows what kind of conditions he/she wants so no major risks in comfort areas
  Network operator can’t know what kind of decisions the consumer does

## Slide 6: Demand response in residential buildings
Third party member (aggregator) is needed in order to sell extra energy to grid
Batteries or other type of reserves inhouse aren’t usable solution due taxing
Selling spare energy should be financially tempting to individual house owners
Pohjolan energia offers first in Finland a “network battery” solution

## Slide 7: Current solutions
Lot of companies offering software to control lighting and electronic devices
Many advertises as being IoT but at moment none really fulfill standards to really be IoT solutions
In Finland there is none offering possibility to control heating in scale of one room at a time

## Slide 8: Challenges
There are lot of standards to fulfill if software developer is aiming for residential building energy markets
Cutting one building on and of the grid can cause problems in form of voltage spikes
Information security is also concern when manual controlling is developing into wireless controlling

## Slide 9: Conclusions
Important to categorize which loads have potential for DR
There are different pros and cons depending on who is responsible for the load control
Heating has most potential but also big challenges to overcome
Small scale local energy sources can help to answer for increasing DR at local energy markets

## Slide 10: Source material used
Sähkön kysyntäjouston toteuttaminen kotitalouksissa, Kauppinen Mikael, Diplomityö 2016, Aalto-yliopisto sähkötekniikan korkeakoulu
Towards the next generation of intelligent building: An assessment study of current automation and future IoT based systems with a proposal for transitional design, Georgios Lilis, Gilbert Conus, Nastaran Asadi, Maher Kayal, Published 2016 in sustainable cities and society
https://www.stat.fi/tup/suoluk/suoluk_energia.html
https://www.vattenfall.fi/energianeuvonta/sahkonkulutus/
Kiinteistön sähkönkulutus osana kysyntäjoustoa. Fidelix Automaatioväylä 2/2015: Automaatiolla tehokkuutta sähkön kysyntäjoustoon, https://docplayer.fi/34817880-Kiinteiston-sahkonkulutus-osana-kysyntajoustoa-fidelix-automaatiovayla-2-2015-automaatiolla-tehokkuutta-sahkon-kysyntajoustoon.html
Experimental Implementation of Demand Response Service for Residential Buildings, Seung Ho Hong, Yi-Chang Li, Jung Hoon Park and Bing Zhao, 2014, Department of Electronics and System Engineering, Hanyang University