## Slide 1: ELEC-E8423 - Smart Grid Smart Meters and Security Issues
Francisco Irazola Mona Bieberich
07.02.2018

## Slide 2: Introduction
General Information about Smart Meters
Smart-Meter-Gateway
Security Issues
Current Situation in Finland and EU
Notes: Francesco

## Slide 3: Smart Meter in general
Digital current meter
Key element in Smart Grids and Advanced Metering Infrastructure
  An entire infrastructure of meters, communication networks, and data management systems is required for advanced information to be measured, collected, and used.
Enables 2-way-communication
  Pricing information (dynamic tariffs)
  Consumption Readings
Notes: Francesco: Advanced Metering Infrastructure (AMI) refers to systems that measure, collect, and analyze energy usage, and communicate with metering devices such as electricity meters, gas meters, heat meters, and water meters, either on request or on a schedule.
Smart meters work through two-way communication via a wireless or Powerline communications network. Not only is the data transmitted to your own personal energy monitor, but it’s also distributed to your energy provider.

## Slide 4: Overview of System Architecture
AMI: Advanced Metering Infrastructure
HAN: Home Area Network
LAN: Local Area Network
WAN: Wide Area Network
Notes: Francesco: A home area network (HAN) is a network that is deployed and operated within a small boundary, typically a house or small office/home office. It enables the communication and sharing of resources between computers, mobile and other devices over a network connection.
A local area network (LAN) is a group of computers and associated devices that share a common communications line or wireless link to a server.
A wide area network (WAN) is a geographically distributed private telecommunications network that interconnects multiple local area networks (LANs).

## Slide 5: Benefits of Smart Metering
First instance:
Improved energy use information for customers
Improved load profiling
Real-time billing
Remote control and monitoring
Improved efficiency of metering
Second instance:
Control and monitoring at LV grid level (locating faults…)
Small-scale generation on customers side
Customer-level energy storages
Electric vehicles (controllable loads)
Notes: Mona

## Slide 6: Appliance load signature
Load Disaggregation depending on sampling rate
Notes: Mona

## Slide 7: Abuse of data and how to avoid it
Data may be used by:
Health Insurance Company (pre-existing conditions)
Landlord (how many people live here? / party?)
Criminals (schedule burglary / pre-identify what items to steal)
Privacy Violation (even visible which movie is watched)
How can this be avoided?
Reading rate (current reading rate of 15 min reveals most appliance signatures)
Encrypted reading
Renewable generation:
  Meter reading = Load – Local Renewable generation
  Like adding noise to meter readings
Load Signature Moderation :
  Meter reading = Load – Discharge + Charge
  by local storage
Notes: Mona

## Slide 8: Current situation in Finland
2009: new law  80% of customers of each DSO must have a Smart Meter until 2013
98% of all customers in Finland are supplied with a smart meter (status: 2016)
  Perfect situation for research
  52 million € Smart Grids & Energy Markets –program (SGEM): cooperation of universities, research institutes, DSOs, and industry partners
Situation around EU
  Positive CBA: large scale roll-out (80%).
  Inconclusive CBA: some do, some do not.
  Negative CBA: no roll out.
Notes: Francesco: The EU Commission requires each member state to equip 80% of all network users with smart meters till 2020. That is, if a Cost-Benefit-Analysis (CBA) shows that smart metering can actually save the network users some money. All member states have conducted these CBAs and the results can be clustered into three categories.
By 2020, it is expected that almost 72% of European consumers will have a smart meter for electricity while 40% will have one for gas.

## Slide 9: Conclusions
Smart Meters for research and development of LV network
Advanced security is necessary to protect the consumers data
Ongoing implementation in Europe: 72% of consumers will have a smart meter by 2020
Notes: Mona

## Slide 10: Source material
https://www.investinfinland.fi/smart-grid
https://tutcris.tut.fi/portal/files/16319602/CIRED2016_0120_final.pdf
https://spectrum.ieee.org/energy/the-smarter-grid/privacy-on-the-smart-grid
https://eur-lex.europa.eu/legal-content/EN/TXT/?qid=1403084595595&uri=COM:2014:356:FIN
https://ses.jrc.ec.europa.eu/smart-metering-deployment-european-union
https://www.bundesnetzagentur.de/SharedDocs/Downloads/DE/Sachgebiete/Energie/Unternehmen_Institutionen/DatenaustauschUndMonitoring/Monitoring/Monitoring2017_Kapitel/E_MessZaehlwesen2017.pdf?__blob=publicationFile&v=1
Prof. Dr.-Ing. Marco Pruckner: Smart Grid, Lecture Slides (2018), Friedrich-Alexander University, Germany.
Aoife Brophy Haney, Tooraj Jamasb and Michael Pollitt: Smart Metering and Electricity Demand:
Technology, Economics and International Experience, CWPE 0905 & EPRG 0903, Cambridge, 2009.
https://www.bsi.bund.de/DE/Themen/DigitaleGesellschaft/SmartMeter/SmartMeterGateway/smartmetergateway_node.html