## Slide 1: ELEC-E8423 - Smart Grid Electric vehicles and their charging systems
Teemu Lehtonen
Jonne Ticklen
26.03.2019

## Slide 2: Introduction
Finland’s EV’s
Today, 2400 full electric vehicles and 13 000 plug-in hybrids in Finland​
​Target is to have 250 000 EV’s by the year 2030
Finland’s charging stations ​
Today, 638 public charging stations with 1811 charging points.
1 500 000 car heating poles which could be utilized for EV charging​
Commercial vehicles have their own charging network
EU’s alternative fuels infrastructure directive expects the amount of charging stations to be 1 per 10 vehicles.
Public charging station network is intended to grow on a market-based basis by energy companies and other commercial actors
​​
EV’s and their charging stations are supported with subsidies​
​
Latauskartta.fi

## Slide 3: Electric vehicles
Price level is descending along with batteries
Nissan leaf costs upward 37 000 €
Tesla model 3 long range-versio 57 000 €
Range of EV’s
Normally 250-350 km (Nissan Leaf)
Up to 530 kilometers (Tesla model 3)
Commercial vehicles are increasing in Finland
  22 electric busses, most in HSL region
  210 electric vans
  1 electric truck

## Slide 4: Charging modes
Charging control abilities:​
Modes 1 and 2 uses normal household sockets and plugs for grid connection -> no data pins​
Modes 3 and 4 uses EV dedicated multi-pin sockets for communication between car and grid​
​
Modes​ | Usage​ | Power (max)​ | Voltage​ | Charger ​
Mode 1​ | Light vehicles​ | 2 (3,5) kW​ | AC, 1-ph​ | Uncontrolled, normal cable​
Mode 2​ | Slow charging ​ | 7 (11) kW​ | AC, 1 or 3-ph​ | Cable with control unit ​
Mode 3 ​ | Basic charging​ | 22 (43) kW​ | AC, 3-ph​ | Dedicated EV charger socket ​
Mode 4​ | Quick charging​ | 50 (350) kW​ | DC​ | Special power charger​

## Slide 5: Charging systems and methods
Plug-in charging
Europe has its own standardized plugs for EV’s
  Slow and basic charging (AC) -> Type 2
  Quick charging (DC) -> CSS Combo
Other types are used for example Japan and US
Pantograph charging
Mainly used in commercial vehicles
HSL busses use this charging method
Induction charging
Used both commercial and private vehicles
Max power 200 kW

## Slide 6: Charging of the EV
Charging differs by location
At home
  Number of charging poles/cables ≈ number of EVs
At workplace
  Number of… EVs ≈ Parking slots > Charging cables > Charging poles
BMS controls SoC of EV’s battery
BMS = Battery management system
SoC = State of Charge
Components in charcing
EV Battery/PEU
  Storage and power electronics indide the EV
EVSE
  EV Supply Equipment
Breakers, Transformers (LV to LV)
Grid-Integrated Vehicle total precentage losses (%) |  |  |  | 
Component | Charging |  | Discharging | 
 | 10 (A) | 40 (A) | 10 (A) | 40 (A)
EV Battery | 0.6 | 1.7 | 0.6 | 1.9
EV PEU | 6.3 | 5.8 | 16.7 | 19.2
EVSE | 0.1 | 0.3 | 1.4 | 1.4
Breakers | 0.0 | 1.3 | 2.8 | 0.6
Transformer | 10.2 | 3.3 | 14.6 | 6.7
Total | 17.2 | 12.4 | 36.1 | 29.8

## Slide 7: Smart charging
OSCP
Distribution company’s grid
24h forecast
OCPP
Charging Point
Open Charge Point Protocol
VSL
Electric Vehicle
Open Smart Charcing Protocol
Vehicle Smart Link
The industry is still evolving, and no protocol has been established as the de-facto standard.

## Slide 8: Conclusions
Directives, standardization and subsidies are needed to propagate EV’s and their charging network
The main advantage of Grid-Integrated Vehicles’ V2G operation is demand peak-shaving
Smart charging is necessary to ensure grid stability in the future

## Slide 9: Source material used
https://www.talouselama.fi/uutiset/joka-viides-uusi-auto-on-pian-sahkoauto-uskokaa-nyt-vaan/bb7cbc95-6a39-33d0-8f17-215d12398434
http://julkaisut.valtioneuvosto.fi/bitstream/handle/10024/161364/3-2019-GASELLI_loppuraportti_.pdf
https://www.volvotrucks.fi/fi-fi/news/press-releases/2019/feb/lehdistotiedote-19022019.html
https://www.liikennefakta.fi/ymparisto
https://www.nissan.fi/ajoneuvot/henkiloautot/leaf.html%3F&cid=psmQy2MdEBK_dc|U
https://www.autotalli.com/artikkeli/Tesla-Model-3-Sai-Suomen-Hinnat---544-Km-Long-Range--Versio-Alkaen-60-500-Euroa?gclid=CjwKCAjw1dzkBRBWEiwAROVDLPRDiOvsuxyJcZFUji_W4H9bdU2HEsA5ksi0B7SEVr3PuzITT5hubBoCQvEQAvD_BwE
https://www.pluglesspower.com/learn/wireless-charging-evs-guide-tesla/
https://www.sciencedirect.com/science/article/pii/S0360544217303730?via%3Dihub
https://www.researchgate.net/publication/266862790_THE_EFFECT_OF_PHEV_AND_HEV_DUTY_CYCLES_ON_BATTERY_AND_BATTERY_PACK_PERFORMANCE/download
https://cleantechnica.com/2018/03/10/electric-car-myth-buster-efficiency/