## Slide 1: ELEC-E8423 - Smart Grid Future Street Lights
Sandesh Badgami
Muhammad Saad Akram
23.04.2019

## Slide 2: Scope
Traditional street lights have energy wastage issue due to their inefficient use. This opens the opportunity to modify street lights to solve the energy wastage crisis.
The scope of this presentation is to outline the possible modifications in street lights for future use.
Notes: Energy bills is reduced
Reducing energy wastage

## Slide 3: Introduction
Adapting the concept of smart city, will require improving street lighting technologies.
Traditional street lights:-
100 % power
Not efficient – energy saving
Costly – operational cost
Environmental issue
Solutions:-
Possibility of incorporating solar and wind energy powered street light systems.
Hybrid Power systems based street lights
LED-based intelligent street lights
Notes: Environmental Issue – VTT report, estemates that the worlds 220 million street lights use 159 TWh of energy annually, generating 81 Mtonnes of CO2 emmisions.
LED based intelliginet systems, a city of one million inhabitans could generate energy saving worth of 2-3 million euros annually.

## Slide 4: Hybrid Power System Supply
Figure: Block diagram of a hybrid power system supply for a prototype street light (Source: Reference 1)
Notes: Charge controller helps to protect the battery from over charging.

## Slide 5: Hybrid continued
Use solar PV to charge battery
Control strategy - based on the battery condition
Above 70% - All LED lights connected to the battery
Below 50% - All LED lights connected to the grid
Table: Control strategy (Source: Reference 1)
Benefit:-
Operational cost
Cost effective option (Nano grid)

## Slide 6: Intelligent Street Lights Systems
Emergence of Internet of Things (IOT):
Incorporate combination of electronic devices, sensors and intelligent software applications to build effective data exchange network
Benefits:-
Possible to reduce energy cost by 50 – 70 %
Automation
Reduce man power
Minimises energy wastage
Notes: IOT is a network of multiple devices all connected together. Uses the concept of machine to machine communication and reduced the human to human and human to machine commhnications.
Advantage:
Automatic, reduce maintenance cost, energy saving and low man power.
Ultrasensor : Detect pedestrian or cars and manage the intensity of the lights. 100% brightness can be reduced to 60% when inactive road.

## Slide 7: VTT AthLEDics Project
Notes: Largest cities London, hong knog Sydney, found that LEDs with smart controls could result in a saving of 85%.
Glasgow, project cost €4 M.

## Slide 8: Constraints/ challenges
Proximity sensors have limited range
Difficult to regulate the intensity of light considering traffic on the street at specified times
Cost
Possibility of errors – E.g. LDR may function when shadows fall on it
Notes: 4 M Glasgow to retrofit 3,500 columns in the city centre

## Slide 9: Case study
City of Harrisburg – LED streetlight conversion project
        $520 k annual savings
        $60 k annual maintenance savings
        60-70 % reduction in utility bills
Peterborough in UK – replacement of 400 low-pressure sodium light
        Halving its energy cost
        Reducing CO2 emissions by nearly 27 tons per year
Boston in USA – converted 40% of its streetlights in 2012
        $2.8 M annual savings

## Slide 10: Conclusions
Reduction in cost (Implementation, Sensors, Maintenance)
Development in sensors
Minimise powerplants electricity wastage in lighting the streets
Notes: Trade off between safety and saving.

## Slide 11: Source material used
K.P. Prajna Cauvery, P. Dharanidhar, K.C. Sindhu Thampatty, “Design and implementation of a Prototypic Hybrid Power System Supply for Street Lighting”, IEEE region 10 humanitarian Technology Conference, 2017
R. Kodali, S. Yerroju, “Energy Efficient Smart Street Lighting”, IEEE, Internation conference on Applied and Theoretical Computing and Communication Technology, 2017
M. Airaksinen, M Kokkala, “Smart City – Resaearch Highlights”, VTT Research highlights 12, VTT, 2015
H. Grffiths, “The Future of Street Lights – The potential of new service development”, Future Cities Catapult, iotuk, 2017